3GPP TSG-SA WG6 Meeting #26	S6-181535

Vilnius, Lithuania, 15th – 19th October 2018	(revision of S6-181310, S6-181450)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.282 | CR | 0118 | rev | 2 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Corrections to Table A.2-1, Table A.4-2 and Table A.5-2 |
| --- | --- |
| Source to WG: | AT&T |
| Source to TSG: | S6 |
| Work item code: | eMCDATA2 |  | Date: | 2018-10-02 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Configuration parameter “>Maximum data size for auto-receive” is incorrectly referencing requirement R-6.2.2.1-003 which is for data transmission control. [R-6.2.2.1-003] The MCData Service shall provide a mechanism for the MCData Administrator to configure the maximum data size for automatic data transmission. |
| Summary of change: | 1.Correct the refence to the requirement for auto-receive parameter and move it up one level to cover all relevant configuration parameters 2. correct the typo in Table A.2-1 |
| Consequences if not approved: | Might confuse stage 3 development. |
| Clauses affected: | A.2, A.4 and A.5 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

# A.2	MCData UE configuration data

The general aspects of UE configuration are specified in 3GPP TS 23.280 [5]. Data in tables A.2-1 and A.2-2 have to be known by the MCData UE after MCData authorization.

Data in table A.2-1 can be configured offline using the CSC-11 reference point. Table A.2-1 contains the UE configuration required to support the use of off-network MCData service.

Table A.2-1: UE configuration data (on and off network)

| Reference | Parameter description |
| --- | --- |
|  | Short data service |
| [R-5.4.2-002] of 3GPP TS 22.280 [2] | > Maximum number of simultaneous SDS transactions (Nc4) |
| [R-5.4.2-004] of 3GPP TS 22.280 [2] | > Requested presentation priority of SDS messages received (see NOTE) |
|  | File distribution |
| [R-5.4.2-002] of 3GPP TS 22.280 [2] | > Maximum number of simultaneous file distribution transactions (Nc4) |
|  | Transmission control |
| [R-5.4.2-002] of 3GPP TS 22.280 [2] | > Maximum number of simultaneous data transmissions (Nc4) |
| [R-5.4.2-003] of 3GPP TS 22.280 [2] | > Maximum number of data transmissions (Nc5) in a group |
|  | Reception control |
| [R-5.4.2-002] of 3GPP TS 22.280 [2] | > Maximum number of simultaneous data receptions (Nc4) |
| [R-5.4.2-003] of 3GPP TS 22.280 [2] | > Maximum number of data receptions (Nc5) in a group |
| NOTE: Priority of SDS messages includes enhanced status updates, since enhanced status updates utilise the SDS mechanism. |

Table A.2-2: UE configuration data (on network)

| Reference | Parameter description |
| --- | --- |
| Subclause 5.2.3 of 3GPP TS 23.280 [6] | Relay service (Y/N) |
| Subclause 5.2.3 of 3GPP TS 23.280 [6] | List of allowed relayed MCData groups and their relay service code (as specified in 3GPP TS 23.303 [7]) (optional) (see NOTE) |
|  | > MCData group ID |
|  | > Relay service code (as specified in 3GPP TS 23.303 [7]) |
| Subclause 5.7 of 3GPP TS 23.280 [6] | Indication of whether the UE shall use IPv4 or IPv6 for on-network MCData |
|  | MCData server |
|  | > Server URI |
| NOTE: When the value of the parameter Relay service is N, this parameter and its child parameters are not needed. |

* * * Second Change * * * *

# A.4	MCData related Group configuration data

The general aspects of group configuration are specified in 3GPP TS 23.280 [5].

Parameters specified in table A.4-1 are child parameters of the "MCData configuration" parameter specified in table A.4-1 in 3GPP TS 23.280 [5]. Parameters specified in table A.4-2 are child parameters of the "MCData configuration" parameter specified in table A.4-2 in 3GPP TS 23.280 [5]. Parameters specified in table A.4-3 are child parameters of the "MCData configuration" parameter specified in table A.4-3 in 3GPP TS 23.280 [5].

Editor's note: Further contents of this configuration data are FFS.

Table A.4-1: Group configuration data (on and off network)

| Reference | Parameter description | MCData UE | MCData Server | Group management server |
| --- | --- | --- | --- | --- |
| [R-5.12-001] of 3GPP TS 22.280 [2] | >> Media confidentiality and integrity protection (see NOTE) | Y | Y | Y |
| [R-5.12-001] of 3GPP TS 22.280 [2] | >> Transmission control confidentiality and integrity protection (see NOTE) | Y | Y | Y |
| [R-5.12-001] of 3GPP TS 22.280 [2] | >> Group media protection security material (see NOTE) | Y | N | Y |
| Subclause 5 | >> MCData sub-services and features enabled for the group |  |  |  |
|  | >>> Short data service enabled | Y | Y | Y |
|  | >>> File distribution enabled | Y | Y | Y |
|  | >>> Conversation management enabled | Y | Y | Y |
|  | >>> Transmission control enabled | Y | Y | Y |
|  | >>> Reception control enabled | Y | Y | Y |
|  | >>> Enhanced status enabled | Y | Y | Y |
|  | >> Transmission and reception control |  |  |  |
| [R-6.2.2.1-001] of 3GPP TS 22.282 [3] | >>> Whether MCData user is permitted to transmit data in the group | Y | Y | Y |
| [R-6.2.3-006] of 3GPP TS 22.282 [3] | >>> Maximum amount of data that the MCData user can transmit in a single request during group communication | Y | Y | Y |
| [R-6.2.3-006] of 3GPP TS 22.282 [3] | >>> Maximum amount of time that the MCData user can transmit in a single request during group communication | Y | Y | Y |
|  | >> Enhanced status |  |  |  |
| [R-6.1.3.2-002] of 3GPP TS 22.282 [3] | >>> List of operational status values | Y | N | Y |
| NOTE: Security mechanisms are specified in 3GPP TS 33.180 [13]. |

Table A.4-2: Group configuration data (on network)

| Reference | Parameter description | MCData UE | MCData Server | Group management server |
| --- | --- | --- | --- | --- |
| [R-6.4.5-001], [R-6.4.5-003] of 3GPP TS 22.280 [2] | >> Authorisation of a user to request a list of affiliated members of a group | Y | Y | Y |
| [R-5.1.7-002], [R-6.2.2-001], [R-6.6.2.2-006], [R-6.8.7.2-003] of 3GPP TS 22.280 [2] | >> Priority of the group | N | Y | Y |
| Subclause 6.2.2 of 3GPP TS 22.282 [3] | >> Transmission and reception control |  |  |  |
|  | >>> Maximum data size for SDS | Y | Y | Y |
|  | >>> Maximum data size for FD | Y | Y | Y |
|  | >>> Maximum data size for auto-receive | N | Y | Y |
| 3GPP TS 23.283 [18] | >> Indication whether use of LMR E2EE is permitted on the MCData group | Y | N | Y |
| 3GPP TS 23.283 [18] | >> LMR specific identity for MCData group (see NOTE) | Y | N | Y |
| 3GPP TS 23.283 [18] | >> Group to key binding (see NOTE) | Y | N | Y |
| NOTE: This is an LMR specific parameter with no meaning within MC services. |

Table A.4-3: Group configuration data (off network)

| Reference | Parameter description | MCData UE | MCData Server | Group management server |
| --- | --- | --- | --- | --- |
| Subclause 10.10 of 3GPP TS 23.280 [5] | >> Default ProSe Per-Packet priority (as specified in 3GPP TS 23.303 [7]) values |  |  |  |
|  | >>> MCData group call signalling | Y | N | Y |
|  | >>> MCData group call media | Y | N | Y |

* * * Third Change * * * *

# A.5	MCData service configuration data

The general aspects of MC service configuration are specified in 3GPP TS 23.280 [5]. The MCData service configuration data is stored in the MCData server.

Tables A.5-1 and A.5-2 describe the configuration data required to support the use of on-network MCData service. Tables A.5-1 and A.5-3 describe the configuration data required to support the use of off-network MCData service. Data in tables A.5-1 and A.5-3 can be configured offline using the CSC-11 reference point.

Table A.5-1: MCData service configuration data (on and off network)

| Reference | Parameter description | MCData UE | MCData Server | Configuration management server |
| --- | --- | --- | --- | --- |
|  | Transmission and reception control |  |  |  |
| [R-6.2.2.1-002d], [R-6.2.2.4-003] of 3GPP TS 22.282 [3] | > Time limit for the temporarily stored data waiting to be delivered to a receiving user | Y | Y | Y |
| [R-6.2.2.3-001] of 3GPP TS 22.282 [3] | > Timer for periodic announcement with the list of available recently invited data group communications | Y | Y | Y |

Table A.5-2: MCData service configuration data (on network)

| Reference | Parameter description | MCData UE | MCData Server | Configuration management server |
| --- | --- | --- | --- | --- |
| Subclause 6.2.2 of 3GPP TS 22.282 [3] | Transmission and reception control |  |  |  |
|  | > Maximum data size for SDS | Y | Y | Y |
|  | > Maximum payload data size for SDS over signalling control plane (NOTE) | Y | Y | Y |
|  | > Maximum data size for FD | Y | Y | Y |
|  | > Maximum data size for auto-receive | N | Y | Y |
| NOTE: The maximum payload data size for SDS over signalling control plane shall be less than or equal to the maximum data size for SDS. |

Table A.5-3: MCData service configuration data (off network)

| Reference | Parameter description | MCData UE | MCData Server | Configuration management server |
| --- | --- | --- | --- | --- |
| Subclause 10.10 of 3GPP TS 23.280 [5] | Default ProSe Per-Packet priority (as specified in 3GPP TS 23.303 [7]) values |  |  |  |
|  | > MCData one-to-one call signalling | Y | N | Y |
|  | > MCData one-to-one call media | Y | N | Y |