3GPP TSG-SA WG6 Meeting #28	S6-190245

Kochi, India, 21st – 25th January 2019	(revision of S6-190150)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.379 | CR | 0171 | rev | 2 | Current version: | 16.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Corrections to MCPTT chat group call late entry procedures |
| --- | --- |
| Source to WG: | Airbus DS SLC |
| Source to TSG: | S6 |
| Work item code: | enh2MCPTT |  | Date: | 2019-01-24 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Subclause 10.6.2.3.1.2.4 (Late entry for chat group call) was revised by S6-181873 (CR161r4). New subclauses 10.6.2.3.1.2.4a and 10.6.2.3.1.2.4b were introduced. The subclause titles and numbering is not logical and needs some corrections. Furthermore, an ambiguous sentence “If MCPTT client 1 is affiliated but not joined to the group…..” was added to step 2 of subclause 10.6.2.3.1.2.4b. Looking at the actions before this step, it is very unclear how this ‘state’ could be reached and how the server would know that client has moved to “affiliated but not joined”state while being out-of-radio-coverage. Moreover, the whole concept of “affiliated but not joined” has not been described anywhere in stage 2 standards. In stage3 standards it is only mentioned in some emergency/imminent peril cases. So the proposal is to remove this sentence now. If necessary, it can be re-introduced with proper definitions later. |
| Summary of change: | The heading text of subclause 10.6.2.3.1.2.4 is amended. Subclause 10.6.2.3.1.2.4a is marked as void and text moved under 10.6.2.3.1.2.4. Subclause 10.6.2.3.1.2.4b is marked as void and text moved under new subclause 10.6.2.3.1.2.5. Sentence starting “If MCPTT client 1 is affiliated but not joined to the group…..” is replaced with a note about possible rejoin signalling from the client. |
| Consequences if not approved: | Confusing subclause numbering and subclause header texts. Ambiguous new ‘state’ introduced in the middle of a late entry procedure with no proper description. |
| Clauses affected: | 10.6.2.3.1.2.4, 10.6.2.3.1.2.4a, 10.6.2.3.1.2.4b, 10.6.2.3.1.2.5 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First change * * * *

10.6.2.3.1.2.4	Late entry chat group call, newly joined group member

Procedures in figure 10.6.2.3.1.2.4-1 are those for a group member entering an ongoing MCPTT group call, i.e. performing a late entry.

Pre-conditions:

1.	MCPTT user 2 and MCPTT user 3 have previously joined to the group. MCPTT client 1, client 2, and client 3 are registered and all users (MCPTT user 1, user 2, and user 3) have been authenticated and authorized to use the MCPTT service.

2.	MCPTT client 1, MCPTT client 2 and MCPTT client 3 may have activated functional alias(es) configured to be used during the group call communication. MCPTT users using MCPTT client 2 and MCPTT client 3 are in an ongoing group call. MCPTT client 1 has not yet joined the group call. Optionally, the MCPTT users may use activated functional aliases.

3.	MCPTT user 1 indicates to join the group communication for the group.

Figure 10.6.2.3.1.2.4-1: Late entry of a newly joined group member

1.	MCPTT client 1 sends a group join request with the MCPTT group ID of the desired group. It contains the MCPTT user's MCPTT ID, the MCPTT client media parameters and optionally a functional alias. If there is a request to transmit, then the group joint request contains an indication of an implicit floor request.

2.	The MCPTT server receives the group join request. MCPTT server generates an implicit affiliation (if the MCPTT user is not already affiliated to the group) and verifies that MCPTT user 1 is authorized to affiliate to the group.

If present, the MCPTT server checks whether the provided functional alias is allowed to be used and has been activated for the user.

3.	The MCPTT server replies with a group join response indicating the acceptance of the group join request.

4.	Media plane between MCPTT client 1 and MCPTT server is established using media plane control signalling.

5.	MCPTT users at MCPTT client 2 and MCPTT client 3 may be notified about the MCPTT client 1 joining the group call. The functional aliases of MCPTT client 1 is displayed, if present.

6.	The MCPTT server sends a floor taken (for the current talker) to MCPTT client 1.

7.	Floor control will continue to be used by the floor participants associated with MCPTT client 1, MCPTT client 2 and MCPTT client 3.

10.6.2.3.1.2.4a	void

10.6.2.3.1.2.4b	void

10.6.2.3.1.2.5	Late entry chat group call, MCPTT client coming back from out of coverage

Procedures in figure 10.6.2.3.1.2.5-1 are those for an MCPTT client coming back from out of coverage during an ongoing MCPTT group call.

Pre-conditions:

- MCPTT client 1, MCPTT client 2 and MCPTT client 3 may have activated functional alias(es) configured to be used during the group call communication. MCPTT users using MCPTT client 1, MCPTT client 2 and MCPTT client 3 are in an ongoing group call when MCPTT client1 goes out of radio coverage.

- MCPTT client1 returns from out of coverage while the group call is still ongoing.

Figure 10.6.2.3.1.2.5-1: Late entry of a MCPTT client returning from out of coverage

1.	MCPTT client 1 or MCPTT server detects that MCPTT client 1 has returned from out of coverage.

NOTE 1:	How the MCPTT client or MCPTT server detects that the client has returned from out of coverage is out of scope of the present document.

2.	Media plane between MCPTT client 1 and MCPTT server is re-established using media plane control signalling.

NOTE 2:	Depending on how long MCPTT client 1 was out of coverage, this step can include signalling from MCPTT client 1 to rejoin the chat group.

3.	MCPTT server sends a floor taken (for the current talker) to MCPTT client 1.

4.	MCPTT users at MCPTT client 2 and MCPTT client 3 may be notified about the MCPTT client 1 returning to the group call. The functional aliases of MCPTT client 1 is displayed, if present.

5.	Floor control will continue to be used by the floor participants associated with MCPTT client 1, MCPTT client 2 and MCPTT client 3.

* * * End of changes * * * *