3GPP TSG-SA WG6 Meeting #28	S6-190246

Kochi, India, 21st – 25th January 2019	(revision of S6-190151)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.379 | CR | 0172 | rev | 2 | Current version: | 16.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Procedure for MCPTT user leaving a group call |
| --- | --- |
| Source to WG: | Airbus DS SLC |
| Source to TSG: | S6 |
| Work item code: | enh2MCPTT |  | Date: | 2019-01-24 |
| Category: | C |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Procedure for MCPTT user leaving a group call is missing from 23.379. Adding this new procedure also requires that information flows “Group call leave request” and “Group call leave response” need to be bidirectional (in the current TS version they are unidirectional). NOTE: This functionality is already specified in stage 3 TS24.379, subclauses 6.2.4.1 and 6.3.3.2.4. |
| Summary of change: | Information flows “10.6.2.2.22 Group call leave request” and “10.6.2.2.23 Group call leave response” are corrected to be bidirectional by adding new subclauses 10.6.2.2.22a and 10.6.2.2.23a. New subclause “10.6.2.3.3 MCPTT user leaving a group call”. The NOTE in subclause 10.6.2.3.1.1.3 can be removed after this new procedure is added. |
| Consequences if not approved: | Missing functionality in MCPTT stage 2 TS. Misalignment with MCPTT stage 3 TS. |
| Clauses affected: | 10.6.2.2.22a (new), 10.6.2.2.23a (new), 10.6.2.3.1.1.3, 10.6.2.3.3 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * 1st change * * * *

##### 10.6.2.2.22a	Group call leave request (MCPTT client – MCPTT server)

Table 10.6.2.2.22-1 describes the information flow group call leave request from the MCPTT client to the MCPTT server.

Table 10.6.2.2.22a-1 Group call leave request information elements

| Information Element | Status | Description |
| --- | --- | --- |
| MCPTT ID | M | The MCPTT ID of the MCPTT group member leaving the group call |
| Functional alias | O | The functional alias of the MCPTT group member |
| MCPTT group ID | M | The MCPTT group ID of the group on which the call is on-going |

* * * 2nd change * * * *

##### 10.6.2.2.23a	Group call leave response (MCPTT server – MCPTT client)

Table 10.6.2.2.23-1 describes the information flow group call leave response from the MCPTT server to the MCPTT client.

Table 10.6.2.2.23a-1 Group call leave response information elements

| Information Element | Status | Description |
| --- | --- | --- |
| MCPTT ID | M | The MCPTT ID of the MCPTT group member leaving the group call |
| Functional alias | O | The functional alias of the MCPTT group member |
| MCPTT group ID | M | The MCPTT group ID of the group on which the call is on-going |

* * * 3rd change * * * *

10.6.2.3.1.1.3	Release pre-arranged group call

The procedure focuses on the case where an MCPTT server initiates the termination of an ongoing MCPTT group call for all the participants of that group call, since at least one of the termination conditions are met e.g., due to hang time expiry, last participant leaving, second last participant leaving, initiator leaving, or minimum number of affiliated MCPTT group members are not present.

Procedures in figure 10.6.2.3.1.1.3-1 are the signalling control plane procedures for the MCPTT server initiating termination of an ongoing MCPTT group call.

Figure 10.6.2.3.1.1.3-1: Release pre-arranged group call

1.	It is assumed that MCPTT users on MCPTT client 1, client 2 and client 3 are already part of the ongoing group call (e.g., as a result of pre-arranged group call setup).

2.	MCPTT server would like to release the MCPTT group call which is ongoing e.g., due to hang time expiry, last participant leaving, second last participant leaving, initiator leaving, or minimum number of affiliated MCPTT group members are not present.

3.	MCPTT server identifies the participants of the ongoing group call and generates group call release request to release ongoing session.

4.	MCPTT server sends a group call release request via SIP core towards each participant of the ongoing group call.

5.	MCPTT users are notified about the release of the group call.

6.	MCPTT client(s) receiving group call release request, acknowledge towards the MCPTT server by sending a group call release response.

7. MCPTT client 1, client 2 and client 3 have successfully released the floor control and media plane resources associated with the group call that is terminated.

* * * 4th change * * * *

##### 10.6.2.3.3	MCPTT user leaving a group call

Procedures in figure 10.6.2.3.3-1 are the signalling control plane procedures for the MCPTT user leaving an ongoing MCPTT group call.

Pre-conditions:

1.	MCPTT group is previously defined on the group management server with MCPTT users affiliated to that group. All members of the group belong to the same MC system.

2.	MCPTT users on MCPTT client 1 to MCPTT client n are on an ongoing call.

3.	MCPTT user 1 indicates to leave the group call.

Figure 10.6.2.3.3-1: MCPTT user leaving a group call

- MCPTT client 1 sends a group call leave request to the MCPTT server.

- MCPTT server sends a group call leave response to MCPTT client 1.

- Release of floor control and media plane resources associated with the group call for MCPTT client 1.

NOTE 1:	MCPTT server checks if group call termination conditions are met, e.g. hang time expiry, last participant leaving, second last participant leaving, initiator leaving, minimum number of affiliated MCPTT group members are not present. If at least one of the group call termination conditions is met, the MCPTT server releases the group call for all participants (see subclauses 10.6.2.3.1.1.3 Release pre-arranged group call and 10.6.2.3.1.2.3 Release chat group call).

- MCPTT users at MCPTT client 2 to MCPTT client n may be notified that the MCPTT user of client 1 has left the group call. The functional alias of MCPTT client 1 is displayed, if present.

NOTE 2:	The MCPTT server does not perform late entry for MCPTT users that have left the group call.

* * * End of changes * * * *