3GPP TSG-SA WG6 Meeting #30	S6-190711

Newport Beach, CA, USA, 8th – 12th April 2019	(revision of S6-190591)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.281 | CR | 0121 | rev | 1 | Current version: | 16.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | User requested priority in 23.281 |
| --- | --- |
| Source to WG: | TD Tech, Chengdu TD Tech |
| Source to TSG: | S6 |
| Work item code: | MONASTERY2 |  | Date: | 2019-04-10 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | According to Solution 26 in TR 23.796, an optional parameter indicating the application layer priority for the specific call or communication is added to the call requests from the MC service client to the MC service server. |
| Summary of change: | Add information element of requested priority to relevant requests from the client to the server. |
| Consequences if not approved: | Requirement regarding user requested application layer priority is not met. |
| Clauses affected: | 7.1.2.2.1, 7.1.2.2.8, 7.1.2.2.10, 7.2.2.2.1, 7.3.2.2.1, 7.4.2.2.1, 7.4.2.2.4 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

##### 7.1.2.2.1	Group call request (MCVideo client – MCVideo server)

Table 7.1.2.2.1-1 describes the information flow group call request from the MCVideo client to the MCVideo server.

Table 7.1.2.2.1-1: Group call request (MCVideo client – MCVideo server)

| Information Element | Status | Description |
| --- | --- | --- |
| MCVideo ID | M | The MCVideo ID of the calling party |
| MCVideo group ID | M | The MCVideo group ID of the group on which the call is requested |
| SDP offer | M | Media parameters of MCVideo clients |
| Implicit transmit media request | O | When originating client requests the permission to transmit media, this element shall be included |
| Broadcast indicator | O | Indicates that the group call request is for a broadcast group call |
| Requested priority | O | Application priority level requested for this call |

* * * Next Change * * * *

##### 7.1.2.2.8	Group call rejoin request (MCVideo client – MCVideo server)

Table 7.1.2.2.8-1 describes the information flow group call rejoin request from the MCVideo client to the MCVideo server.

Table 7.1.2.2.8-1: Group call rejoin request (MCVideo client – MCVideo server))

| Information Element | Status | Description |
| --- | --- | --- |
| MCVideo ID | M | The MCVideo ID of the re-joining MCVideo group member |
| MCVideo group ID | M | The MCVideo group ID of the group on which the call is on-going |
| SDP offer | M | Media parameters of MCVideo client |
| Requested priority | O | Application priority level requested for this call |

* * * Next Change * * * *

##### 7.1.2.2.10	Group call join request (MCVideo client – MCVideo server)

Table 7.1.2.2.10-1 describes the information flow group call join request from the MCVideo client to the MCVideo server.

Table 7.1.2.2.10-1: Group call join request (MCVideo client – MCVideo server)

| Information Element | Status | Description |
| --- | --- | --- |
| MCVideo ID | M | The MCVideo ID of the MCVideo group member joining the group communications for the group |
| MCVideo group ID | M | The MCVideo group ID of the group to which the group communication is requested |
| SDP offer | M | Media parameters of MCVideo client |
| Requested priority | O | Application priority level requested for this call |

* * * Next Change * * * *

##### 7.2.2.2.1	MCVideo private call request (MCVideo client – MCVideo server)

Table 7.2.2.2.1-1 describes the information flow MCVideo private call request from the MCVideo client to the MCVideo server.

Table 7.2.2.2.1-1: MCVideo private call request (MCVideo client – MCVideo server)

| Information Element | Status | Description |
| --- | --- | --- |
| MCVideo ID | M | The MCVideo ID of the calling party |
| MCVideo ID | M | The MCVideo ID of the called party |
| Transmit media request indication | M | This element indicates whether transmission control will be used for the private call. |
| SDP offer | M | Media parameters of MCVideo client. |
| Requested commencement mode | O | An indication that is included if the user is requesting a particular commencement mode |
| Implicit transmit media request | O | An indication that the user is also requesting the permission to transmit video |
| Push indication | O | Indicates that the private call request is for a one-to-one push call |
| Pull indication | O | Indicates that the private call request is for a one-to-one pull call |
| Requested priority | O | Application priority level requested for this call |

* * * Next Change * * * *

##### 7.3.2.2.1	MCVideo pull from server request

Table 7.3.2.2.1-1 describes the information flow MCVideo pull from server request from the MCVideo client to the MCVideo server.

Table 7.3.2.2.1-1: MCVideo pull from server request

| Information Element | Status | Description |
| --- | --- | --- |
| MCVideo ID | M | The MCVideo ID of the calling party |
| File URL | M | URL of the video file to be streamed |
| SDP offer | M | Media parameters of MCVideo client |
| Requested priority | O | Application priority level requested for this call |

* * * Next Change * * * *

##### 7.4.2.2.1	Remote video push request

Table 7.4.2.2.1-1 describes the information flow remote video push request from the MCVideo client to the MCVideo server and from the MCVideo server to the MCVideo client.

Table 7.4.2.2.1-1: Remote video push request

| Information Element | Status | Description |
| --- | --- | --- |
| MCVideo ID | M | The MCVideo ID of the call originating party |
| MCVideo ID | M | The MCVideo ID of the source party who should transmit media |
| MCVideo ID | O (see NOTE) | The MCVideo ID of the destination party who should receive media |
| MCVideo group ID | O (see NOTE) | The MCVideo group ID of the destination group whose affiliated group members should receive media |
| SDP offer | O | Media parameters of MCVideo client. |
| Requested commencement mode | O | An indication that is included if the user is requesting a particular commencement mode |
| Requested priority | O | Application priority level requested for this call |
| NOTE: MCVideo ID information element is present if remote video push to destination user is requested. MCVideo group ID information element is present if remote video push to group is requested. |

* * * Next Change * * * *

##### 7.4.2.2.4	MCVideo push to server request

Table 7.4.2.2.4-1 describes the information flow MCVideo push to server request from the MCVideo client to the MCVideo server.

Table 7.4.2.2.4-1: MCVideo push to server request

| Information Element | Status | Description |
| --- | --- | --- |
| MCVideo ID | M | The MCVideo ID of the calling party |
| Time limit | O | Requested duration of the stream to be recorded |
| SDP offer | M | Media parameters of MCVideo client |
| Requested priority | O | Application priority level requested for this call |