3GPP TSG-SA WG6 Meeting #30	S6-190865

Newport Beach, CA, USA, 8th – 12th April 2019	(revision of S6-190823)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.281 | CR | 0125 | rev | 3 | Current version: | 16.1.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | x | Radio Access Network |  | Core Network | x |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Add functional alias to MCVideo for video pull and push operations |
| --- | --- |
| Source to WG: | Kapsch CarrierCom |
| Source to TSG: | S6 |
| Work item code: | MONASTERY2 |  | Date: | 2019-04-11 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Currently MCVideo specification does not contain functional alias, but this is required for rail applications. |
| Summary of change: | Add functional alias for video pull and push, mainly messages and procedure descriptions |
| Consequences if not approved: | Important functionaliy for rail applications is not available |
| Clauses affected: | 7.3.2.3.2, 7.4.2.2.1, 7.4.2.3.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

##### 7.3.2.3.2	One-to-one video pull – call setup

The procedure describes the case where an MCVideo user is initiating an MCVideo private call to pull video from called MCVideo user in an automatic or manual commencement mode. Only the called party is allowed to transmit video.

Procedures in figure 7.3.2.3.2-1 are the basic signalling control plane procedures for the MCVideo client initiating establishment of MCVideo private call with the chosen MCVideo user for video pull.

Pre-conditions:

1.	Optionally, MCVideo client 1 may have a functional alias activated to be used.

2.	The MCVideo server may have subscribed to the MCVideo functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 7.3.2.3.2-1: One-to-one video pull

1.	MCVideo user on MCVideo client 1 initiates video pull from MCVideo client 2, by sending a private call request to the MCVideo server using a service identifier as defined in 3GPP TS 23.228 [5] for MCVideo, for establishing a private call with the chosen MCVideo user for video pull. The MCVideo private call request contains MCVideo ID of invited user, an SDP offer containing one or more media types and the video pull indication to indicate that invited user is requested to transmit video to the requester. The MCVideo user at MCVideo client 1 may include a functional alias used within the MCVideo private call request.

2.	MCVideo server checks whether the MCVideo user at MCVideo client 1 is authorized to initiate the private call for video pull, and that MCVideo user at MCVideo client 2 is authorized to receive the private call for video pull. MCVideo server verifies whether the provided functional alias, if present, can be used and has been activated for the user.

3.	MCVideo server may provide a progress indication to MCVideo client 1 to indicate progress in the call setup process.

NOTE 1:	Step 3 can occur at any time following step 4, and prior to step 6.

4.	If authorized, MCVideo server includes information that it communicates using MCVideo service, offers the same media types or a subset of the media types contained in the initial received request, includes the requested automatic commencement mode indication based on a requested commencement mode by the calling user or based upon the setting of the called MCVideo client and sends the corresponding MCVideo private call request towards the MCVideo client 2, including the MCVideo ID, and, if available the functional alias of the calling MCVideo user 1. If the called MCVideo user has registered to the MCVideo service with multiple MCVideo UEs and has designated the MCVideo UE for receiving the private calls, then the incoming MCVideo private call request is delivered only to the designated MCVideo UE.

5.	The MCVideo client 2 notifies the user about the incoming private call for video pull. If a functional alias of the calling user is included it is displayed.

6.	The receiving MCVideo client 2 accepts the private call for video pull, and sends an MCVideo private call response to the MCVideo server with an implicit transmit media request.

7.	Upon receiving the MCVideo private call response from MCVideo client 2 accepting the private call request for video pull, the MCVideo server informs the MCVideo client 1 about successful call establishment via a private call response message.

8.	MCVideo client 1 and MCVideo client 2 have successfully established media plane and transmission control for media communication.

NOTE 2:	When the video transmission is completed, the private call is released.

* * * Next Change * * * *

##### 7.4.2.2.1	Remote video push request

Table 7.4.2.2.1-1 describes the information flow remote video push request from the MCVideo client to the MCVideo server and from the MCVideo server to the MCVideo client.

Table 7.4.2.2.1-1: Remote video push request

| Information Element | Status | Description |
| --- | --- | --- |
| MCVideo ID | M | The MCVideo ID of the call originating party |
| Functional alias | O | The functional alias of the originating party |
| MCVideo ID | M | The MCVideo ID of the source party who should transmit media |
| MCVideo ID | O (see NOTE) | The MCVideo ID of the destination party who should receive media |
| MCVideo group ID | O (see NOTE) | The MCVideo group ID of the destination group whose affiliated group members should receive media |
| SDP offer | O | Media parameters of MCVideo client. |
| Requested commencement mode | O | An indication that is included if the user is requesting a particular commencement mode |
| NOTE: MCVideo ID information element is present if remote video push to destination user is requested. MCVideo group ID information element is present if remote video push to group is requested. |

* * * Next Change * * * *

#### 7.4.2.3	One-to-one video push

##### 7.4.2.3.1	General

One-to-one video push is a private call that only allows the calling party to transmit video to the called party, and the private call ends when the video transmission is completed.

##### 7.4.2.3.2	One-to-one video push – call setup

Procedures in figure 7.4.2.3.2-1 are the basic signalling control plane procedures for the MCVideo client initiating establishment of MCVideo private call with the chosen MCVideo user for video push.

Pre-conditions:

1.	This procedure is initiated either manually by the authorized MCVideo users at MCVideo client 1, or automatically due to triggers set by authorized MCVideo users at MCVideo client 1.

2.	Optionally, MCVideo client 1 may have a functional alias activated to be used.

3.	The MCVideo server may have subscribed to the MCVideo functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 7.4.2.3.2-1: One-to-one video push

1.	MCVideo client 1 initiates push video to MCVideo client 2, and sends a private call request to the MCVideo server using a service identifier as defined in 3GPP TS 23.228 [5] for MCVideo, for establishing a private call with the chosen MCVideo user for video push. The MCVideo private call request contains MCVideo ID of invited user, an SDP offer containing one or more media types and the video push indication to indicate that requestor is requesting to transmit video to the called party. The MCVideo user at MCVideo client 1 may include a functional alias used within the MCVideo private call request.

2.	MCVideo server checks whether the MCVideo user at MCVideo client 1 is authorized to initiate the private call for video push, and that MCVideo user at MCVideo client 2 is authorized to receive the private call for video push. MCVideo server verifies whether the provided functional alias, if present, can be used and has been activated for the user.

3.	MCVideo server may provide a progress indication to MCVideo client 1 to indicate progress in the call setup process.

NOTE 1:	Step 3 can occur at any time following step 4, and prior to step 6.

4.	If authorized, MCVideo server includes information that it communicates using MCVideo service, offers the same media types or a subset of the media types contained in the initial received request, includes the requested automatic commencement mode indication based on a requested commencement mode by the calling user or based upon the setting of the called MCVideo client and sends the corresponding MCVideo private call request towards the MCVideo client 2, including the MCVideo ID and, if available the functional alias of the calling MCVideo user 1. If the called MCVideo user has registered to the MCVideo service with multiple MCVideo UEs and has designated the MCVideo UE for receiving the private calls, then the incoming MCVideo private call request is delivered only to the designated MCVideo UE.

5.	The MCVideo client 2 notifies the user about the incoming private call for video push. If the functional alias of the calling user is included it is displayed.

6.	The MCVideo client 2 accepts the private call for video push, and sends an MCVideo private call response to the MCVideo server.

7.	Upon receiving the MCVideo private call response from MCVideo client 2 accepting the private call request for video push, the MCVideo server informs the MCVideo client 1 about successful call establishment via a private call response message.

8.	MCVideo client 1 and MCVideo client 2 have successfully established media plane and transmission control for media communication.

NOTE 2:	When the video transmission is completed, the private call is released.

* * * End of Changes * * * *