3GPP TSG-SA WG6 Meeting #30	S6-190869

Newport Beach, CA, USA, 8th – 12th April 2019	(revision of S6-190798)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.379 | CR | 0180 | rev | 3 | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Adding newly affiliated user to preconfigured group regroup |
| --- | --- |
| Source to WG: | FirstNet, Motorola Solutions |
| Source to TSG: | S6 |
| Work item code: | enh2MCPTT |  | Date: | 2019-04-12 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Details are needed to define how newly affiliated users are added to on-going preconfigured group regroup operations. |
| Summary of change: | A new procedure is added describing how a newly affiliated user is added to a preconfigured group regroup. |
| Consequences if not approved: | This aspect might be overlooked in Stage 3 leading to interoperability problems in fielded MCPTT systems. |
| Clauses affected: | 10.6.2.9.4 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First change * * *

##### 10.6.2.9.4	Adding newly affiliated user to preconfigured group regroup

Figure 10.6.2.9.4-1 illustrates the procedure to add a newly affiliated user to an in-progress preconfigured MCPTT group regroup operation.

Pre-conditions:

-	The MCPTT client is a member of a MCPTT group that is part of an in-progress preconfigured group regroup operation.

-	The MCPTT group identity and group configuration for the regroup MCPTT group has been preconfigured in the MCPTT client, and the MCPTT client has received the relevant security related information to allow it to communicate in the regroup MCPTT group.

Figure 10.6.2.9.4-1: Procedure to add a newly affiliated user to a preconfigured regroup

1.	The MCPTT client affiliates to an MCPTT group that is currently part of an in-progress preconfigured group regroup. The affiliation follows the procedure in section 10.8.3.1 of TS 23.280 [16].

2.	The MCPTT server retrieves the MCPTT group ID of the regroup group and the MCPTT group ID of the group from which configuration information for the regroup group is to be taken.

3.	The MCPTT server sends the preconfigured regroup request to the MCPTT client.

4.	The MCPTT client notifies the user of the regrouping.

5.	The MCPTT client may send the preconfigured regroup response to the MCPTT server to acknowledge the regrouping action. These acknowledgements are not sent in response to a multicast transmission of the preconfigured regroup request.

6.	The MCPTT server affiliates the regrouped MCPTT client to the regroup group.

Editor's Note: It is FFS whether this procedure can be generalized to apply to both preconfigured and GMS-based group regrouping.

Editor's Note: Affiliations of the MCPTT client to the pre-configured regroup group in the MCPTT server and coordination to the MC System is FFS.

* * * End of first change * * *

* * * End of changes * * *