3GPP TSG-SA WG6 Meeting #30	S6-190879

Newport Beach, CA, USA, 8th – 12th April 2019	(revision of S6-190799)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.379 | CR | 0182 | rev | 3 | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Broadcast group regroup call using preconfigured group |
| --- | --- |
| Source to WG: | FirstNet, Motorola Solutions |
| Source to TSG: | S6 |
| Work item code: | enh2MCPTT |  | Date: | 2019-04-12 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Enhance the preconfigured group regrouping mechanism to support a broadcast regroup call (aka MultiSelect/SimulSelect). This allows an authorized MCPTT user to initiate a broadcast call to a set of MCPTT groups, which are regrouped only for the duration of the broadcast call. |
| Summary of change: | A new procedure is added for broadcast group regroup call using a preconfigured group. |
| Consequences if not approved: | An important feature for public safety will be unsupported by the preconfigured regroup method of doing group regroup operations. |
| Clauses affected: | 10.6.2.12 (new), 10.6.2.12.1 (new), 10.6.2.12.2 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First change * * *

#### 10.6.2.12	Broadcast group regroup call using preconfigured group

##### 10.6.2.12.1	General

The temporary group created using a preconfigured group can be a broadcast group or a non-broadcast group.  The broadcast regroup is used for one-way communication where only an authorized MCPTT user is allowed to transmit and all other regroup members are only allowed to receive the communication (e.g. a call from a dispatcher to all regroup members).  The non-broadcast regroup is used for two-way communication where all regroup members can transmit and receive (i.e. the regroup group call behaves like a normal non-broadcast group call).  The broadcast regroup satisfies the temporary group-broadcast group requirements defined in 3GPP TS 22.280 [2] and is an alternative to the "Temporary group – broadcast group call" procedure (10.6.2.5.3) defined in 3GPP TS 23.379 [16].

A broadcast group regroup call using preconfigured groups can be achieved by first regrouping MCPTT users into a preconfigured group regroup group, making the broadcast group call on the preconfigured group, and then cancelling the preconfigured group regroup.

##### 10.6.2.12.2	Broadcast group regroup call procedure using preconfigured group in a single MCPTT system

The broadcast group regroup call procedure using preconfigured group allows an authorized MCPTT user to initiate a broadcast call to a set of MCPTT groups, which are regrouped only for the duration of the broadcast call. The regroup is cancelled at the end of the broadcast call to prevent users from talking back on the regroup group.  This procedure requires that the authorized MCPTT user is a group member of at least one of the MCPTT groups included in the regroup operation.

Figure 10.6.2.12.2-1 illustrates the procedure to initiate a broadcast group regroup call using a preconfigured MCPTT regroup group.

Pre-conditions:

-	MCPTT clients 1, 2, and 3 are registered with the MCPTT service.

-	The MCPTT group identity and group configuration for the regroup MCPTT group have been preconfigured in MCPTT clients 1, 2, and 3, and MCPTT clients 1, 2 and 3 have received the relevant security related information to allow them to communicate in the regroup MCPTT group.

-	MCPTT client 1 is authorized to initiate a group regroup using the preconfigured regroup procedure.

-	MCPTT client 1 is aware of a suitable preconfigured regroup group whose configuration has been preconfigured in the MC service UEs of the MCPTT users who will be regrouped.

-	MCPTT client 1 is affiliated to group 1, MCPTT client 2 is affiliated to group 2, and MCPTT client 3 is affiliated to group 3.  Group 4 is used as the regroup group.

Figure 10.6.2.12.2-1: Broadcast group regroup call using preconfigured group in a single MCPTT system

1.	The authorized user of MCPTT client 1 initiates the group regroup formation procedure using preconfigured groups as specified in 10.6.2.9.2.1. MCPTT groups 1, 2, and 3 are regrouped into group 4.

2.	The MCPTT user at MCPTT client 1 performs the broadcast group call procedure as specified in 10.6.2.5.2.

3.	If the broadcast group call is based on the preconfigured group, the MCPTT client 1 initiates the preconfigured group regroup cancellation procedure using preconfigured groups as specified in 10.6.2.9.2.2.

* * * End of first change * * *

* * * End of changes * * *