3GPP TSG-SA WG6 Meeting #30	S6-190880

Newport Beach, CA, USA, 8th – 12th April 2019	(revision of S6-190800)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.379 | CR | 0183 | rev | 3 | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Preconfigured regroup exception cases |
| --- | --- |
| Source to WG: | FirstNet, Motorola Solutions |
| Source to TSG: | S6 |
| Work item code: | enh2MCPTT |  | Date: | 2019-04-12 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Details are needed to define how exception cases are handled when a MCPTT client requests a group call on one of its affiliated groups when that group is part of a preconfigured group regroup (instead of making the request on the regroup group), and when a MCPTT client requests a group call on the preconfigured regroup group after the preconfigured group regroup has been cancelled. |
| Summary of change: | Two new procedures are added associated with preconfigured regroup describing how the MCPTT server handles these cases. |
| Consequences if not approved: | This aspect might be overlooked in Stage 3 leading to interoperability problems in fielded MCPTT systems. |
| Clauses affected: | 10.6.2.9.5 (new), 10.6.2.9.5.1 (new), 10.6.2.9.5.2 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First change * * *

##### 10.6.2.9.5	Preconfigured regroup update procedures

###### 10.6.2.9.5.1	MCPTT client PTTs on MCPTT group during an in-progress preconfigured group regroup

Figure 10.6.2.9.5.1-1 illustrates the procedure when a user attempts to setup a MCPTT group call on a group involved in an in-progress preconfigured MCPTT group regroup.

Pre-conditions:

-	The MCPTT client is an affiliated member of MCPTT group A that is part of an in-progress preconfigured group regroup with MCPTT groups B and C.

-	MCPTT group D is being used as the preconfigured regroup group.

-	The MCPTT client has missed the preconfigured regroup request message (e.g. poor signalling conditions, race condition).

Figure 10.6.2.9.5.1-1: Procedure for MCPTT client PTTs on MCPTT group during an in-progress preconfigured group regroup

1.	The MCPTT client attempts to start a call on MCPTT group A. The MCPTT client sends a group call request message to the MCPTT server containing MCPTT group A as the target group.

2.	The MCPTT server checks to see whether MCPTT group A is currently part of a preconfigured group regroup. In this case the group is part of an active preconfigured group regroup.

3.	The MCPTT server sends a group call response to the MCPTT client indicating that the call setup is denied because the group is part of an in-progress group regroup.

4.	The MCPTT server sends the preconfigured regroup request to the MCPTT client containing MCPTT group D, the group ID of the preconfigured regroup group.

NOTE 1: This message should be sent over unicast.

5.	The MCPTT client notifies the user of the group call setup failure and of the regrouping procedure.

6.	The MCPTT client sends the preconfigured regroup response to the MCPTT server to acknowledge the regrouping action.

7.	The MCPTT server affiliates the regrouped MCPTT client to the regroup group.

NOTE 2:	If there is a call currently in progress on the regroup group then this MCPTT client can be added to the call using the late entry procedure.  If there is no call currently in progress then the MCPTT user can retry the group call setup.

* * * End of first change * * *

* * * Second change * * *

###### 10.6.2.9.5.2	MCPTT client PTTs on preconfigured regroup group after group regroup has been cancelled

Figure 10.6.2.9.5.2-1 illustrates the procedure when a user attempts to setup a MCPTT group call on a preconfigured regroup group after the preconfigured MCPTT group regroup has been cancelled.

Pre-conditions:

-	The MCPTT client is a member of MCPTT group A that was part of an in-progress preconfigured group regroup with MCPTT groups B and C that has been cancelled.  MCPTT group D was used as the preconfigured regroup group.

-	The MCPTT client has missed the preconfigured regroup cancel request message (e.g. poor signalling conditions, race condition).

Figure 10.6.2.9.5.2-1: Procedure for MCPTT client PTTs on preconfigured regroup group after the group regroup is cancelled

1.	The MCPTT client attempts to start a call on MCPTT group D, the preconfigured regroup group. The MCPTT client sends a group call request message to the MCPTT server containing MCPTT group D as the target group.

2.	The MCPTT server checks to see whether MCPTT group D is currently being used as part of a preconfigured group regroup.  In this case the preconfigured group regroup is no longer active.

NOTE 1: The preconfigured regroup group D can be a group in the MCPTT client's profile, and the MCPTT client can be a member of group D.

3.	The MCPTT server sends a group call response to the MCPTT client indicating that the call setup is denied because the group regroup is no longer active.

NOTE 2: In the following, steps 4 and 6 are optional.

4.	The MCPTT server sends the preconfigured regroup cancel request to the MCPTT client.

NOTE 3: This message should be sent over unicast.

5.	The MCPTT client notifies the user of the group call setup failure and of the regrouping cancellation.

6.	The MCPTT client sends the preconfigured regroup cancel response to the MCPTT server to acknowledge the regrouping cancellation.

NOTE 4:	If there is a call currently in progress on MCPTT group A that was previously part of the group regroup then this MCPTT client can be added to the call using the late entry procedure.  If there is no call currently in progress then the MCPTT user can retry the group call setup on MCPTT group A.

* * * End of second change * * *

* * * End of changes * * *