3GPP TSG-SA WG6 Meeting #30	S6-190850

Newport Beach, California, USA, 8th – 12th April 2019	(revision of S6-190603/0701)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.379 | CR | 0200 | rev | 2 | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Functional alias call |
| --- | --- |
| Source to WG: | Huawei, Hisilicon |
| Source to TSG: | S6 |
| Work item code: | MONASTERY2 |  | Date: | 2019-03-20 |
| Category: | B |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Currently, the activation, deactivation and taken of the functional alias is managed at the functional controlkling MCPTT server. In other words, functional alias controlling server helds the latest MCPTT users who activate the functional alias. While the functional controlling server may be a different one from the call controlling MCPTT server configured for private/group call in R15 and before, especially considering multilple functional alias controlling servers deployments shown below. During the call setup with the called party to be a functional alias, the call controlling MCPTT server has to get the latest MCPTT ID of the user who activates the functional alias for call request routing, which is missing from current specification. This CR propose the procedure to enable call controlling MCPTT server to subscribe the activated MCPTT user(s) of a functional alias from the functional alias controlling server. |
| Summary of change: | New procedures and information flows about activated MCPTT user(s) of functional alias subscription and notification. |
| Consequences if not approved: | Can not support functional alias to be used in call setup. |
| Clauses affected: | 10.x (new), 10.x.1 new), 10.x.2 (new), 10.x.2.1 (new), 10.x.2.2 (new), 10.x.2.2 (new), 10.x.2.3 (new), 10.x.2.4 (new), 10.7.2.x.2 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

## 10.x	Subscription and notification for functional alias

### 10.x.1	General

The MCPTT server obtains the list of MCPTT users who have activated a functional alias from the functional alias controlling MCPTT server via subscription and notification mechanisms.

Editor's note:	It is FFS whether this procedure is general to all the MC services and can be moved to 3GPP TS 23.280.

#### 10.x.2	Information flows for subscription and notification for functional alias

##### 10.x.2.1	Subscribe functional alias request

Table 10.x.2.1-1 describes the information flow subscribe functional alias request from the MCPTT server to the functional alias controlling MCPTT server.

Table 10.x.2.1-1: Subscribe functional alias request

| Information element | Status | Description |
| --- | --- | --- |
| Functional alias | M | The functional alias for which subscription is requested by the MCPTT server. |

##### 10.x.2.2	Subscribe functional alias response

Table 10.x.2.2-1 describes the information flow subscribe functional alias response from the functional alias controlling MCPTT server to the MCPTT server.

Table 10.x.2.2-1: Subscribe functional alias response

| Information element | Status | Description |
| --- | --- | --- |
| Functional alias | M | The functional alias for which subscription is requested by the MCPTT server. |
| Status | M | Success or failure of the request |

##### 10.x.2.3	Notify functional alias request

Table 10.x.2.3-1 describes the information flow notify functional alias request from the functional alias controlling MCPTT server to the MCPTT server.

Table 10.x.2.3-1: Notify functional alias request

| Information element | Status | Description |
| --- | --- | --- |
| Functional alias | M | The functional alias subscribed to by the MCPTT server |
| MCPTT ID list (NOTE) | M | The list of MCPTT IDs that is activated for the functional alias |
| NOTE: The MCPTT ID list can be an empty list if no MCPTT user activates the functional alias. |

##### 10.x.2.4	Notify functional alias response

Table 10.x.2.4-1 describes the information flow notify functional alias response from the MCPTT server to the functional alias controlling MCPTT server.

Table 10.x.2.4-1: Notify functional alias response

| Information element | Status | Description |
| --- | --- | --- |
| Functional alias | M | The functional alias for which a list of MCPTT users who activate the functional alias is requested. |

### 10.x.3	Procedure

#### 10.x.3.1	Subscription for functional alias procedure

The procedure for subscription for functional alias is described in figure 10.x.3.1-1.

Pre-conditions:

-	The functional alias controlling MCPTT server holds a list of MCPTT users who has activated the functional alias.

Figure 10.x.3.1-1: Subscription for functional alias

1.	The MCPTT server sends a subscribe functional alias request to the functional alias controlling MCPTT server in order to receive notifications about the  list of MCPTT users who has activated the function alias.

2.	The functional alias controlling MCPTT server provides a subscribe functional alias response to the MCPTT server indicating success or failure of the request.

#### 10.x.3.2	Notification for functional alias procedure

The procedure for notification for functional alias as shown in figure 10.x.3.2-1 is used by the functional alias controlling MCPTT server to inform the MCPTT server about MCPTT users who activate of the functional alias.

Pre-conditions:

-	The MCPTT server has subscribed to the functional alias

-	The list of MCPTT users who has activated the functional alias is changed at functional alias controlling MCPTT server due to activation, deactivation or taken over.

Figure 10.x.3.2-1: Notification for the functional alias

1.	The functional alias controlling MCPTT server provides the list of MCPTT users who has activated the functional alias in the notify functional alias request to the call controlling MCPTT server.

2.	The call controlling MCPTT server provides a notify functional alias response to the functional alias controlling MCPTT server.