## Slide 1: MEC update for SA6
Olaf Pollakowski
3GPP delegate, Nokia

## Slide 2
Where are we now?
92 members - Operators – Technology Vendors – IT players – Application developers
Foundation for Edge Computing created – Fully standardized solution to enable applications in distributed cloud created by ETSI MEC + 3GPP
API Framework
API Principles & Guidelines
Service exposure via standardized APIs
Management & Orchestration of Applications
Selection & re-location of UPF
AF influence on traffic routing
Mobility event notifications from SMF
Concurrent access to local and central DN
+
=
ETSI MEC – What we have achieved

## Slide 3
Focused on application enablement & APIs
Application Enablement
(API Framework)
Specific service-related APIs
Management and Orchestration related APIs
API Principles
Facilitate the running of applications at the correct location at the right time, based on technical and business parameters
Services expose network and context information via specific service-related APIs.
A different set of services may be applicable at different locations
A framework for delivering services which may be consumed or offered by (locally hosted or remote) authorized applications. It enables:
registration, announcement, discovery and notification of services;
authentication and authorization of applications providing and consuming services;
communication support for services (query/response and notifications).
A set of API principles and guidance for developing and documenting APIs inside or outside ETSI which ensures that a consistent set of APIs are used by developers.
The work was inspired by the TMF and OMA best practices.
The APIs are designed to be application-developer friendly and easy to implement so as to stimulate innovation and foster the development of applications.
Enables a myriad of new use cases across multiple sectors as well as innovative business opportunities
ETSI MEC – Foundation for Edge Computing

## Slide 4
* Device = e.g. UE or laptop w internet connectivity | CFS = Customer Facing Service | LCM = LifeCycle Management
  MEC Management and orchestration
    Facilitates running applications at the right location at the right time, based on technical and business parameters. Applications can be onboarded directly, via the CFS portal, or from Device (UE).
  MEC Host
    Offers virtualisation infrastructure to run mobile edge applications (possibly alongside with network functions)
  MEC Platform
    An environment where applications can discover, advertise, consume and offer mobile edge services.
    Controls the data-plane based on traffic rules
  MEC Services
    Exposes network and context information, such as:
    Radio network information service
    Location information service
    Bandwidth manager service
    UE Identity Service
ETSI MEC – Reference Architecture

## Slide 5: Now in our 2nd 3-year Phase of work
Key overall specification
  Technical Requirements (MEC 002)
  Framework and Reference Architecture (MEC 003)
  MEC Proof of Concept (PoC) Process (MEC-IEG 005)
  API Framework (MEC 009)
IaaS Management APIs
  Platform mgmt. (MEC 010-1)
  Application mgmt. (MEC 010-2)
  Device-triggered LCM operations (MEC 016)
Application Enablement & Service Exposure
  Required Platform Svcs / App. Enablement (MEC 011)
  Service APIs (MEC 012, 013, 014, 015)
Key Studies for Future Work
  Study on MEC in NFV (MEC 017)
  Study on Mobility Support (MEC 018)
ETSI MEC phase 1 (Completed)
ETSI MEC phase 2 (in Progress)
Evolution of Phase 1 and closing open items
  Application Mobility (MEC 021)
  Lawful Intercept (MEC 026 - published)
Addressing key Industry Segments
  V2X (MEC 022 - published, MEC 030)
  IoT (MEC 033), Industrial Automation, VR/AR
Key use-cases and new requirement
  Network Slicing (MEC 024)
  Container Support (MEC 027)
Normative work for integration with NFV
  Incorporate in v2 of existing specs as needed
From “Mobile” to “Multi-Access”
  Wi-Fi (MEC 028)
  Fixed Access (MEC 029)
MEC integration in 5G networks (MEC 031)
Developer community engagement
  API publication through ETSI Forge (more overleaf)
  Hackathons
Testing and Compliance (MEC 025 - published, MEC 032)

## Slide 6: ETSI MEC links to the ecosystem
Alignment with ETSI NFV
MEC architecture variant for deploying MEC in NFV environments has been developed
Work in collaboration with ETSI NFV
Alignment with 3GPP in areas of Information Exposure and API framework
ETSI MEC has active work to further align through “MEC in 5G” study
ETSI MEC is exploring the use of CAPIF APIs for publishing and discovering MEC APIs
Increase MEC adoption by making it available in Open Source
ETSI MEC API framework contributed to Linux Foundation Akraino
MEC APIs publicly available to developers
Machine-readable representation of APIs available in OpenAPI format through ETSI forge
Sandbox environment in creation
ETSI MEC
SDOs
NFV, 3GPP, …
Open Source Communities
Cloud Application
Developers