3GPP TSG-SA WG6 Meeting #32	S6-191606

Rome, Italy, 8th – 12th July 2019	(revision of S6-191554)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.280 | CR | 0207 | rev | 3 | Current version: | 16.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Providing activated functional alias information to the group controlling server |
| --- | --- |
| Source to WG: | Nokia, Nokia Shanghai Bell |
| Source to TSG: | S6 |
| Work item code: | eMONASTERY2 |  | Date: | 2019-07-01 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Stage 1 requirements 3GPP TS 22.280 [R-6.4.4-003] and [R-6.4.4-004] require to prevent de-affiliation when using a specific functional alias(es) and [R-5.9a-029] requires to get the list of currently affiliated members of an MC service group including the activated functional alias(es) of those members. Both features require that the group controlling server has knowledge about the functional alias used by the MC service client within the group. The CR suggests to add client initiated functional alias to group binding and unbinding procedures. |
| Summary of change: | Adds new informations flows and procedures for client initiated functional alias to group binding and unbinding procedures. |
| Consequences if not approved: | Specification is incomplete. |
| Clauses affected: | 10.1.2.X (new), 10.1.2.Y (new), 10.1.2.Z (new), 10.1.2.XX (new), 10.13.X (new), 10.13.X.1 (new), 10.13.X.2 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

#### 10.1.2.X	Functional alias to group binding request

Table 10.1.2.X-1 describes the information flow functional alias to group binding request from the MC service client to the MC service server.

Table 10.1.2.X-1: Functional alias to group binding request

| Information element | Status | Description |
| --- | --- | --- |
| MC service ID | M | The MC service ID of the originator who triggers the functional alias to group binding request. |
| MC service group ID list (see NOTE) | M | A list of MC service group IDs to which the originator requests the functional alias to group binding. |
| Functional alias list (see NOTE) | M | A list of functional aliases. |
| NOTE: MC service group IDs and functional aliases have a one to one relationship. |

#### 10.1.2.Y	Functional alias to group binding response

Table 10.1.2.Y-1 describes the information flow functional alias to group binding response from the MC service client to the MC service server.

Table 10.1.2.Y-1: Functional alias to group binding response

| Information element | Status | Description |
| --- | --- | --- |
| MC service ID | M | The MC service ID of the originator who triggers the functional alias to group binding request. |
| Result | M | Indicates the success or failure for the result |

#### 10.1.2.Z	Functional alias to group unbinding request

Table 10.1.2.Z-1 describes the information flow functional alias to group unbinding request from the MC service client to the MC service server.

Table 10.1.2.Z-1: Functional alias to group unbinding request

| Information element | Status | Description |
| --- | --- | --- |
| MC service ID | M | The MC service ID of the originator who triggers the functional alias to group unbinding request. |
| MC service group ID list (see NOTE) | M | A list of MC service group IDs to which the originator requests the functional alias to group unbinding. |
| Functional alias list (see NOTE) | M | A list of functional aliases. |
| NOTE: MC service group IDs and functional aliases have a one to one relationship. |

#### 10.1.2.XX	Functional alias to group unbinding response

Table 10.1.2.XX-1 describes the information flow functional alias to group unbinding response from the MC service client to the MC service server.

Table 10.1.2.XX-1: Functional alias to group unbinding response

| Information element | Status | Description |
| --- | --- | --- |
| MC service ID | M | The MC service ID of the originator who triggers the functional alias to group unbinding request. |
| Result | M | Indicates the success or failure for the result |

* * * Next Change * * * *

### 10.13.X	Functional alias to group binding

#### 10.13.X.1	General

The MC service client creates a functional alias to group binding association to be stored within the group controlling MC server. Once a functional alias is bound to a group it is bound till the functional alias is unbound to the group. After an MC service log-off the user's functional alias to group bindings are deleted.

NOTE:	Affiliation and de-affiliation procedures do not change the functional alias to group binding.

Editor's note:	How the functional alias to group binding impacts existing group call requests is FFS.

#### 10.13.X.2	Functional alias to group binding

The procedure for binding a functional alias with a group is described in figure 10.13.X.2-1.

Pre-conditions:

-	The MC service server has subscribed to the MC service functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 10.13.X.2-1: Functional alias to group binding procedure

1.	The MC service client sends a functional alias to group binding request to the group controlling MC service server to bind functional aliases to groups to be used for communications within those groups.

2.	The group controlling MC service server provides a functional alias to group binding response to the MC service client indicating success or failure of the request.

#### 10.13.X.3	Functional alias to group unbinding

The procedure for unbinding a functional alias with a group is described in figure 10.13.X.3-1.

Pre-conditions:

-	The MC service server has subscribed to the MC service functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 10.13.X.3-1: Functional alias to group unbinding procedure

1.	The MC service client sends a functional alias to group unbinding request to the group controlling MC service server to unbind functional aliases from groups which are not used for communications within those groups anymore.

2.	The group controlling MC service server provides a functional alias to group unbinding response to the MC service client indicating success or failure of the request. The MC service server also checks whether the MC service client is the last client who has bound a certain functional alias to a group which may prevent unbinding that functional alias from the group.

* * * End of Changes * * * *