3GPP TSG-SA WG6 Meeting #32	S6-191557

Roma, Italy 8th – 12th July 2019	(revision of S6-191453_was_S6-191271)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.282 | CR | 0163 | rev | 2 | Current version: | 16.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | SDS addressing based on functional alias |
| --- | --- |
| Source to WG: | UIC |
| Source to TSG: | S6 |
| Work item code: | eMONASTERY2 |  | Date: | 2019-07-10 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Based on the requirement in TS 22.280, the addressed MCData user shall be adressable by its associated functional alias. This functionality is missing in the SDS context. [R-5.9a-002] The MCX User shall be reachable by its functional alias(es) from within the MCX Service system where the functional alias was activated. |
| Summary of change: | The present change request adds the use of the functional alias as an addressing element to reach the target user for one-to-one SDS service. A functional alias can be shared by MCData users at the same time and may require to include all MCData users sharing the same functional alias. In order not to violate the standalone SDS principle and the associated end-to-end security context it continues to be standalone SDS relationship when multiple MCData user share a single functional alias, only one MCData user behind the functional alias can be involved. Accordingly, the MCData server resolves the association of the functional alias to the corresponding MCData users. Then in a top-down approach, the MCData users are verified if their clients have SDS capabilities. The first MCData user in the FA association list that matches will be included in the IP connectivity point-to-point connection. The present CR proposal just indicates the changes necessary compared to the case no functional alias is used to address the target MCData user. |
| Consequences if not approved: | The requirement R-5.9a-002 in TS 22.280 clause 5.9a cannot be fulfilled. |
| Clauses affected: | 7.4.2.2.1, 7.4.2.2.2, 7.4.2.3.1, 7.4.2.3.2, 7.4.2.4.1, 7.4.2.4.2, 7.4.2.1.1, 7.4.2.1.3, 7.4.2.1.5, 7.4.2.1.4 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: | None |

********************************************1st Change*******************************************

#### 7.4.2.2	One-to-one standalone short data service using signalling control plane

##### 7.4.2.2.1	General

A MCData user initiates a standalone SDS data transfer with another MCData user. For the SDS data transfer signalling plane is used. The target MCData user may be addressed using the functional alias that can be shared with other MCData users.

In order not to violate the standalone principle when a functional alias is shared among multiple MCData users, only one target MCData user can participate to a standalone short data service. The MCData server resolves the associated MCData users of the functional alias and checks the MCData users that are on the list about its SDS capabilities. Processing in the delivery of the SDS starts with the number 1 (topmost) MCData ID having SDS capabilities on the list and, if necessary, is continued consecutively in the numbering. If a MCData user has SDS capabilities, the SDS will be forwarded to this MCData ID. If the SDS data request is rejected by the addressed MCData client, the MCData server addresses the next MCData ID from the list. This process is continued until all associated MCData IDs have been checked. If the destination MCData user on the list cannot be established, the initiating MCData user will be informed accordingly.

##### 7.4.2.2.2	Procedure

The procedure in figure 7.4.2.2.2-1 describes the case where an MCData user is initiating one-to-one MCData data communication for sending standalone SDS data to other MCData user, with or without disposition request. Standalone refers to sending unidirectional data in one transaction.

Pre-conditions:

1.	The SDS payload data size is below the configured maximum payload data size for SDS over signalling control plane.

2.	MCData users on MCData client 1 and MCData client 2 are already registered for receiving MCData service.

3.	MCData client 1 and MCData client 2 belong to the same MCData system.

4.	Optionally, the MCData client may have activated functional alias to be used.

5.-	The MCData server may have subscribed to the MCData functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 7.4.2.2.2-1: One-to-one standalone short data service using signalling control plane

1.	The user at MCData client 1 initiates an SDS data transfer for the chosen MCData user.

2.	MCData client 1 sends a MCData standalone data request towards the MCData server. The MCData standalone data request contains conversation identifier for message thread indication. The MCData standalone data request may contain disposition request if indicated by the user at MCData client 1. MCData user at MCData client 1 may include a functional alias within the SDS data transfer and addresses the target MCData client 2 using a functional alias.

3.	MCData server checks whether the MCData user at MCData client 1 is authorized to send MCData standalone data request. MCData server verifies whether the provided functional alias of MCData client 1, if present, can be used and has been activated for the user. The MCData server also checks whether any policy is to be asserted to limit certain types of message or content to certain members due, for example, to location or user privilege or affiliation. If functional alias is used to address that target MCData user, the MCData server resolves the MCData IDs of the functional alias. The resulting list contains all associated MCData IDs/MCData users that share this functional alias. The MCData server now checks which MCData users have SDS capabilities and which are authorized to receive SDS. The MCData server allows only two participating MCData clients for a standalone short data service.

4.	MCData server initiates the MCData standalone data request towards the MCData user that is the first on the list according to step 3.

5.	If the payload is for MCData user consumption (e.g. is not application data, is not command instructions, etc.) then the MCData user of MCData client 2 may be notified. Otherwise if the payload is not for MCData user consumption, then the MCData user of MCData client 2 shall not be notified. The action taken when the payload contains application data or command instructions are specific based on the contents of the payload. Payload content received by MCData client 2 which is addressed to a known local non-MCData application that is not yet running shall cause the MCData client 2 to start the local non-MCData application (i.e., remote start application) and shall pass the payload content to the just started application.

6.	If the MCData data disposition for delivery was requested by the user at MCData client 1, then the receiving MCData client initiates a MCData data disposition notification for delivery report. The MCData data disposition notification from MCData client may be stored by the MCData server for disposition history interrogation from authorized MCData users.

7.	MCData data disposition notification is sent to the disposition requesting user at MCData client 1.

8.	If the MCData data disposition for read was requested by the user at MCData client 1, then once the receiving user reads the data, the receiving MCData client 2 initiates a MCData data disposition notification for read report. The MCData data disposition notification from MCData client may be stored by the MCData server for disposition history interrogation from authorized MCData users. The MCData data disposition notification from MCData client may be stored by the MCData server for disposition history interrogation from authorized MCData users.

9.	MCData data disposition notification is sent to the disposition requesting user at MCData client 1.

#### 7.4.2.3	One-to-one standalone short data service using media plane

##### 7.4.2.3.1	General

A MCData user initiates a standalone SDS data transfer with another MCData user. For the SDS data transfer media plane is used. The target MCData user may be addressed using the functional alias that can be shared with other MCData users.

In order not to violate the standalone principle when a functional alias is shared by multiple MCData users, only one target MCData user can participate to a standalone short data service. The MCData server resolves the associated MCData users of the functional alias and checks the MCData users that are on the list about its SDS capabilities. Processing in the delivery of the SDS starts with the number 1 (topmost) MCData ID having SDS capabilities on the list and, if necessary, is continued consecutively in the numbering. If a MCData user has SDS capabilities, the SDS will be forwarded to this MCData user. If the SDS data request is rejected by the addressed MCData client, the MCData server addresses the next MCData ID from the list. This process is continued until all associated MCData IDs have been checked. If the SDS service to the destination MCData users on the list cannot be established, the initiating MCData user will be informed accordingly.

##### 7.4.2.3.2	Procedure

The procedure in figure 7.4.2.3.2-1 describes the case where an MCData user is initiating one-to-one MCData data communication for sending standalone SDS data to other MCData user, with or without disposition request. Standalone refers to sending unidirectional data in one transaction. The SDS payload data size is assumed to be above the configured maximum payload data size for SDS over signalling control plane.

Pre-conditions:

1.	MCData users on MCData client 1 and MCData client 2 are already registered for receiving MCData service.

2.	MCData client 1 and MCData client 2 belong to the same MCData system.

3.	Optionally, the MCData client may have an activated functional alias to be used.

4.	The MCData server may have subscribed to the MCData functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 7.4.2.3.2-1: One-to-one standalone short data service using media plane

1.	User at MCData client 1 would like to initiate an SDS data transfer request for the chosen MCData user.

2.	MCData client 1 sends a MCData standalone session data request towards the MCData server. The MCData standalone data request contains one MCData user for one-to-one data communication as selected by the user at MCData client 1. The MCData standalone session data request contains conversation identifier for message thread indication. The MCData data request may contain disposition request if indicated by the user at MCData client 1. MCData user at MCData client 1 may include a functional alias within the SDS data transfer and addresses the target MCData client 2 using a functional alias.

3.	MCData server checks whether the MCData user at MCData client 1 is authorized to send MCData standalone session data request. MCData server verifies whether the provided functional alias of MCData client 1, if present, can be used and has been activated for the user. The MCData server also checks whether any policy is to be asserted to limit certain types of message or content to certain members due, for example, to location or user privilege. MCData server determines the eligible MCData user(s) after policy assertion for sending the MCData standalone session data request. If functional alias is used to address that target MCData user, the MCData server resolves the MCData IDs of the functional alias. The resulting list contains all associated MCData IDs/MCData users that share this functional alias. The MCData server now checks which MCData users have SDS capabilities and which are authorized to receive SDS. The MCData server allows only two participating MCData clients for a standalone short data service. To integrate a possible MCData user from the list to the standalone SDS data service, the MCData server works the list of the MCData user from top to bottom and stops until one of the corresponding MCData users from the list accepts the standalone SDS service.

4.	MCData server initiates the MCData standalone session data request towards the MCData users determined.

NOTE:	MCData client 2 corresponds to the MCData user(s) after resolution of the functional alias.

5.	The receiving MCData client 2 automatically accepts the MCData standalone session data request and responds with MCData standalone session data response towards MCData server.

6.	MCData server forwards the MCData client 2 accepted response to the MCData user initiating the MCData standalone session data request.

7.	MCData client 1 and MCData client 2 have successfully established media plane for data communication and the MCData client 1 transmits the SDS data.

8.	If the payload is for MCData user consumption (e.g. is not application data, is not command instructions, etc.) then the MCData user of MCData client 2 may be notified. Otherwise if the payload is not for MCData user consumption, then the MCData user of MCData client 2 shall not be notified. The action taken when the payload contains application data or command instructions are specific based on the contents of the payload. Payload content received by MCData client 2 which is addressed to a known local non-MCData application that is not yet running shall cause the MCData client 2 to start the local non-MCData application (i.e., remote start application) and shall pass the payload content to the just started application.

9.	If the MCData data disposition for delivery was requested by the user at MCData client 1, then the receiving MCData client initiates a MCData data disposition notification for delivery report. The MCData data disposition notification from the receiving MCData client may be stored by the MCData server for disposition history interrogation from authorized MCData users.

10.	MCData data disposition notification is sent to the disposition requesting user at MCData client 1.

11. If the MCData disposition for read was requested by the user at MCData client 1, then once the receiving user reads the data, the receiving MCData client 2 initiates a MCData disposition notification for read report. The MCData data disposition notification from the receiving MCData client may be stored by the MCData server for disposition history interrogation from authorized MCData users.

12.	MCData data disposition notification is sent to the disposition requesting user at MCData client 1.

#### 7.4.2.4	One-to-one short data service session

##### 7.4.2.4.1	General

A MCData user triggers an establishment of a MCData session with another MCData user for the exchange of SDS data. The target MCData user may be addressed using the functional alias that can be shared with other MCData users.

In order not to violate the standalone principle when a functional alias is shared by multiple MCData users, only one target MCData user can participate to a standalone short data service. The MCData server resolves the associated MCData users of the functional alias and checks the MCData users that are on the list about its SDS capabilities. Processing in the delivery of the SDS starts with the number 1 (topmost) MCData ID having SDS capabilities on the list and, if necessary, is continued consecutively in the numbering. If a MCData user has SDS capabilities, the SDS will be forwarded to this MCData user. If the SDS data request is rejected by the addressed MCData client, the MCData server addresses the next MCData user from the list. This process is continued until all associated MCData IDs have been checked. If the SDS service to the destination MCData users on the list cannot be established, the initiating MCData user will be informed accordingly.

##### 7.4.2.4.2	Procedure

The procedure in figure 7.4.2.4.2-1 describes the case where an MCData user is initiating data communication session with another MCData user for exchanging at least one SDS data transaction between them, with or without disposition request using MCData-SDS-1 and MCData-SDS-2 or MCData-SDS-3 reference points.

Pre-conditions:

1.	MCData users on MCData client 1 and MCData client 2 are already registered for receiving MCData service.

2.	Optionally, the MCData client may have activated functional alias to be used.

3.	The MCData server may have subscribed to the MCData functional alias controlling server within the MC system for functional alias activation/de-activation updates.

Figure 7.4.2.4.2-1: One-to-one short data service session

1.	User at MCData client 1 would like to initiate an SDS data communication session request for the chosen MCData user.

2.	MCData client 1 sends a MCData session data request towards the MCData server. The MCData standalone data request contains one MCData user for one-to-one data communication as selected by the user at MCData client 1. The MCData session data request contains conversation identifier for message thread indication. MCData user at MCData client 1 may include a functional alias within the SDS data transfer and addresses the target MCData client 2 using a functional alias.

3.	MCData server checks whether the MCData user at MCData client 1 is authorized to send MCData session data request. The MCData server also checks whether any policy is to be asserted to limit certain types of message or content to certain members due, for example, to location or user privilege. MCData server determines the eligible MCData user(s) after policy assertion for sending the MCData session data request. MCData server also verifies whether the provided functional alias of MCData client 1, if present, can be used and has been activated for the user. If functional alias is used to address that target MCData user, the MCData server resolves the MCData IDs of the functional alias. The resulting list contains all associated MCData IDs/MCData users that share this functional alias. The MCData server now checks which MCData users have SDS capabilities and which are authorized to receive SDS. The MCData server allows only two participating MCData clients for a standalone short data service. To integrate a possible MCData user from the list to the standalone SDS data service, the MCData server works the list of the MCData user from top to bottom and stops until one of the corresponding MCData users from the list accepts the standalone SDS service.

4.	MCData server initiates the MCData session data request towards the MCData users determined.

NOTE:	MCData client 2 corresponds to the MCData user(s) after resolution of the functional alias.

5.	The receiving MCData client 2 optionally notifies the user about the incoming MCData session data request.

6.	The receiving MCData client 2 accepts the MCData session data request and responds with MCData session data response towards MCData server.

7.	MCData server forwards the MCData client 2 accepted response to the MCData user initiating the MCData session data request.

8. and 10.	MCData client 1 and MCData client 2 have successfully established media plane for data communication and either MCData client can transmit SDS data. The MCData data request may contain disposition request if indicated by the client sending data. If MCData data disposition was requested by the user, then the receiving MCData client initiates a MCData data disposition notification for delivery, read reports to the disposition requesting user. The MCData data disposition notification from MCData user may be stored by the MCData server for disposition history interrogation from authorized users.

9. and 11.	If the payload is for MCData user consumption (e.g. is not application data, is not command instructions, etc.) then the MCData user of MCData client 2 may be notified, otherwise the MCData user of MCData client 2 shall not be notified.

12. After SDS data transaction is complete, the established media plane is released.

********************************************2nd Change***************************************

#### 7.4.2.1	Information flows for short data service

##### 7.4.2.1.1	MCData standalone data request

Table 7.4.2.1.1-1 describes the information flow for the MCData standalone data request sent from the MCData client to the MCData server and from the MCData server to another MCData client.

Table 7.4.2.1.1-1: MCData standalone data request (MCData client to MCData server)

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user sending data |
| Functional alias | O | The associated functional alias of the MCData user sending data. |
| MCData ID (NOTE 2) | O | The identity of the MCData user towards which the data is sent |
| Functional alias (NOTE 2) | O | The associated functional alias of the MCData user identity towards which the data is sent. |
| Conversation Identifier | M | Identifies the conversation |
| Transaction Identifier | M | Identifies the MCData transaction |
| Reply Identifier | O | Identifies the original MCData transaction to which the current transaction is a reply to |
| Disposition Type | O | Indicates the disposition type expected from the receiver (i.e., delivered or read or both) |
| Payload Destination Type | M | Indicates whether the payload is for application consumption or MCData client consumption |
| Application identifier (see NOTE 1) | O | Identifies the application for which the payload is intended (e.g. text string, port address, URI) |
| Payload | M | SDS content |
| NOTE 1: The application identifier shall be included only if the payload destination type indicates that the payload is for application consumption. NOTE 2: Either the MCData ID or the functional alias must be present. |

Table 7.4.2.1.1-2: MCData standalone data request (MCData server to MCData client)

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user sending data |
| MCData ID | M | The identity of the MCData user towards which the data is sent |
| Conversation Identifier | M | Identifies the conversation |
| Transaction Identifier | M | Identifies the MCData transaction |
| Reply Identifier | O | Identifies the original MCData transaction to which the current transaction is a reply to |
| Disposition Type | O | Indicates the disposition type expected from the receiver (i.e., delivered or read or both) |
| Payload Destination Type | M | Indicates whether the payload is for application consumption or MCData client consumption |
| Application identifier (see NOTE) | O | Identifies the application for which the payload is intended (e.g. text string, port address, URI) |
| Payload | M | SDS content |
| NOTE: The application identifier shall be included only if the payload destination type indicates that the payload is for application consumption. |

********************************************3rd Change***************************************

##### 7.4.2.1.3	MCData standalone session data request

Table 7.4.2.1.3-1 describes the information flow for the MCData standalone session data request sent from the MCData client to the MCData server and from the MCData server to another MCData client.

Table 7.4.2.1.3-1: MCData standalone session data request (MCData client to MCData server)

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user sending data |
| Functional alias | O | The associated functional alias of the MCData user sending data. |
| MCData ID (NOTE 2) | O | The identity of the MCData user towards which the data is sent |
| Functional alias (NOTE 2) | O | The associated functional alias of the MCData user identity towards which the data is sent. |
| Conversation Identifier | M | Identifies the conversation |
| Transaction Identifier | M | Identifies the MCData transaction |
| Reply Identifier | O | Identifies the original MCData transaction to which the current transaction is a reply to |
| Transaction type | M | Standalone transaction |
| Disposition Type | O | Indicates the disposition type expected from the receiver (i.e., delivered or read or both) |
| Payload Destination Type | M | Indicates whether the SDS payload is for application consumption or MCData user consumption |
| Application identifier (see NOTE 1) | O | Identifies the application for which the payload is intended (e.g. text string, port address, URI) |
| SDP offer | M | Media parameters offered |
| NOTE 1: The application identifier shall be included only if the payload destination type indicates that the SDS message is for application consumption. NOTE 2: Either the MCData ID or the functional alias must be present. |

Table 7.4.2.1.3-2: MCData standalone session data request (MCData server to MCData client)

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user sending data |
| MCData ID | O | The identity of the MCData user towards which the data is sent |
| Conversation Identifier | M | Identifies the conversation |
| Transaction Identifier | M | Identifies the MCData transaction |
| Reply Identifier | O | Identifies the original MCData transaction to which the current transaction is a reply to |
| Transaction type | M | Standalone transaction |
| Disposition Type | O | Indicates the disposition type expected from the receiver (i.e., delivered or read or both) |
| Payload Destination Type | M | Indicates whether the SDS payload is for application consumption or MCData user consumption |
| Application identifier (see NOTE 1) | O | Identifies the application for which the payload is intended (e.g. text string, port address, URI) |
| SDP offer | M | Media parameters offered |
| NOTE 1: The application identifier shall be included only if the payload destination type indicates that the SDS message is for application consumption. |

********************************************4th Change***************************************

##### 7.4.2.1.5	MCData session data request

Table 7.4.2.1.5-1 describes the information flow for the MCData session data request sent from the MCData client to the MCData server and from the MCData server to another MCData client.

Table 7.4.2.1.5-1: MCData session data request (MCData client to MCData server)

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user sending data |
| Functional alias | O | The associated functional alias of the MCData user sending data. |
| MCData ID (NOTE 2) | O | The identity of the MCData user towards which the data is sent |
| Functional alias (NOTE 2) | O | The associated functional alias of the MCData user identity towards which the data is sent. |
| Conversation Identifier | M | Identifies the conversation |
| Transaction Identifier | M | Identifies the MCData transaction |
| Reply Identifier | O | Identifies the original MCData transaction to which the current transaction is a reply to |
| Transaction type | M | Session based transactions |
| Disposition Type | O | Indicates the disposition type expected from the receiver (i.e., delivered or read or both) |
| Payload Destination Type | M | Indicates whether the SDS payload is for application consumption or MCData user consumption |
| Application identifier (see NOTE 1) | O | Identifies the application for which the payload is intended (e.g. text string, port address, URI) |
| SDP offer | M | Media parameters offered |
| Requested priority | O | Application priority level requested for this communication session |
| NOTE 1: The application identifier shall be included only if the payload destination type indicates that the SDS message is for application consumption. NOTE 2: Either the MCData ID or the functional alias must be present. |

Table 7.4.2.1.5-2: MCData session data request (MCData server to MCData client)

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user sending data |
| MCData ID | O | The identity of the MCData user towards which the data is sent |
| Conversation Identifier | M | Identifies the conversation |
| Transaction Identifier | M | Identifies the MCData transaction |
| Reply Identifier | O | Identifies the original MCData transaction to which the current transaction is a reply to |
| Transaction type | M | Session based transactions |
| Disposition Type | O | Indicates the disposition type expected from the receiver (i.e., delivered or read or both) |
| Payload Destination Type | M | Indicates whether the SDS payload is for application consumption or MCData user consumption |
| Application identifier (see NOTE 1) | O | Identifies the application for which the payload is intended (e.g. text string, port address, URI) |
| SDP offer | M | Media parameters offered |
| Requested priority | O | Application priority level requested for this communication session |
| NOTE 1: The application identifier shall be included only if the payload destination type indicates that the SDS message is for application consumption. |

********************************************5th Change***************************************

##### 7.4.2.1.4	MCData standalone session data response

Table 7.4.2.1.4-1 describes the information flow for the MCData standalone session data response sent from the MCData client to the MCData server and from the MCData server to another MCData client.

Table 7.4.2.1.4-1: MCData standalone session data response

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID | M | The identity of the MCData user receiving data |
| MCData ID | M | The identity of the MCData user sent data |
| Conversation Identifier | M | Identifies the conversation |
| SDP answer | M | Media parameters selected |
| Establishment reason | M | Reason for establishment or rejection |

********************************************End of Changes***************************************