3GPP TSG-SA WG6 Meeting #32	S6-191616

Roma, Italy 8th – 12th July 2019	(revision of S6-191608_S6-191559_S6-191456_S6-191273)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.282 | CR | 0165 | rev | 4 | Current version: | 16.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Remote tear down of point-to-point IP connectivity |
| --- | --- |
| Source to WG: | UIC |
| Source to TSG: | S6 |
| Work item code: | eMONASTERY2 |  | Date: | 2019-07-12 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | TS 22.282 requires the teardown of IP connectivity between MCData user initiated by a user. This is missing in current 3GPP TS 23.282 specifiction. [R-5.5.2-003] The MCData Service shall enable an authorized person for an MCData user to authorize initiation of transport of IP data from that MCData user to specific destinations. This authorization may be preconfigured or may be provided by the authorized person when IP data transport to a new destination is initiated. Authorization may be revoked on demand by the authorized person. |
| Summary of change: | This CR aims to enable remote tear down of point-to-point IP connectivity between two users. |
| Consequences if not approved: | Not fulfilling the requirements of TS 22.282 clause 5.5.2 |
| Clauses affected: | New 7.14.2.1.5, New 7.14.2.1.6, New 7.14.2.4, Table A.3-2, 5.11 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: | None |

********************************************1st Change*******************************************

##### 7.14.2.1.5	Remote MCData IPcon point-to-point tear down

Table 7.14.2.1.X-1 describes the information flow of the remote MCData IPcon point-to-point tear down request sent from the remote MCData client to the MCData server and from the MCData server to the  asked target MCData client.

Table 7.14.2.1.5-1: MCData IPcon point-to-point data tear down request

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID remote | M | The MCData identity of the remote MCData client that requests another MCData user to tear down an IP connectivity point-to-point session. |
| Functional alias remote | O | The associated functional alias of the remote MCData user; |
| MCData ID asked | M | The MCData identity of the MCData client that is asked to tear down an IP connectivity point-to-point session. |
| Functional alias asked | O | The functional alias associated with the MCData identity of the MCData client that is asked to tear down an IP connectivity point-to-point session. |
| MCData ID targeted (NOTE) | O | The MCData identity of the MCData client that is the target to be tear down from the IP connectivity point-to-point session. |
| Functional alias targeted (NOTE) | O | The functional alias associated with the MC MCData identity of the MCData client that is the target to be tear down from the IP connectivity point to point session. |
| NOTE: Either the MCData ID or the functional alias of the targeted MCData user must be present. |

##### 7.14.2.1.6	MCData IPcon point-to-point tear down response

Table 7.14.2.1.X-1 describes the information content of the MCData IPcon point-to-point tear down response as answer to MCData remote IPcon point-to-point tear down request.

Table 7.14.2.1.6-1: MCData IPcon point-to-point tear down response

| Information element | Status | Description |
| --- | --- | --- |
| MCData ID asked | M | The MCData identity of the required MCData client. |
| MCData ID remote | M | The MCData identity of the remote MCData client. |
| Tear down status | M | The status information about the IP connectivity tear down status information |

********************************************2nd Change*******************************************

#### 7.14.2.4	MCData user remote initiated tear down point-to-point IP connectivity

##### 7.14.2.4.1	General

The MCData service shall support mechanisms that allow an MCData user to tear down remotely an established point-to-point IP connectivity. This encompasses the procedure of a remote MCData user that addresses the tear down of an IP connectivity between the requested MCData client and the destination MCData client.

##### 7.14.2.4.2	Procedure

The procedure in figure 7.14.2.4.2-1 describes the case where an authorised MCData user triggers remotely the tear down of a point-to-point IP connectivity connection between two other MCData users, the asked MCData user that tear down IP connectivity session to the targeted MCData user.

Pre-conditions:

-	MCData clients belong to the same MCData system.

-	MCData clients have IP connectivity capabilities.

-	The MCData server has subscribed to the MCData functional alias controlling server within the MC system for functional alias activation/de-activation updates.

-	Optionally, the MCData clients may have activated a functional alias to be used.

-	MCData client 1 is authorized to tear down point-to-point IP connectivity sessions.

Figure 7.14.2.4.2-1: Establishment of a remote point-to-point IP connectivity

1.	MCData client 1 would like to tear down a point-to-point IP connectivity between two other MCData clients, the asked MCData client 2 and the targeted MCData client 3.

2.	The MCData client 1 sends a MCData IPcon point-to-point tear down request towards the MCData server. The MCData IPcon point-to-point tear down request contains the MCData ID and/or the corresponding functional aliases of MCData client 2 and MCData client 3. MCData user at MCData client 1 may include its associated functional alias.

3.	MCData server checks whether MCData user at MCData client 1 is authorized to send MCData IPcon point-to-point tear down request and checks if the asked MCData client 2 allows the tear down of an IP connectivity point-to-point session.

4.	MCData server sends the MCData IPcon point-to-point tear down request towards the MCData client 2.

5.	MCData client 2 considers the provided targeted MCData id or targeted functional alias to tear down the point-to-point IP connectivity to MCData client 3 according to clause 7.2.2.5 or 7.2.2.6. The status of the IP connectivity tear down request shall be forwarded by MCData client 2 to remote MCData client 1.

6.	MCData client 2 sends MCData IPcon point-to-point tear down response to the MCData server encompassing the tear down IP connectivity status between MCData client 2 and MCData client 3.

7.	The MCData server forwards the MCData IPcon point-to-point tear down response to the remote MCData client 1.

******************************************4th Change*******************************************

# A.3	MCData user profile configuration data

Table A.3-2: MCData user profile configuration data (on network)

| Reference | Parameter description | MCData UE | MCData Server | Configuration management server | MCData user database |
| --- | --- | --- | --- | --- | --- |
| [R-5.1.5-001], [R-5.1.5-002], [R-5.10-001], [R-6.4.7-002], [R-6.8.1-008], [R-6.7.4-002] of 3GPP TS 22.280 [2] | List of on-network MCData groups for use by an MCData user |  |  |  |  |
|  | > MCData Group ID | Y | Y | Y | Y |
|  | > Application plane server identity information of group management server where group is defined |  |  |  |  |
|  | >> Server URI | Y | Y | Y | Y |
|  | > Application plane server identity information of identity management server which provides authorization for group (see NOTE 1) |  |  |  |  |
|  | >> Server URI | Y | Y | Y | Y |
| 3GPP TS 33.180 [13] | > KMSUri for security domain of group (see NOTE 2) | Y | Y | Y | Y |
|  | > Presentation priority of the group relative to other groups and users (see NOTE 3) | Y | N | Y | Y |
| Subclause 5.2.5 of 3GPP TS 23.280 [5] | List of groups user implicitly affiliates to after MCData service authorization for the user |  |  |  |  |
|  | > MCData Group ID | Y | Y | Y | Y |
| [R-6.4.2-006] of 3GPP TS 22.280 [2] | Authorisation of an MCData user to request a list of which MCData groups a user has affiliated to |  | Y | Y | Y |
| [R-6.4.6.1-002], [R-6.4.6.1-003] of 3GPP TS 22.280 [2] | Authorisation to change affiliated groups of other specified user(s) |  | Y | Y | Y |
| [R-6.4.6.2-001], [R-6.4.6.2-002] of 3GPP TS 22.280 [2] | Authorisation to recommend to specified user(s) to affiliate to specific group(s) |  | Y | Y | Y |
| [R-6.6.1-004] of 3GPP TS 22.280 [2] | Authorisation to perform regrouping | Y | Y | Y | Y |
| [R-6.7.2-001] of 3GPP TS 22.280 [2] | Presence status is available/not available to other users | Y | Y | Y | Y |
| [R-6.7.1-002], [R-6.7.2-002] of 3GPP TS 22.280 [2] | List of MCData users that MCData user is authorised to obtain presence of |  |  |  |  |
|  | > MCData IDs | Y | Y | Y | Y |
| [R-6.8.7.4.2-001], [R-6.8.7.4.2-002] of 3GPP TS 22.280 [2] | Authorisation of a user to cancel an emergency alert on any MCData UE of any user |  | Y | Y | Y |
| [R-6.13.4-001] of 3GPP TS 22.280 [2] | Authorisation for an MCData user to enable/disable an MCData user |  | Y | Y | Y |
| [R-6.13.4-003], [R-6.13.4-005], [R-6.13.4-006], [R-6.13.4-007] of 3GPP TS 22.280 [2] | Authorisation for an MCData user to (permanently /temporarily) enable/disable a UE |  | Y | Y | Y |
| [R-7.14-002], [R-7.14-003] of 3GPP TS 22.280 [2] | Authorization for manual switch to off-network while in on-network | Y | Y | Y | Y |
| [R-5.1.5-004] of 3GPP TS 22.280 [2] | Limitation of number of affiliations per user (N2) | N | Y | Y | Y |
| [R-6.4.6.1-001], [R-6.4.6.1-004] of 3GPP TS 22.280 [2] | List of MCData users whose selected groups are authorized to be remotely changed |  |  |  |  |
|  | > MCData ID | Y | Y | Y | Y |
| [R-6.3.1.2-007] of 3GPP TS 22.282 [3] and 3GPP TS 33.180 [13] | List of MCData users this MCData user is authorized to receive a one-to-one communication |  |  |  |  |
|  | > MCData ID | Y | Y | Y | Y |
|  | > KMSUri for security domain of MCData ID | Y | Y | Y | Y |
|  | Conversation management |  |  |  |  |
| [R-6.1.1.2-009] of 3GPP TS 22.282 [3]. | > List of MCData users to be sent message delivered disposition notifications in addition to the message sender | N | Y | Y | Y |
|  | >> MCData ID | N | Y | Y | Y |
| [R-6.1.1.2-009] of 3GPP TS 22.282 [3]. | > List of MCData users to be sent message read disposition notifications in addition to the message sender | N | Y | Y | Y |
|  | >> MCData ID | N | Y | Y | Y |
| 3GPP TS 23.283 [18] | Authorised to use LMR E2EE for interworking | Y | Y | Y | Y |
| 3GPP TS 23.283 [18] | > List of supported LMR technology types |  |  |  |  |
| 3GPP TS 23.283 [18] | >> LMR technology type (P25, TETRA etc.) | Y | N | Y | Y |
| 3GPP TS 23.283 [18] | >> URI of LMR key management functional entity (see NOTE 4 ) | Y | N | Y | Y |
| 3GPP TS 23.283 [18] | >> LMR specific identity (RSI for P25 or ITSI for TETRA) (see NOTE 5) | Y | N | Y | Y |
| 3GPP TS 23.283 [18] | >> LMR specific security information (see NOTE 5) | Y | N | Y | Y |
|  | List of servers used in the private and group communications |  |  |  |  |
|  | > MCData content server where the HTTP FD file is uploaded |  |  |  |  |
|  | >> Server URI | Y | Y | Y | Y |
|  | > MCData message store where the communication history stores |  |  |  |  |
|  | >> Server URI | Y | Y | Y | Y |
| Subclause 5.2.9 of 3GPP TS 23.280 [16] | List of partner MCData systems in which this profile is valid for use during migration |  |  |  |  |
| Subclause 5.2.9 of 3GPP TS 23.280 [16] | > Identity of partner MCData system | Y | Y | Y | Y |
| Subclause 10.1.1 of 3GPP TS 23.280 [16] | > Access information for partner MCData system (see NOTE 6) | Y |  | Y | Y |
| [R-5.9a-012] of 3GPP TS 22.280 [2] [R-5.9a-013] of 3GPP TS 22.280 [2] | Authorised to request information query of the association between active functional alias(es) and the MCData ID(s) |  | Y | Y | Y |
| [R-6.6.4.2-002a] and [R-6.6.4.2-002b] of 3GPP TS 22.280 [2] | List of groups the client affiliates/de-affiliates when criteria is met |  |  |  |  |
|  | > MCData Group ID | Y | Y | Y | Y |
|  | >> Criteria for affiliation (see NOTE 7) | Y | Y | Y | Y |
|  | >> Criteria for de-affiliation (see NOTE 7) | Y | Y | Y | Y |
|  | >> Manual de-affiliation is not allowed if criteria for affiliation are met | Y | Y | Y | Y |
| [R-6.6.4.2-002] of 3GPP TS 22.280 [2] | List of groups the client affiliates after receiving an emergency alert |  |  |  |  |
|  | > MCData Group ID | Y | Y | Y | Y |
|  | >> Manual de-affiliation is not allowed if criteria for affiliation are met | Y | Y | Y | Y |
|  | List of functional alias(es) of the MCData user |  |  |  |  |
| [R-5.9a-005] of 3GPP TS 22.280 [2] | > Functional alias | Y | Y | Y | Y |
| [R-5.9a-018] of 3GPP TS 22.280 [2] | >> Criteria for automatic activation by the MCData server (see NOTE 8) | N | Y | Y | Y |
| [R-5.9a-017], [R-5.9a-018] of 3GPP TS 22.280 [2] | >> Criteria for automatic de-activation by the MCData server (see NOTE 8) | N | Y | Y | Y |
|  | List of functional alias(es) of the MCData user |  |  |  |  |
| [R-5.9a-005] of 3GPP TS 22.280 [2] | > Functional alias | Y | Y | Y |  |
| [R-5.9a-019] of 3GPP TS 22.280 [2] | >> Location criteria for activation | Y |  | Y | Y |
| [R-5.9a-019] of 3GPP TS 22.280 [2] | >> Location criteria for de-activation | Y |  | Y | Y |
|  | >> Manual de-activation is not allowed if the location criteria are met | Y |  | Y | Y |
| [R-5.9a-012] of 3GPP TS 22.280 [2] | Authorised to take over a functional alias from another MCData user |  | Y | Y | Y |
|  | Authorised to participate in an IP connectivity session | Y | Y | Y | Y |
| [R-5.5.2-003], [R-5.5.2-004] 3GPP TS 22.282 [3] | >List of MCData users which can be included in IP connectivity sessions. |  |  |  |  |
|  | >> MCData ID | Y | Y | Y | Y |
| 3GPP TS 33.180 [13] | >> KMSUri for security domain of the MCData ID | Y | Y | Y | Y |
|  | >>List of associated data host IP information |  |  |  |  |
|  | >>>IP information (see NOTE 9) | Y | Y | Y | Y |
| [R-5.5.2-003] 3GPP TS 22.282 [3] | Authorised to tear down point-to-point IP connectivity sessions | N | Y | Y | Y |
|  | >List of MCData users which can be addressed in a remote initiated IP connectivity session tear down; |  |  |  |  |
|  | >> MCData ID | N | Y | Y | Y |
| NOTE 1: If this parameter is not configured, authorization to use the group shall be obtained from the identity management server identified in the initial MC service UE configuration data (on-network) configured in table A.6-1 of 3GPP TS 23.280 [5]. NOTE 2: If this parameter is absent, the KMSUri shall be that identified in the initial MC service UE configuration data (on-network) configured in table A.6-1 of 3GPP TS 23.280 [5]. NOTE 3: The use of this parameter by the MCData UE is outside the scope of the present document. NOTE 4: The LMR key management functional entity is part of the LMR system and is outside the scope of the present document. NOTE 5: This is an LMR specific parameter with no meaning within MC services. NOTE 6: Access information for each partner MCData system comprises the list of information required for initial UE configuration to access an MCData system, as defined in table A.6-1 of 3GPP TS 23.280 [16] NOTE 7: The criteria may consist conditions such as the location of the MCData user or the active functional alias of the MCData user. NOTE 8: The criteria may consist of conditions such as MCData user location or time. NOTE 9: IP information may contain IP addresses, corresponding subnet masks, gateway and DNS settings. |

*********************************************5th Change******************************************

## 5.11	IP connectivity (IPcon) capability

IP connectivity service enables the exchange of IP Data using MCData transport service and provides the transport of IP Data for e.g. data hosts, servers, etc. that do not have mission critical communication capabilities. The exchange of IP Data is not limited in a transaction.

Figure 5.11-1: IP connectivity model

The corresponding MCData client enables bidirectional IP Data communication with the support of the IP connectivity service and thus forms the gateway to data hosts or servers. Therefore, the IP connectivity MCData client requests the MCData transport service with the associated QoS requirement and communication priority.

An authorised MCData client supporting IP connectivity capabilities is able to bar incoming IP connectivity requests either on demand or by providing a list of excluded origins identified by the MCData ID and, if available, by the functional alias.

For IP connectivity, the MCData server may support following limitation to exchange IP Data:

-	limit the total data volume between the authorized MCData clients, divided by transmission and reception;

-	max time limit, e.g. total minutes or allow exchange between predefined start and end time.

IP connectivity MCData service supports MCData transport services for one-to-one and group communication.

The IP address allocation necessary for user-IP connectivity MCData transport service is independent to the IP address allocation of the individual data hosts attached with the MCData client supporting IP connectivity capabilities. The required IP address pools for the user-IP connectivity MCData service are managed by the IP connectivity MCData transport service.

Editor's note:	The remote initiation of IP connectivity service is FFS.

Editor's note:	The control of QoS based on per packet priority is FFS.

Editor's note:	The impact of IP connectivity services on interworking is FFS.

******************************************End of Changes*****************************************