3GPP TSG-SA WG6 Meeting #32	S6-191522

Rome, Italy, 8th July – 12th July, 2019	(revision of S6-191314)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.282 | CR | 0169 | rev | 1 | Current version: | 16.3.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Fix omission of location services in MCData |
| --- | --- |
| Source to WG: | AT&T |
| Source to TSG: | S6 |
| Work item code: | eMCData2 |  | Date: | 2019-06-26 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Location services functionality and interfaces for MC Services have been defined in the Common functional architecture specification 23.280. For MCVideo, location services functionality was explicitly added to 23.281 in Rel-14, but in case of MCData, the addition appears to have been omitted from 23.282. |
| Summary of change: | Add explicit location services functionality to MCData, based on the functionality described in the Common functional architecture. The text added to 23.282 via this CR closely follows the similar text used in 23.281 for location by MCVideo. |
| Consequences if not approved: | Absence of proper location information handling by MCData, may seriously limit the data transmission/reception functionality, making it impossible to have location specific transmissions. SDS service requires support for inclusion of location data. Location information can also be used to know when to turn on/off MBMS transmission, making location support an essential functionality. Alias processing and alerts also take advantage of location. It is clear that without location support the MCData functionality will be seriously restricted. Current ongoing Stage 3 work in CT1 would also be negatively impacted. |
| Clauses affected: | 7.15 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

## 7.15	Location information (on-network)

The MCData system makes use of all of the procedures for location management as specified in 3GPP TS 23.280 [5], utilising the CSC-14 reference point between the location management client and location management server and the CSC-15 reference point between the MCData server and location management server.

-	The MC service client is the MCData client;

-	The MC service server is the MCData server;

-	The MC service group is the MCData group;

-	The MC service ID is the MCData ID; and

-	The MC service group ID is the MCData group ID.

* * * * End of Changes * * * *