3GPP TSG-SA WG6 Meeting #32	S6-191538

Roma, Italy 8th – 12th July 2019	(revision of S6-191470)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0001 | rev | 2 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Remove EN GeoIDs |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S6 |
| Work item code: | V2XAPP |  | Date: | 2019-07-01 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | A definition of geographical area identities has been added to Section 8.5. The editor’s note is not needed anymore. |
| Summary of change: | Remove editor’s note “The definition of geographical area identifiers is FFS” as a definition has already been added to Section 8.5. 8.5 Geographical area identity (GEO ID) The V2X service provider defined identity of a geographical area. The GEO ID supports different representations of geographical area (e.g. geo-fence, tile identifiers). The VAE server maintains the mapping of the GEO ID with the location corresponding to one or more V2X UE IDs. The GEO ID may support the format of a URI. |
| Consequences if not approved: | Creates confusion for stage 3 when Geo IDs are already defined in the document. |
| Clauses affected: | 9.3.2.1 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

### 9.3.2	Information flows

#### 9.3.2.1	Subscription request

Table 9.3.2.1-1 describes the information flow for a VAE client to subscribe to a geographical area at the VAE server.

Table 9.3.2.1-1: Subscription request

| Information element | Status | Description |
| --- | --- | --- |
| V2X UE ID | M | Identifier of the V2X UE |
| GEO ID | M | Geographical area identifier (e.g. subscription URI, tile identifier, geo-fence tile identifier) |

* * * End of Changes * * * *