3GPP TSG-SA WG6 Meeting #32	S6-191539

Roma, Italy 8th – 12th July 2019	(revision of S6-191472)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0002 | rev | 2 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Functionalities with SA2 dependency |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S6 |
| Work item code: | V2XAPP |  | Date: | 2019-07-01 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The procedures on service negotiation with the underlying 3GPP network are in informative section (annex B1) due to dependencies with SA2. |
| Summary of change: | Proposal to resolve dependencies with SA2. The procedure and information flows are moved to new Section 9.x with reference to 23.286 message names and clauses. The information flows not supported by 23.286 remain in Annex B1. |
| Consequences if not approved: | The current procedures remain in informative section and the dependencies to SA2 are not resolved. |
| Clauses affected: | B1, 9.x (new), 9.x.1 (new), 9.x.2 (new), 9.x.2.1 (new), 9.x.2.2 (new), 9.x.2.3 (new), 9.x.2.4 (new), 9.x.2.5 (new), 9.x.2.6 (new), 9.x.2.7 (new), 9.x.2.8 (new), 9.x.3 (new), 9.x.4 (new). |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

## 9.x	Service negotiation with underlying 3GPP network

### 9.x.1	General

This subclause describes the procedures for the VAE server to provide service requirements to the 3GPP network system. The Service Capability Exposure Function (SCEF) can be used for this purpose. As described in 3GPP TS 23.682 [8], the SCEF provides a means to expose the services and capabilities provided by 3GPP network interfaces and provides a means for the discovery of the exposed services and capabilities.

### 9.x.2	Information flows

#### 9.x.2.1	On-demand QoS request

The information flow On-demand QoS request from VAE server (acting as SCS/AS) to SCEF over T8 reference point is specified in clause 5.11 (when setting up a session with required QoS) in 3GPP TS 23.682 [8].

#### 9.x.2.2	On-demand QoS response

The information flow On-demand QoS response from SCEF to VAE server (acting as SCS/AS) over T8 reference point is specified in clause 5.11 in 3GPP TS 23.682 [8].

#### 9.x.2.3	Background data transfer request

The information flow Background data transfer request from VAE server (acting as SCS/AS) to SCEF over T8 reference point is specified in clause 5.9 (resource management for background data transfer) in 3GPP TS 23.682 [8].

#### 9.x.2.4	Background data transfer response

The information flow Background data transfer response from SCEF to VAE server (acting as SCS/AS) over T8 reference point is specified in clause 5.9 in 3GPP TS 23.682 [8].

#### 9.x.2.5	Network Status Request

The information flow Network Status Request from VAE server (acting as SCS/AS) to SCEF over T8 reference point is specified in clause 5.8 in 3GPP TS 23.682 [8].

#### 9.x.2.6	Network Status Response

The information flow Network Status Response from SCEF to VAE server (acting as SCS/AS) over T8 reference point is specified in clause 5.8 in 3GPP TS 23.682 [8].

#### 9.x.2.7	Network Status Report

The information flow Network Status Report from SCEF to VAE server (acting as SCS/AS) over T8 reference point is specified in clause 5.8 in 3GPP TS 23.682 [8].

#### 9.x.2.8	Network Status Acknowledgment

The information flow Network Status Acknowledgment from VAE server (acting as SCS/AS) to SCEF over T8 reference point is specified in clause 5.8 in 3GPP TS 23.682 [8].

### 9.x.3	Communication of service requirements from the VAE server

The procedure uses the APIs defined in subclauses 5.8, 5.9 and 5.11 in 3GPP TS 23.682 [8] for setting up an AS session with required QoS procedure. This procedure defines the information elements that need to be exchanged between the VAE server (acting as SCS/AS) and the SCEF function during service negotiation.

### 9.x.4	Notification generation by the SCEF function

The procedure notification generation by the SCEF function in response to the service requirements from the VAE server. The SCEF function notifies the VAE server if the service requirements can be satisfied. This procedure uses the APIs defined in subclause 5.8 in 3GPP TS 23.682 [8] for informing about potential network issues.

* * * Next Change * * * *

Annex B (informative):
Functionalities with SA2 dependency

## B.1	Service negotiation with underlying 3GPP network

### B.1.1	General

The following information flows for service negotiation with the 3GPP network are not supported in 3GPP TS 23.682 [8].

### B.1.1	Information flows

#### B.1.1.1	Supporting information request

Table B.1.1.1-1 describes the information flow for a VAE server to provide the network with supporting information for service negotitation with the 3GPP network.

Table B.1.1.1-1: Supporting information request

| Information element | Status | Description |
| --- | --- | --- |
| Supporting Information | O | Indicating supporting information by the VAE server to increase the network awareness related to the service. Example of supporting information is planned/expected UE trajectory, which can be provided in the form of waypoints (GPS coordinates) and associated timestamps. |

Editor's note:	Reference to the appropriate SA2 specification is needed and corresponding information flow table can be removed.

Editor's note:	Need to verify with SA2 specifications on the exact support provided to this feature.

#### B.1.1.2	Supporting information  response

Table B.1.1.2-1 describes the information flow for a network to provide a response associated to a supporting information request.

Table B.1.1.2-1: Supporting information response

| Information element | Status | Description |
| --- | --- | --- |
| Result | M | Response from the network if supporting information is supported by the 3GPP network. |

Editor's note:	Reference to the appropriate SA2 specification is needed and corresponding information flow table can be removed.

* * * End of Changes * * * *