3GPP TSG-SA WG6 Meeting #32	S6-191473

Roma, Italy 8th – 12th July 2019	(revision of S6-191370)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0004 | rev | 1 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Update to network QoS and situation monitoring aligned with SA2 |
| --- | --- |
| Source to WG: | Huawei, Hisilicon |
| Source to TSG: | S6 |
| Work item code: | V2XAPP |  | Date: | 2019-06-24 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | In Annex B.2, the procedure for network QoS and situation monitoring is required to be aligned with the latest SA2 specification on SCEF in TS 23.682. |
| Summary of change: | Moved the procedure in Annex B.2 to normative clause and modified the procedure as supported by TS 23.682. |
| Consequences if not approved: | The procedure for network QoS and situation monitoring with the underlying network will be incomplete. |
| Clauses affected: | B.2, 9.13 (new), 9.13.1 (new), 9.13.2 (new), 9.13.2.1 (new), 9.13.2.2 (new), 9.13.2.3 (new), 9.13.3 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

## B.2	void

* * * Next Change * * * *

## 9.13	Network situation and QoS monitoring and reporting

### 9.13.1	General

The VAE server supports monitoring of 3GPP systems' network situation for V2X services. The VAE server receives and processes access network-related monitoring events/reports from SCEF (EPS entity of the 3GPP network system) as specified in 3GPP TS 23.682 [8]. The monitoring events/report may also include RAN-related resource/traffic situation information and QoS related notifications per UE or group of UEs. The VAE server initiates monitoring of the QoS for single or aggregately for groups of vehicles (supporting a V2X service and being in proximity) having ongoing sessions. The information from V2X UE related to monitoring events (e.g. location, groups, resource usage) can be available at the VAE server using the network resource management and location management services of the SEAL.

### 9.13.2	Information flows

#### 9.13.2.1	Monitoring request

The information flow monitoring request from VAE server (acting as SCS/AS) to SCEF over T8 reference point is specified in clause 5.6 and clause 5.8 (when monitoring request comprises Network Status Request) in 3GPP TS 23.682 [8].

#### 9.13.2.2	Monitoring response

The information flow monitoring response from SCEF to VAE server (acting as SCS/AS) over T8 reference point is specified in clause 5.6 and clause 5.8 (when monitoring request comprises Network Status Response) in 3GPP TS 23.682 [8].

#### 9.13.2.3	Monitoring report

The information flow monitoring report from the SCEF to the VAE server over T8 reference point is specified in clause 5.6, clause 5.8 (when monitoring report comprises Network Status Information Report) and clause 5.11 (when monitoring report comprises notification of QoS/bearer level events) in 3GPP TS 23.682 [8].

### 9.13.3	Procedure

The VAE server acts as SCS/AS and initiates the procedure for monitoring with the SCEF as specified in the clause 5.6 and clause 5.8 in 3GPP TS 23.682 [8] by including the V2X application information corresponding to one or many V2X UEs.

The SCEF provides the monitoring reports (including the RAN related network situation information and QoS notification information for the corresponding V2X application, V2X UE or group of V2X UEs) to the VAE server as specified in the clause 5.6, clause 5.8 and clause 5.11 in 3GPP TS 23.682 [8].