3GPP TSG-SA WG6 Meeting #32	S6-191540

Roma, Italy 8th – 12th July 2019	(revision of S6-191371, 1475)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0005 | rev | 2 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Dynamic group API |
| --- | --- |
| Source to WG: | Huawei, Hisilicon |
| Source to TSG: | S6 |
| Work item code: | V2XAPP |  | Date: | 2019-06-24 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The API definition for Dynamic group is missing while the procedure for configure dynamic group is specified. |
| Summary of change: | Add the API operation definition for configure dynamic group |
| Consequences if not approved: | The configure dynamic group interaction between V2X application specific server and VAE server cannot be completed. |
| Clauses affected: | 9.12.2.2 (new), 10.2.1, 10.2.5 (new), 10.2.5.1 (new), 10.2.5.2 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

#### 9.12.2.2	Configure dynamic group

Table 9.12.2.2-1 describes the information flow configure dynamic group from the V2X application specific sever to the VAE server and from the V2X application specific server to the VAE client.

Table 9.12.2.2-1: Configure dynamic group

| Information element | Status | Description |
| --- | --- | --- |
| Dynamic group information | M | Group information including dynamic group ID, group definition, group leader ID |

* * * Next Change * * * *

### 10.2.1	General

Table 10.2.1-1 illustrates the VAE server APIs.

Table 10.2.1-1: List of VAE server APIs

| API Name | API Operations | Known Consumer(s) | Communication Type |
| --- | --- | --- | --- |
| VAE_V2X_Message_Delivery API | V2X_Message_Delivery | V2X application specific server | Request/ Response |
| VAE_File_Distribution API | Initiate_File_Distribution | V2X application specific server | Request/ Response |
| VAE_V2X_Application_Requirement API | V2X_Application_Requirement | V2X application specific server | Subscribe/notify |
| VAE_V2X_Dynamic_Group API | Configure_Dynamic_Group | V2X application specific server | Request/Response |

Editor's note:	Whether the VAE_V2X_Dynamic_Group API is to be moved to SEAL is FFS.

* * * Next Change * * * *

### 10.2.5	VAE_V2X_Dynamic_Group API

#### 10.2.5.1	General

API description: This API enables the V2X application specific server to communicate with the VAE server to configure dynamic group information.

#### 10.2.5.2	Configure_Dynamic_Group operation

API operation name: Configure_Dynamic_Group

Description: Configures the dynamic group information at the VAE server.

Known Consumers: V2X application specific server.

Inputs: Refer subclause 9.12.2.2.

Outputs: None.

See subclause 9.12.3 for the details of usage of this API operation.