3GPP TSG-SA WG6 Meeting #32	S6-191474

Roma, Italy 8th – 12th July 2019	(revision of S6-191372)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0006 | rev | 1 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Correction to push layer-2 group ID mapping information flow |
| --- | --- |
| Source to WG: | Huawei, Hisilicon |
| Source to TSG: | S6 |
| Work item code: | V2XAPP |  | Date: | 2019-06-24 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The information flow descriptions for push layer-2 group ID mapping is incorrect. |
| Summary of change: | The push layer-2 group ID mapping information flow is specified between VAE server and VAE client and between VAE clients. |
| Consequences if not approved: | Push layer-2 group ID mapping information flow cannot be implemented by stage 3 groups. |
| Clauses affected: | 9.12.2.1 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

#### 9.12.2.1	Push Layer-2 group ID mapping

Table 9.12.2.1-1 describes the information flow push layer-2 group ID mapping from the VAE server to the VAE client and between the VAE clients.

Table 9.12.2.1-1: Push Layer-2 group ID mapping

| Information element | Status | Description |
| --- | --- | --- |
| Dynamic group information | M | Group information including dynamic group ID, group definition, group leader ID |
| ProSe Layer-2 Group ID | M | ProSe Layer-2 Group ID corresponding to the dynamic group information |

Editor's note:	Whether the procedures and information flows for dynamic group management are to be moved to SEAL is FFS.