3GPP TSG-SA WG6 Meeting #32	S6-191572

Roma, Italy 8th – 12th July 2019	(revision of S6-191393, 1471)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0007 | rev | 2 | Current version: | 16.0.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Corrections on notifications for network monitoring procedure |
| --- | --- |
| Source to WG: | Huawei, Hisilicon |
| Source to TSG: | S6 |
| Work item code: | V2XAPP |  | Date: | 2019-06-20 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | 1) In clause 9.7.3.2, currently the UE subscribes to all types of network monitoring event. However, a UE may be only interested in some of those information. 2) The VAE server knows the service requirements and the network monitoring information, which will enable the VAE server to hide the real network conditions and inform the VAE client the processed information e.g., e.g. uplink or downlink link degradations, congestions, overload. |
| Summary of change: | Update the information flows in 9.7.2 Update the procedure description in 9.7.3.2 and 9.7.4.2 |
| Consequences if not approved: | Incorrect implementation of the monitoring information notification. |
| Clauses affected: | 9.7.2.1, 9.7.2.3, 9.7.4.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

*********************** 1st change *******************

#### 9.7.2.1	Network monitoring information subscription request

Table 9.7.2.1-1 describes the information flow network monitoring information subscription request from the VAE client to the VAE server.

Table 9.7.2.1-1: Network monitoring information subscription request

| Information element | Status | Description |
| --- | --- | --- |
| V2X UE ID | M | Identity of the V2X UE subscribing for the network monitoring information |
| Subscription event | M | Identify one or multiple network monitoring events (e.g. uplink degradation, congestion, overload, coverage) |
| Triggering criteria | M | Identify when the VAE server will send the monitoring reports to the VAE client. |

#### 9.7.2.3	Network monitoring information notification

Table 9.7.2.3-1 describes the information flow network monitoring information notification from the VAE server to the VAE client.

Table 9.7.2.3-1: Network monitoring information notification

| Information element | Status | Description |
| --- | --- | --- |
| V2X UE ID | M | Identity of the V2X UE |
| Network monitoring information | M | This includes information on network status for the triggering criteria, and may include the following parameters: - Uplink quality level - Congestion level - Overload level - Geographical Area (cell area or TA for which the monitoring applies) - Time Validity (the period for which the monitoring applies) - Coverage level and bearer level events (optionally, for MBMS) |

*********************** Next change *******************

#### 9.7.4.2	Procedure

Figure 9.7.4.2-1 illustrates the procedure where the VAE server sends notification of the network monitoring information to the V2X UEs.

Pre-conditions:

1.	The VAE server acting as a SCS/AS is configured with the SCEF information and is authorized to exchange information with the SCEF as specified in subclause 4.9 in 3GPP TS 23.682 [8];

2.	The V2X UE1 and V2X UE2 have subscribed for the network monitoring information at the VAE server.

Figure 9.7.4.2-1: Notifications for network monitoring information

1.	The VAE server communicates with the SCEF to receive network monitoring information as per the procedure in subclause 4.9 of 3GPP TS .23.682 [8].

2.	The monitoring information (e.g. uplink or downlink link degradations, congestions, overload) available at the VAE server about the on-going V2V session(s) is based on the original network monitoring information provided by the SCEF in step 1.

3.	The monitoring information is sent to the subscribed V2X UEs via network monitoring information notification.