3GPP TSG-SA WG6 Meeting #35	S6-200168

Hyderabad, India, 13rd - 17th Jan 2020	(revision of S6-200075)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0014 | rev | 1 | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Add VAE service continuity API |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S6 |
| Work item code: | V2XAPP |  | Date: | 2020-01-14 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The VAE-E interaction between VAE servers for service continuity is not captured in the VAE server API in subclause 10.2.1. |
| Summary of change: | Update subclause 10.2.1 with VAE_ServiceContinuity API; Add new subclause under subclause 10.2 with VAE_ServiceContinuity API definition. |
| Consequences if not approved: | The API for VAE service continuity is not complete; and it may create confusion in stage 3 protocol realization. |
| Clauses affected: | 10.2.1, 10.2.x (new), 10.2.x.1 (new), 10.2.x.2 (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

### 10.2.1	General

Table 10.2.1-1 illustrates the VAE server APIs.

Table 10.2.1-1: List of VAE server APIs

| API Name | API Operations | Known Consumer(s) | Communication Type |
| --- | --- | --- | --- |
| VAE_MessageDelivery API | Deliver_DL_Message | V2X application specific server | Request/ Response |
|  | Deliver_UL_Message | V2X application specific server | Subscribe/notify |
| VAE_FileDistribution API | Distribute_File | V2X application specific server | Request/ Response |
| VAE_ApplicationRequirement API | Reserve_NetworkResource | V2X application specific server | Subscribe/notify |
| VAE_DynamicGroup API | Configure_DynamicGroup | V2X application specific server | Request/Response |
| VAE_ServiceContinuity API | Query_ServiceContinuity | VAE server | Request/Response |

Editor's note:	Whether the VAE_DynamicGroup API is to be moved to SEAL is FFS.

* * * Next Change * * * *

### 10.2.x	VAE_ServiceContinuity API

#### 10.2.x.1	General

API description: This API enables the VAE server to query whether the target VAE server can serve the GEO ID and V2X Service ID for service continuity.

#### 10.2.x.2	Query_ServiceContinuity operation

API operation name: Query_ServiceContinuity

Description: Query the service continuity information.

Known Consumers: VAE server.

Inputs: Refer subclause 9.10.2.1.

Outputs: Refer subclause 9.10.2.2.

See subclause 9.10.3 for the details of usage of this API operation.

* * * End of Changes * * * *