3GPP TSG-SA WG6 Meeting #35	S6-200170

Hyderabad, India, 13rd - 17th Jan 2020	(revision of S6-200077)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0015 | rev | 1 | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Correct Group Management procedure |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S6 |
| Work item code: | V2XAPP |  | Date: | 2020-01-04 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | The existing procedure cannot let the V2X application specific server be aware of the result of group member join/leave since there may be UEs not reachable by PC5. In addition, the configure dynamic group in subclause 9.12.2.2 mentions the communication between the VAE client and V2X application specific server, this is incorrect. And the corresponding configure dynamic group response is missing. |
| Summary of change: | 1. clause 9.12.2.2 is updated with end point information. 2. add configure dynamic group response and notification in information flow. 3. change the procedure in clause 9.12.3.2 with configure dynamic group response and add the procedure in new subclause for notification. 4. update the API description in clause 10.2. |
| Consequences if not approved: | Incorrect information left in 9.12.2.2; The V2X application specific server may wrongly believe all UEs in the requested group are pertained in the group. |
| Clauses affected: | 9.12.2.2, 9.12.2.x (new), 9.12.2.y (new), 9.12.2.z (new), 9.12.3.2, 9.12.X (new), 9.12.X.1 (new), 9.12.X.2 (new), 10.2.1, 10.2.5.2, 10.2.5.x (new) |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

#### 9.12.2.2	Configure dynamic group request

Table 9.12.2.2-1 describes the information flow for configure dynamic group request from the V2X application specific sever to the VAE server.

Table 9.12.2.2-1: Configure dynamic group request

| Information element | Status | Description |
| --- | --- | --- |
| Dynamic group information | M | Group information including dynamic group ID, group definition, group leader ID |
| Endpoint information | M | End point information to which the configure dynamic group notification has to be sent |

* * * Next Change * * * *

#### 9.12.2.x	Configure dynamic group response

Table 9.12.2.x-1 describes the information flow for configure dynamic group response from the VAE server to the V2X application specific sever.

Table 9.12.2.x-1: Configure dynamic group response

| Information element | Status | Description |
| --- | --- | --- |
| Result | M | Result from the VAE server in response to the configure dynamic group request. |

* * * Next Change * * * *

#### 9.12.2.y	Configure dynamic group notification

Table 9.12.2.y-1 describes the information flow for configure dynamic group notification from the VAE server to the V2X application specific sever.

Table 9.12.2.y-1: Configure dynamic group notification

| Information element | Status | Description |
| --- | --- | --- |
| Dynamic group information | M | Group information including dynamic group ID, UE ID (joined or left UE(s)) |

* * * Next Change * * * *

#### 9.12.2.z	Identity list notification

Table 9.12.2.z-1 describes the information flow identity list notification from from the VAE client to the VAE server.

Table 9.12.2.z-1: Identity list notification

| Information element | Status | Description |
| --- | --- | --- |
| Dynamic group information | M | Group information including dynamic group ID, UE ID (joined or left UE(s)) |

* * * Next Change * * * *

#### 9.12.3.2	Procedure

The procedure for on-network dynamic group creation is illustrated in figure 9.12.3.2-1.

Pre-condition:

1.	V2X application dynamic group is defined at the V2X application specific server with V2X UE assigned as dynamic group leader.

2.	VAE server has a pool of the ProSe Layer-2 Group IDs that can be assigned to dynamic groups

Figure 9.12.3.2-1: On-network dynamic group creation

1.	The V2X application specific server requests the VAE server to configure dynamic group corresponding to the dynamic group information (e.g. dynamic group ID, group definition, group leader).

2.	To enable PC5 communication, the VAE server assigns ProSe Layer-2 Group ID to the received dynamic group information from the available ProSe Layer-2 Group ID pool.

3.	The VAE server responds to the V2X application specific server for the request to configure dynamic group.

4.	The VAE server triggers a push request including ProSe Layer-2 Group ID corresponding to the dynamic group information to the VAE client.

5.	The VAE client stores the received PC5 communication parameters corresponding to the dynamic group information received from the VAE server.

NOTE 1:	The VAE client may further announce the dynamic group information including the corresponding ProSe Layer-2 Group ID to the other VAE clients within the PC5 communication proximity on a PC5 channel dedicated for V5-AE communications, enabling more V2X UEs to join the dynamic group.

NOTE 2:	When there is loss of connectivity with the network by the V2X UEs, service continuity is ensured by the V2X UEs switching to PC5 communication using the VAE server assigned ProSe Layer-2 Group ID corresponding to the dynamic group formation.

### 9.12.X	On-network dynamic group notification

#### 9.12.X.1	General

Once the on-network dynamic group is created as defined in subclause 9.12.3, the VAE client notifies the VAE server about changes in the group (i.e. UE joins or leaves the group) and finally the V2X application specific server is notified with such information.

#### 9.12.X.2	Procedure

The procedure for on-network dynamic group notification is illustrated in figure 9.12.X.2-1.

Pre-condition:

1.	V2X application dynamic group is created as defined in subclause 9.12.3.

Figure 9.12.X.2-1: On-network dynamic group notification

1.	The VAE client sends identity list notification to the VAE server about group member changes.

2.	Upon receipt of the identity list notification from the VAE client, the VAE server further notifies the V2X application specific server about the newly joined or left group member(s).

* * * Next Change * * * *

### 10.2.1	General

Table 10.2.1-1 illustrates the VAE server APIs.

Table 10.2.1-1: List of VAE server APIs

| API Name | API Operations | Known Consumer(s) | Communication Type |
| --- | --- | --- | --- |
| VAE_ MessageDelivery API | Deliver_DL_Message | V2X application specific server | Request/ Response |
|  | Deliver_UL_Message | V2X application specific server | Subscribe/notify |
| VAE_FileDistribution API | Distribute_File | V2X application specific server | Request/ Response |
| VAE_ ApplicationRequirement API | Reserve_NetworkResource | V2X application specific server | Subscribe/notify |
| VAE_ DynamicGroup API | Configure_DynamicGroup | V2X application specific server | Request/Response |
|  | Notify_DynamicGroup |  |  |

Editor's note:	Whether the VAE_ DynamicGroup API is to be moved to SEAL is FFS.

* * * Next Change * * * *

#### 10.2.5.2	Configure_DynamicGroup operation

API operation name: Configure_DynamicGroup

Description: Configures the dynamic group information at the VAE server.

Known Consumers: V2X application specific server.

Inputs: Refer subclause 9.12.2.2.

Outputs: Refer subclause 9.12.2.x.

See subclause 9.12.3 for the details of usage of this API operation.

* * * Next Change * * * *

#### 10.2.5.x	Notify_DynamicGroup operation

API operation name: Notify_DynamicGroup

Description: Notify the dynamic group information (i.e. group member joins or leaves) at the VAE server.

Known Consumers: V2X application specific server.

Inputs: Refer subclause 9.12.2.y.

Outputs: None.

See subclause 9.12.X for the details of usage of this API operation.

* * * End of Changes * * * *