3GPP TSG-SA WG6 Meeting #35	S6-200073

Hyderabad, India, 13rd - 17th Jan 2020	(revision of S6-20xxxx)

| CR-Form-v11.2 |
| --- |
| CHANGE REQUEST |
|  | 23.434 | CR | 0017 | rev | - | Current version: | 16.2.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME | X | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Correct dynamic MBMS bearer establishment |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S6 |
| Work item code: | SEAL |  | Date: | 2020-01-04 |
| Category: | F |  | Release: | Rel-16 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) |
| Reason for change: | Step 6 & 7 are marked on wrong entity in Figure 14.3.4.3.2-1. |
| Summary of change: | Put Step 6 & 7 on VAL UE instead of NRM server. |
| Consequences if not approved: | Incorrection information remains. |
| Clauses affected: | 14.3.4.3.2 |
|  | Y | N |  |  |
| Other specs |  | X | Other core specifications | TS/TR ... CR ... |
| affected: |  | X | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | X | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |

* * * First Change * * * *

##### 14.3.4.3.2	Procedure

Figure 14.3.4.3.2-1 illustrates the use of dynamic MBMS bearer establishment.

Figure 14.3.4.3.2-1: Use of dynamic MBMS bearer establishment

1.	A VAL service group communication session is established.

2.	The downlink data is sent by unicast delivery.

3.	The VAL server sends MBMS bearers request to the NRM server.

4.	The NRM server establishes the MBMS bearer(s) for the VAL service group communication session according to the procedures defined in 3GPP TS 23.468 [16]. Service description associated with the MBMS bearer(s) is returned from the BM-SC.

5.	The NRM server provides service description information associated with the MBMS bearer to the UE. The VAL UE obtains the TMGI from the announcement message. This message may be sent on an application level control signalling bearer.

6.	The VAL UE starts monitoring data over MBMS associated with the TMGI, while in the service area associated with the TMGI.

7.	The VAL UE detects that it is able to receive data over MBMS associated with the TMGI.

8.	The NRM client notifies the NRM server the MBMS listening status associated to the monitored TMGI, (e.g. that it is successfully receiving the TMGI). The NRM client may also notify the MBMS reception quality level of the TMGI.

9.	The NRM server provides an MBMS bearer response to the VAL server with the dynamic MBMS bearer(s) information. The VAL server stops sending VAL service communication data over unicast way to the VAL client.

NOTE:	The MBMS reception quality level may be used by the NRM server to make an efficient decision to switch again to a unicast transmission or to take measures to prepare such a switch (e.g. when the quality level indicates that the reception quality of the MBMS bearer is decreasing or reaching an insufficient quality level for the reception of VAL services).

10.	A VAL service group communication session via dynamic MBMS bearer(s) is established.

11.	The VAL server sends the downlink VAL service communication for the VAL service group communication session over the MBMS.

* * * End of Changes * * * *