3GPP TSG-SA WG6 Meeting #39-bis-e	S6-201733r1

e-meeting, 12th – 20th October 2020	(revision of S6-20xxxx)

Source:	InterDigital

Title:	Update to EEC executed application context relocation

Spec:	3GPP TS 23.558 v1.0.0

Agenda item:	7.6

Document for:	Approval

Contact:	Atle Monrad <atle.monrad@interdigital.com>

1. Introduction

As per 8.8.2.3 step 3, the EEC:

- discovers the T-EES per clause 8.3

- selects T-EES

- discovers T-EAS querying T-EES per clause 8.5.2.

- Step 3 on figure needs to be updated

Step 3 on the figure does not match Step 3 in the procedure.

Figure shows T-EAS discovery from the S-EES,  procedure describes discovery from the T-EES

- Procedure should clearly indicate that the UE may need to establish a PDU connection to the target EDN in order to establish connectivity prior to accessing the T-EES.

2. Reason for Change

Align figure to procedure and indicate PDU connection requirement to the target EDN.

4. Proposal

It is proposed to agree to the following changes to clause 8.8.2.3 in 3GPP TS 23.558 v1.0.0

* * * * First Change * * * *

#### 8.8.2.3	EEC executed application context relocation

Figure 8.8.2.3-1 illustrates the procedure for the EEC to execute the application context relocation from the S-EAS to the T-EAS

Pre-condition:

1.	The AC at the UE already has a connection to the S-EAS; and

2.	The EEC is able to communicate with the S-EES.

Figure 8.8.2.3-1: EEC executed application context relocation procedure

1.	The EEC detects that application context relocation may be required.

Editor's Note	:	Details of detection event including what events the EEC detects is FFS

2.	The EEC decides to proceed required procedures for triggering application context relocation.

Editor's Note:	Gathering consent from other EDGEAPP entities is FFS.

3.	The EEC determines the T-EES by using the provisioned information or performing service provisioning procedure per clause 8.3 of the present document. Upon selecting T-EES,the UE may need to establish a new PDU connection to the target EDN when the selected T-EES resides in a different EDN. The EEC can then discover and select T-EAS by performing EAS Discovery with the T-EES per clause 8.5.2 of the present document.4.	The EEC sends the Application Context Relocation Request message to the S-EES to initiate application context transfer between the S-EAS and the T-EAS. The S-EES authorises the request from the EEC. The S-EES decides to execute application context relocation based on the information received by the EEC and the information of EEC context or EAS profile, and then proceed the below steps.

5. The S-EES sends the Application Context Relocation Notify message to the S-EAS to initiate application context transfer between the S-EAS and the T-EAS.

6. The S-EAS transfers the application context to the T-EAS at implementation specific time. This process is out of scope of the present specification.

7. The T-EAS sends the Application Context Relocation Complete message to the T-EES to confirm that the application context relocation has completed.

8. The S-EAS sends the Application Context Relocation Complete message to the S-EES to confirm that the application context relocation has completed.

9. The S-EES sends the Application Context Relocation Complete message to the EEC to confirm that the application context relocation has completed.

Editor's Note:	How the EEC modifies user plane connectivity for the AC is FFS.

Editor's Note:	Definition of the Information Flows in these procedures is FFS.

Editor's Note:	How the EES influences 3GPP Core Network in this procedure to modify user plane connectivity for the UE is FFS.

* * * * End of Change * * * *