3GPP TSG-SA WG6 Meeting #39-bis-e	S6-201734r1

e-meeting, 12th – 20th October 2020	(revision of S6-20xxxx)

Source:	InterDigital

Title:	Clarifications on Source EAS decided application context relocation

Spec:	3GPP TS 23.558 v1.0.0

Agenda item:	7.6

Document for:	Approval

Contact:	Atle Monrad <atle.monrad@interdigital.com>

1. Introduction

The highlighted reference in section 8.8.2.4 step 3 is incorrect:

3.	If no target Edge Application Server is available at the source Edge Application Server, the source Edge Application Server discovers the target Edge Application Server as described in clause 8.8.2.

The highlighted text in section 8.8.2.4 step 4 is incomprehensible

4.	The source Edge Application Server transfers the application context to the target Edge Application Server as per the time decides as per implementation. This process is out of scope of the present specification.

2. Reason for Change

Innacurate text in section 8.8.2.4

3. Proposal

It is proposed to agree to the following changes to clause 8.8.2.4 in 3GPP TS 23.558 v1.0.0.

* * * * First Change * * * *

#### 8.8.2.4	Source EAS decided application context relocation scenario

The procedure in this clause illustrates the scenario for source EAS decided application context relocation.

In this procedure, the source EAS may detect the need of application context relocation locally or is notified by the source Edge Enabler Server. The source EAS make the decision about whether to perform the application context relocation, and starts the application context relocation at a proper time.

Editor's Note:	It is FFS for the various events notified by S-EES.

Figure 8.8.2.4-1: Source EAS decided application context relocation scenario

The source Edge Application Server decided application context relocation scenario is outlined with four main phases: detection, decision, execution and clean up.

Phase I: Application context relocation detection

1.	The source Edge Application Server either receives notifications from source Edge Enabler Sever indicating that application context relocation may be required, or self detects the need for application context relocation. The notification may contain the target Edge Application Server information.

NOTE 1:	How the source Edge Application Server self detects the local need for application context relocation is outside the scope of this specification.

Editor's Note:	Whether and what kind of EEC detection can be provided to EAS via EES is FFS.

Phase II: Application context relocation decision

2.	The source Edge Application Server makes the decision to perform the application context relocation

NOTE 2:	How the source Edge Application server determines when to start the application context relocation is outside the scope of this specification.

Phase III:	Application context relocation execution

3.	If no target Edge Application Server is available at the source Edge Application Server, the source Edge Application Server discovers the target Edge Application Server as described in clause 8.8.3.2.

4.	The source Edge Application Server transfers the application context to the target Edge Application Server selected in step 3. This process is out of scope of the present specification.

Editor's Note:	It is FFS whether application context can be transferred via the Edge Enabler Layer.

Phase IV:	Post clean up after application context relocation

5.	All required entities perform clean-up

Editor's note:	Whether to inform the EEC as a post-application context relocation action at phase IV is FFS.

Editor's Note:	Detailed operation for cleaning up at each entity is FFS.

* * * * End of Change * * * *