3GPP TSG-SA WG6 Meeting #39-bis-e	S6-201752r1

e-meeting, 12 – 20 October 2020	(revision of S6-20xxxx)

Source:	Apple, Intel

Title:	Pseudo-CR on Determination of common application context transfer solutions

Spec:	3GPP TS 23.558 v1.0.0

Agenda item:	7.6

Document for:	Approval

Contact:	Mona Mustapha, Robert Zaus

1. Introduction

This pCR proposes that additional considerations are needed, should TS 23.558 continue to support multiple different solutions for application context relocation.

2. Reason for Change

The latest version of TS 23.588 specifies 5 different solutions for application context transfer, which are least partially incompatible. If the incompatible options remain in TS 23.558, then a successful application context transfer will only be possible, if all involved entities: AC, EEC, s-EES, s-EAS, t-EES and t-EAS are supporting a common procedure.

From a UE/EEC perspective, all the different solutions would need to be supported as UEs may roam to different networks and will need to interact with EDNs supporting different solutions. From an EDN perspective, there may also be a need to support more than one solution, given that we will be defining APIs to support service continuity and application developers may choose to use different mechanisms in their respective applications.

If SA6 does not mandate that both EECs and EDNs shall support all solutions, then the currently defined indications "service continuity required", signalled in the Application Client Profile IE from EEC to EES, and "service continuity supported", signalled in the EAS Profile IE from EAS to EES, are not sufficient to ensure a fully workable application context relocation procedure in deployed networks.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TS 23.558 v1.0.0.

* * * First Change * * * *

### 5.2.11	Service continuity

#### 5.2.11.1	General

This clause specifies the requirements for service continuity.

#### 5.2.11.2	Requirements

[AR-5.2.11.2-a]	The application layer architecture shall provide mechanisms to support service continuity such that the Application Context with a source Edge Application Server is transferred to a target Edge Application Server.

* * * First Change * * * *

### 8.8.2	Scenarios

#### 8.8.2.1	General

Editor's note:	whether the scenarios are overlapping and how to solve any co-existence issues are FFS

* * * End Changes * * * *