3GPP TSG-SA WG6 Meeting #39-bis-e	S6-201875

e-meeting, 12th – 20th October 2020	(revision of S6-20xxxx)

Source:	Samsung, InterDigital

Title:	Pseudo-CR on Key issue on monitor flight path

Spec:	3GPP TR 23.755 0.10.0

Agenda item:	8.5

Document for:	Approval

Contact:	Basavaraj (Basu) Pattan, basavarajjp@samsung.com

1. Introduction

According to the requirements [R-5.1-012] and [R-5.1-013] of TS 22.125, one of the key functionality of the UTM is to track the UAV/UAV-C location. This contribution proposes new key issue to track the flight path of the UAV.

2. Reason for Change

New key issue proposed on flight path tracking

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.755 v0.10.0.

* * * First Change * * * *

## 5.Z	Key issue#Z: Track UAV flight path

According to the requirements [R-5.1-012] and [R-5.1-013] of TS 22.125 [3], one of the key functionality of the UTM is to track the UAV/UAV-C location. Also, for “Automatic flight by UTM” control mode as mentioned in TS 22.125[3], it is required for UTM to track the UAV’s flight path. In order to achieve this, the USS/UTM needs to obtain UAV’s current location information periodically and process it to confirm the UAV’s compliance with the flight path.

Hence, it is required to the study the following:

- How the UAE/SEAL layer facilitates the USS/UTM to monitor the location deviation of an UAV.

- Whether the existing location reporting capabilities in the UAE/SEAL are sufficient to enable the USS/UTM to monitor the UAV’s pre-scheduled flight path.

* * * End of Change * * * *