3GPP TSG-SA WG6 Meeting #39-bis-e	S6-201876

e-meeting, 12th – 20th October 2020	(revision of S6-20xxxx)

Source:	Samsung

Title:	Pseudo-CR on Key Issue - Detection of problematic UAV

Spec:	3GPP TR 23.755 0.10.0

Agenda item:	8.5

Document for:	Approval

Contact:	Basavaraj (Basu) Pattan, basavarajjp@samsung.com

1. Introduction

As per TS 22.125, “The 3GPP system shall support detection, identification and reporting of problematic UAV(s) and the UAV controller to a UTM”. Considering this requirement, USS/UTM should be able to monitor all the UAVs served by the USS/UTM for any abnormal behaviour from UAVs.

2. Reason for Change

This pCR to proposes new key issue to study on detection of problematic UAVs.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.755 v0.10.0.

* * * First Change * * * *

## 5.Y	Key issue#Y: Problematic UAVs information to USS/UTM

As per TS 22.125 [3], “The 3GPP system shall support detection, identification and reporting of problematic UAV(s) and the UAV controller to a UTM”.

To detect and report the problematic UAV (for e.g, loss of connectivity, abnormal behaviour, unauthorized etc), many events related to the UAV need to be taken into consideration to conclude that the UAV is problematic. USS/UTM may be able to fetch multiple events related to the UAV (UE) from the 3GPP core network, using the current services of NEF/SCEF. However, achieving this, also needs constant monitoring and processing of multiple types of events related to the UAV, which is an additional burden on the USS/UTM.

Taking the above into consideration, this key issue is needed to study:

- Whether the existing event monitoring and reporting capabilities in the UAE/SEAL layers are sufficient to enable the USS/UTM in detecting problematic UAVs.

* * * End of Change * * * *