3GPP TSG-SA WG6 Meeting #39-bis-e	S6-20xxxx

e-meeting, 12th – 20th October 2020	(revision of S6-201720)

Source:	Huawei, Hisilicon

Title:	Pseudo-CR on FS 5GMARCH Solution on message reply from Non-3GPP UE to 5GMSGS UE

Spec:	3GPP TR 23.700-24 v1.0.0

Agenda item:	8.6

Document for:	Approval

Contact:	Hongxia Hao, haohongxia@huawei.com

1. Introduction

The solution addresses the identified gaps(in KI#5) about message delivery from Non-3GPP UE.

2. Reason for Change

Solution on the procedure of message delivery from Non-3GPP UE to MSGin5G Server is missing.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.0.0.

* * * First Change * * * *

#### 6.15.1.X	Non-3GPP UE replying a message to 5GMSGS UE

Figure 6.15.3-1 shows the solution of a Non-3GPP UE (e.g. RCS, LwM2M) replying a message to a 5GMSGS UE.

Pre-conditions:

1)	5GMSGS client in 5GMSGS UE and Non-3GPP UE has registered with the MSGin5G server.

Editor's Note: The Non-3GPP UE registration procedure is FFS.

2)	The Non-3GPP UE received a message from the 5GMSGS UE.

3)	The Non-3GPP Message Gateway is aware of the Non-3GPP message client on the Non-3GPP UE and provides the mapping to MSGin5G service ID.

4)	The Non-3GPP UE replies to the 5GMSGS UE upon receiving the message from the 5GMSGS UE.

Figure 6.15.1.X-1: Non-3GPP UE replies to 5GMSGS UE

1)	The Non-3GPP message client in Non-3GPP UE sends a Non-3GPP message request to the Non-3GPP Message Gateway through Non-3GPP Message server. The delivery report is requested in the message.

NOTE:	If the delivery report is not requested this procedure will stop after step 3 and step 4 to 6 will not be needed.

2)	The Non-3GPP Message Gateway translates the Non-3GPP message to MSGin5G message with delivery report requested and sends a MSGin5G message request to the MSGin5G Server, including the IEs of MSGin5G message according to the table 6.15.1.2-1.

Table 6.15.1.X-1: MSGin5G message request

| Information element | Status | Description |
| --- | --- | --- |
| Originator MSGin5G service ID | M | The service identity of the sender sending the message. |
| Recipient MSGin5G service ID | M | The service identity of the recipient receiving the message. |
| Message ID | M | Unique identifier of this message |
| Delivery report | O | Indicates if delivery acknowledgement is requested |
| Application ID | O | Identifies the application client for which the payload is intended. |
| Payload | M | Payload of the message |

3)	The MSGin5G Server forwards the MSGin5G message request to the target 5GMSGS Client in a 5GMSGS UE.

4)	The 5GMSGS Client in 5GMSGS UE sends an MSGin5G message delivery report to the MSGin5G Server.

5)	The MSGin5G Server forwards the MSGin5G message delivery report to the Non-3GPP Message Gateway.

6)	The Non-3GPP Message Gateway translates the MSGin5G message delivery report to a Non-3GPP message delivery report and sends it to the Non-3GPP message client through Non-3GPP message server.

* * * Next Change * * * *

### 6.15.2	Solution Evaluation

The solution in 6.15.1.2 is applicable for the SMS UE which is IMS or non-IMS based UE.

The solution in 6.15.1.X is applicable for the Non-3GPP UE which has a Non-3GPP message client. This solution enables the interworking with Non-3GPP message service and enables message reply from Non-3GPP UE to 5GMSGS UE, it requires Non-3GPP Message Gateway to be aware of the Non-3GPP message client on the Non-3GPP UE and provides the mapping to MSGin5G service ID. It requires no enhancement on current Non-3GPP Message Service procedure.

* * * Next Change * * * *