3GPP TSG-SA WG6 Meeting #39-bis-e	S6-201821 Rev2

e-meeting, 12th – 20th October 2020	(revision of S6-201821)

Source:	China Mobile

Title:	Pseudo-CR on FS_5GMARCH deliver message to Application Client

Spec:	3GPP TR 23.700-24 v1.0.0

Agenda item:	8.6

Document for:	Approval

Contact:	liuyueyjy@chinamobile.com

# 1. Introduction

This document proposes a new key issue that MSGin5G Service shall support delivery of a message to a specific application in the terminated UE. The terminated UE may or may not support a 5GMSGS client.

# 2. Reason for Change

Contribution with new text.

# 3. Conclusions

<Conclusion part (optional)>

# 4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.0.0.

* * * First Change * * * *

# 5	Key Issues

## 5.X	Key Issue X: deliver message to Application Client

### 5.X.1	Description

The requirement of deliver message to specific Application Client listed below is specified in [R-5.1.2-003] of 3GPP TS 22.262 [2].

[R-5.1.2-003] The MSGin5G Service shall support delivery of a message to a specific application in the terminated UE. This message contains the contents that can be handled by the specific application.

It is assume that each specific application is handled by a specific Application Client in the terminated UE. Multiple Application Clients may be hosted in the terminated UE. Meanwhile, the terminated UE may or may not support a 5GMSGS client.

Issues include:

- How to enable the 5GMSGS client to route MSGin5G messages to the specific Application Client, especially when Application ID is not included in the message (i.e. Application ID is not known by the sender) or Application ID of the Application Client is not known by the 5GMSGS client in the terminated UE

- If 5GMSGS client is not supported by the terminated UE, how to deliver the received message to the specific Application Client hosted in the terminated UE.

- , If the message can not be delivered to the 5GMSGS client but can be delivered to the Legacy-3GPP Client (e.g. the terminated UE loses data connection), how to deliver the received message to the specific Application Client hosted in the terminated UE.

### 5.X.2	Identified Gaps

The following gaps have been identified to fulfil the identified requirements:

- The Application Clients configuration procedure which enables the 5GMSGS Client to route MSGin5G messages to Application Clients is needed to be studied.

- If 5GMSGS client is not supported by the terminated UE, or the message can not be delivered to the 5GMSGS client but can be delivered to the Legacy-3GPP/non-3GPP Client, whether it is possible to deliver the message to the Application Client is needed to be studied. If the message can be delivered to the Application Client, the related procedure of message delivery is needed to be studied.

- Editor's note:	If the Application Clients are MSGin5G un-aware, i.e. they don't know that they are talking via a 5GMSGS client or gateway, how to deliver messages to this kind of Application Client is FFS.