3GPP TSG-SA WG6 Meeting #39-bis-e	S6-201860-rev1

e-meeting, 12th – 20th October 2020	(revision of S6-201860)

Source:	Samsung

Title:	Pseudo-CR on Solution for group list fetch

Spec:	3GPP TR 23.700-24 v1.0.0

Agenda item:	8.6

Document for:	Approval

Contact:	Basavaraj (Basu) Pattan, basavarajjp@samsung.com

1. Introduction

This contribution provides solution where the 5GMSGS Client can fetch the list of groups in which it is member with help of group management client.

2. Reason for Change

KI#8 has identified following gap:

- Long latency may exist between UE and MSGin5G server due to the UE may be offline or in Power Saving Mode specified in 3GPP TS 23.682 [3]. The group data in the UE and the MSGin5G server may not be synchronized on time, so some abnormal scenarios are needed to be specified.

When the group is created by authorized user, the SEAL Group Management server sends group creation notification to all members. If a UE is offline at the time when group is created, it may not receive notification. It is required for the 5GMSGS Client to know latest updated list of groups in which it is a member.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.0.0.

* * * First Change * * * *

### 6.4.X	Solution description for group list fetch

This solution addresses issues related to synchronization of group information between UE and SEAL Group management server. As specified in KI#8, the UE may be offline or in Power Saving Mode and may not be aware about newly created or deleted MSGin5G groups in which the UE/User is a member.

* * * Next Change * * * *

#### 6.4.X.1	Information Elements

##### 6.4.X.1.1	Group list fetch request

Table 6.4.X.1.1-1 describes the information flow for group list fetch request from the SEAL Client (group management client) to the SEAL Server (group management server).

Table 6.4.X.1.1-1: Group list fetch request

| Information element | Status | Description |
| --- | --- | --- |
| Identity | M | The MSGin5G service ID (VAL user or VAL UE) performing the operation. |

##### 6.4.X.1.2	Group list fetch response

Table 6.4.X.1.2-1 describes the information flow for Group list fetch response from the SEAL Server (group management server) to the SEAL Client (group management client).

Table 6.4.X.1.2-1: Get group list fetch response

| Information element | Status | Description |
| --- | --- | --- |
| Result | M | Result from the SEAL Server (group management server) in response to group list fetch request indicating success or failure |
| MSGin5G service ID (VAL User ID) | M | The identity of the MSGin5G service ID (VAL User) for whom this notification is targeted. |
| Group service ID (VAL group IDs) | M | The list of Group service ID (VAL groups) for which the MSGin5G service ID (VAL User) is member |

* * * Next Change * * * *

#### 6.4.X.2	Group List Fetch

Pre-conditions:

1)	Group is previously defined on the SEAL Server (group management server) including the list of users.

2)	List of groups to which a MSGin5G service ID (VAL UE/ VAL User) belongs to is known to the SEAL Server (group management server) for each of the MSGin5G service ID (VAL UE/ VAL User).

3)	MSGin5G service ID (VAL user) has not received group announcement message as it was offline previously.

Figure 6.4.X.2-1: Group list fetch

1)	The 5GMSGS Client (VAL client) requests SEAL Client (group management client) to provide the list of groups in which the MSGin5G service ID (VAL UE or VAL User) is a member.

2)	The SEAL Client (group management client) initiates the group list fetch request towards the SEAL server (group management server). The information elements described in clause 6.4.X.1.1 are included in the group list fetch request.

3)	The SEAL server (group management server) checks the authorization of group list subscribe request and if authorized, sends the group list fetch response containing list of groups in which the MSGin5G service ID (VAL user) is member. The information elements described in clause 6.4.X.2.1 are included in the group list fetch response.

4)	The SEAL Client (group management client) notifies the list of groups to the 5GMSGS Client (VAL client).

* * * End of Change * * * *