3GPP TSG-SA WG6 Meeting #39-bis-e	S6-20XXXX

e-meeting, 12th – 20th October 2020	(revision of S6-201722)

Source:	Huawei, Hisilicon

Title:	Pseudo-CR on FS 5GMARCH solution on APIs provided by MSGin5G server

Spec:	3GPP TR 23.700-24 v1.0.0

Agenda item:	8.6

Document for:	Approval

Contact:	Hongxia Hao, haohongxia@huawei.com

1. Introduction

The solution addresses the identified issues and gap in Key Issue #9.

2. Reason for Change

In KI#9, Issues include:

-	For the MOAT message,

-	How to interact between MSGin5G server and different logical application servers in MOAT scenario.

The following gaps have been identified in KI#9:

-	The interaction procedure between different kinds of logical application servers and 5GMSGS server is needed to be defined.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.0.0.

* * * First Change * * * *

## 6.X	Solution X: APIs provided by MSGin5G server

### 6.X.1	Description

This solution addresses the following identified issues and gaps related with the interaction between AS and MSGin5G Server under Key Issue #9.

Editor's Note:	More APIs are FFS.

### 6.X.2	APIs provided to Application Server

MSGin5G server provides restful APIs to Application Server.

#### 6.X.2.1 Message Delivery API

MSGin5G server provides Message Delivery API to Application Server, the App Server may use this API with the following information elements to the MSGin5G server for delivering a message to the recipient:

# Table 6.X.2-1: Message Delievery API request

| Information element | Status | Description |
| --- | --- | --- |
| Originator ID | M | The identifier of Application Server |
| Recipient ID | O | The identifier of recipient |
| Group ID | O | The identifier of Group if the target of the message is a group. |
| Service Area ID | O | The identifier of Group if the message is broadcast message. |
| Application ID | O | The identifier of application |
| Delivery report request | O | Indicates whether the delivery status of this message from the recipient is required. |
| Message Content | M | Message content that will be used as a payload of a MSGin5G message |
| Security Credentials | O | Security information required by the MSGin5G Server. |
| NOTE: At least one of Recipient ID, Group ID or Service Area ID shall be present. |

#### 6.X.2.2 Application Server Registration API

MSGin5G server provides Application Server Registration API to Application Server, the App Server may use this API to register on the MSGin5G Server. The API request includes the information elements in table 6.11.1.3-1, the API response includes the information elements in table 6.11.1.3-2.

* * * Next Change * * * *