3GPP TSG-SA WG6 Meeting #39-bis-e	S6-201785

e-meeting, 12th – 20th October 2020

3GPP TSG|WG-??? Meeting #nn 	XX-yyxxxx

Location, Country, Date 	(revision of xx-yyxxxx)

# Source:	CATT

# Title:	New SID on study on location management service supporting 5G location services

# Document for:	Approval

Agenda Item:	9

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	Study on location management service supporting 5G location services

## Acronym: FS_5GLMS

## Unique identifier:

Potential target Release: Rel-17

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  | X |  |
| No |  |  |  |  |  |
| Don't know | X |  | X |  |  |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

This work item is a

|  | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
| X | Study Item |

### 2.2	Parent Work Item

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |

Dependency on non-3GPP (draft) specification:

## 3	Justification

The 5G system has been designed and expected to provide highly efficient positioning services that enable a vast amount of different location-based applications and location-aware communications. SA1 has specified in TS 22.261 the requirements for high accuracy positioning and positioning services that have been derived from multiple vertical use cases including mission critical, road-related, rail, aerial-related and other scenarios. The stage 2 work of location services in 5G system has been defined by SA2 as in TS 23.273. The UE Positioning function of NG-RAN has been defined by RAN2 as in TS 38.305.

Requirements for 5G positioning utilized by verticals have been addressed in TS 22.261, for example:

The 5G system shall be able to make the position-related data available to an application or to an application server existing within the PLMN, external to the PLMN, or in the User Equipment.

The 5G System shall be able to negotiate the positioning methods according to the operator's policy or the application’s requirements or the user's preferences and shall support mechanisms to allow the network or the UE to trigger this negotiation.

It is deserved for the application layer to leverage 5G positioning and location capabilities to meet the growing needs of verticals for location services.

## 4	Objective

The objectives of the study include:

1)	Evaluate stage 1 requirements (including 3GPP TS 22.261, TS 22.071, TR 22.872) regarding positioning and location that have potential application level impacts;

2)	Evaluate existing application layer architectures and functions of location management, and analyse the gap and architectural requirements for supporting 5G location services; the aspects for the application layer supporting 5G location services can include:

-	Retrieval of LCS location information from the 5G network;

-	Determination of QoS and other attributes used for service requests of 5GS LCS;

-	Correlations of network level and application level identities for location retrieval;

-	Use of location information from different source (e.g. from 5GS LCS and the third party);

-	Management of location information and location related data;

-	Negotiation for positioning methods (e.g. hybrid positioning).

3)	Identify issues and develop solutions based on 1) and 2) to provide the application level location service leveraging the 5G positioning and location capabilities.

NOTE:	During the study the existing solutions developed by SEAL can be considered.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Rapporteur |
| TR | 23.XXX | Study on location management service supporting 5G location services | TSG#93 | TSG#94 | Zhang, Ling, CATT, zhangling@catt.cn |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |

## 6	Work item Rapporteur(s)

Zhang, Ling, CATT, zhangling@catt.cn

## 7	Work item leadership

SA6

## 8	Aspects that involve other WGs

SA2 for core network architecture aspects, SA3 for security aspects

## 9	Supporting Individual Members

Supporting IM name

CATT

China Mobile

China Unicom

CALTTA

Convida Wireless