3GPP TSG-SA WG6 Meeting #39-bis-e	S6-20xxxx

e-meeting, 12th – 20th October 2020	(revision of S6-201947)

Source:	Samsung

Title:	Pseudo-CR on Solution for group notification

Spec:	3GPP TR 23.700-24 v1.0.0

Agenda item:	8.6

Document for:	Approval

Contact:	Basavaraj (Basu) Pattan, basavarajjp@samsung.com

1. Introduction

This contribution provides solution where the MSGin5G Server sends group notification to the legacy 3GPP UEs and non-3GPP UEs, which are members of newly created group.

2. Reason for Change

KI#8 has identified following gap:

- The group management interworking in the MSGin5G gateway are needed to be defined.

When a new group is created with members including 5GMSGS UE, Legacy 3GPP UE and Non-3GPP UE, the SEAL Group Management server sends group creation notification to the member UEs having group management client. However when the newly created group has members which do not have group management client, such as Legacy 3GPP UEs and Non-3GPP UEs, the MSGin5G Server sends group notification to those UEs via Message Gateway. If group information is not known to the Legacy 3GPP UEs and Non-3GPP UEs, then those cannot initiate communication to groups.

The pCR also provides the SEAL enhancments required to the solution in SEAL TS 23.434 [9] subclause 10.3.3.

Lastly, the pCR provides some editorials to subclauses 6.4.2, 6.4.3 and 6.4.4.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.0.0.

* * * First Change * * * *

### 6.4.5	Solution description for group notification interworking using SEAL

Figure 6.4.5-1 below illustrates MSGin5G Server (VAL server) sending the group notification towards the Message Gateways (the Legacy 3GPP Message Gateway or the non-3GPP Message Gateway or both) in order to notify the UEs (who are members of the created group) which do not support SEAL client (Group management client). In this procedure, the group notification is handled by MWGin5G Server, when the group management is using SEAL as specified in 3GPP TS 23.434 [9].

Editor's note:	The solution for Group update notification is FFS.

Pre-conditions:

1)	MSGin5G Server interacts with SEAL Server using the procedures over SEAL-S reference point as specified in 3GPP TS 23.434 [9].

2)	MSGin5G Server is aware of the legacy 3GPP message client (e.g. SMS client) in legacy 3GPP UE and interacts with it via Legacy 3GPP Message Gateway.

3)	MSGin5G Server is aware of the Non-3GPP message client in Non-3GPP UE and interacts with it via Non-3GPP Message Gateway.

4)	The group creation notification includes identities belonging to different types of UEs i.e. 5GMSGS UE, Legacy 3GPP UE and Non-3GPP UE.

5)	Legacy 3GPP Message Gateway and Non-3GPP Message Gateway does not support SEAL group management functionality.

# Figure 6.4.5-1: Group notification in MSGin5G service

1)	The SEAL Server (Group management server) sends a group creation notification message to the MSGin5G Server including the list of identities belonging to different types of UEs i.e. 5GMSGS UE, Legacy 3GPP UE and Non-3GPP UE. The information elements defined in table 10.3.2.3-1 specified in 3GPP TS 23.434 [9] are included in the message.

2)	The MSGin5G server (VAL server) determines whether the received group creation notification message has list of identities that belong to Legacy 3GPP UEs or Non-3GPP UEs or both i.e. MSGin5G server analyses the registration status of the members in the received identity list and determines if it is to be routed to a Legacy 3GPP UE or Non-3GPP UEs or both and that a group notification message should be sent to those UEs.

3)	Upon determining in Step 2) that the group notification message should be sent to Legacy 3GPP UEs:

3a)	The MSGin5G Server initiates the group notification message to the legacy 3GPP Message Gateway for delivery. The information elements defined in Table 6.4.5-1 are included in the request.

Table 6.4.5-1: group notification to Legacy 3GPP UEs

| Information element | Status | Description |
| --- | --- | --- |
| MSGin5G Server Address | M | The address of the MSGin5G server sending the message. |
| List of MSGin5G service ID(s) | M | The service identity of the recipient Legacy 3GPP UE(s) where the notification is to be sent. (NOTE 1) |
| Message ID | M | Unique identifier of this message |
| Application ID | O | Identifies the application for which the payload is intended. |
| Group ID | M | Payload of the message containing VAL group ID that was created |
| List of members | M | List of VAL user IDs or VAL UE IDs that are part of the created group |
| Group Configuration | M | Group configuration information (NOTE 2) |
| NOTE 1: List of MSGin5G service ID(s) could be one or more. NOTE 2: Group configuration information can be obtained independently by MSGin5G Server (VAL server) according to subclause 10.3.6.2 specified in 3GPP TS 23.434 [9]. |

3b)		The legacy 3GPP Message Gateway translates the group notification message to a legacy 3GPP message and sends it to the legacy 3GPP message client according the procedures in TS 23.204 or the procedure in clause 4.13.3 of TS 23.502. This step is outside the scope of the current specification.

NOTE:	Whether or not to include, group members and group configuration information towards the Legacy 3GPP UE is outside the scope of the current specification.

4)	Upon determining in Step 2) that the group notification message should be sent to Non-3GPP UEs:

4a)	The MSGin5G Server initiates the group notification message to the Non-3GPP Message Gateway for delivery. The information elements defined in Table 6.4.5-2 are included in the request.

Table 6.4.5-2: group notification to Non-3GPP UEs

| Information element | Status | Description |
| --- | --- | --- |
| MSGin5G Server Address | M | The address of the MSGin5G server sending the message. |
| MSGin5G service ID | M | The service identity of the recipient Non-3GPP UEs where the notification is to be sent. |
| Message ID | M | Unique identifier of this message |
| Application ID | O | Identifies the application for which the payload is intended. |
| Group ID | M | Payload of the message containing VAL group ID that was created |
| List of members | M | List of VAL user IDs or VAL UE IDs that are part of the created group |
| Group Configuration | O | Group configuration information (NOTE) |
| NOTE: Group configuration information can be obtained independently by MSGin5G Server (VAL server) according to subclause 10.3.6.2 specified in 3GPP TS 23.434 [9]. |

4b)		The Non-3GPP Message Gateway translates the group notification message to a Non-3GPP message and sends it to the Non-3GPP message client. This step is outside the scope of the current specification.

* * * Next Change * * * *

### 6.4.6	Solution description for SEAL enhancements to group notification interworking

The solution in SEAL TS 23.434 [9] subclause 10.3.3 is necessary to be enhanced for group management in MSGin5G Service for supporting group management interworking with the Message Gateway. The enhancement is required for both the types of Message Gateways used to deliver MSGin5G messages to different UE types: the Legacy 3GPP Message Gateway and the non-3GPP Message Gateway.

The 5GMSGS Client (or the Application Server) interacts with the Group management client of the SEAL group management service and the MSGin5G Server interacts with the Group management server of the SEAL group management service specified in 3GPP TS 23.434 [9].

Figure 6.4.5-1 below illustrates the group creation operations by authorized VAL user/UE/administrator to create a group. It applies to the scenario of normal group creation by a VAL administrator or by authorized user/UE. Further the identity list that is part of the group to be created may contain the list of VAL user IDs or VAL UE IDs which does not have group management client on the UE (e.g. legacy UEs).

Pre-conditions:

1.	The group management client, group management server, VAL server and the VAL group members belong to the same VAL system.

2.	The authorized VAL user/UE/administrator is aware of the users' identities which will be combined to form the VAL group.

3.	Identity list that is part of the group to be created may contain the list of VAL user IDs or VAL UE IDs which does not have group management client on the UE (e.g. legacy UEs).

Figure 6.4.6-1: Figure 10.3.3-1 in SEAL TS 23.434 [9] subclause 10.3.3

1.	The group management client of the authorized VAL user/UE/administrator requests group create operation to the group management server. The identities of the users or UEs being combined and the information of the VAL services that are enabled on the group shall be included in this message.

2.	During the group creation, the group management server creates and stores the information of the group. The group management server performs the check on the policies e.g. maximum limit of the total number of VAL group members for the VAL group(s).

NOTE:	The exact policies are out of scope of the present document.

3.	The group management server may conditionally notify the VAL server regarding the group creation with the information of the group members. When the identity list with the list of VAL user IDs or VAL UE IDs that are part of the created group contain the list of VAL user IDs or VAL UE IDs which does not have group management client on the UE (e.g. Legacy UEs or Non-3GPP UEs), it is responsibility of the VAL server to initiate the group creation notification towards those UEs.4.	The VAL group members of the VAL group are notified about the newly created VAL group configuration data. Such notification is sent to the VAL group members having group management client and for the VAL group members not having group management client (e.g. Legacy UEs or Non-3GPP UEs) the notification is sent as described in Step-3.

5.	The group management server provides a group creation response to the group management client of the administrator/authorized VAL user/UE.

### 6.4.7	Solution evaluation

Editor's Note: Solution evaluation is FFS.

* * * Next Change * * * *

### 6.4.2	Solution description for establishing a group

The solution in SEAL TS 23.434 [9] subclause 10.3.3 is used for group creation in MSGin5G Service. The 5GMSGS Client (or the Application Server) interacts with the Group management client of the SEAL group management service and the MSGin5G Server interacts with the Group management server of the SEAL group management service specified in 3GPP TS 23.434 [9].

### 6.4.3	Solution description for adding UEs to the group or removing UEs from the group

The solution in SEAL TS 23.434[9] subclause 10.3.5.2 is used for adding UEs to the group or removing UEs from the group in MSGin5G Service. The 5GMSGS Client (or the Application Server) interacts with the Group management client of the SEAL group management service and the MSGin5G Server interacts with the Group management server of the SEAL group management service specified in 3GPP TS 23.434 [9].

### 6.4.4	Solution description for configuration of a maximum number of members in a group

The solution in SEAL TS 23.434[9] subclause 10.3.6.1 is used for configuration of a maximum number of members in a group in MSGin5G Service. The 5GMSGS Client (or the Application Server) interacts with the Group management client of the SEAL group management service and the MSGin5G Server interacts with the Group management server of the SEAL group management service specified in 3GPP TS 23.434 [9].

* * * End of Change * * * *