3GPP TSG-SA WG6 Meeting #39-bis-e	S6-20xxxx

e-meeting, 12th – 20th October 2020	(revision of S6-201965 was 1800)

Source:	Samsung Electronics

Title:	Relation between DNAIs of EAS, EES and EDN

Spec:	3GPP TS 23.558 v1.0.0

Agenda item:	7.6

Document for:	Approval

Contact:	Nishant Gupta <nishant.gup@samsung.com>

1. Introduction

This contribution provides the relationship between the DNAIs of the EAS, EES and the EDN, and closes several related ENs.

2. Reason for Change

Considering the following:

-	To connect to an EAS from UE's current location, the UE, from the same location, shall be able to connect to the EES at which EAS is registered. Otherwise, discovery of the EAS is not possible.

-	Given that the EASs may have individual service areas, it is not necessary that if the EEC in a UE is able to connect to an EES, the ACs in the same UE, from the same location can also connect to all the EASs registered with the EES.

-	To connect to an EES from UE's current location, the UE, from the same location, shall be able to connect to the EDN in which the EES resides.

-	It is not necessary that if a UE is able to connect to an EDN, the UE, from the same location has local access to all the EESs located in the EDN. E.g., in a shared EDN such as internet DN (deployment option 1), all EES may not be available locally available to UEs location.

The contribution proposes that the list of DNAIs of the EAS is a subset of the list of DNAIs of the EES.

Similarly, the list of DNAIs of the EES is a subset of the list of DNAIs of the EDN.

Essentially:

DNAIs of an EAS ⊂ DNAIs of the EES where the EAS is register at ⊂ DNAIs of the EDN where the EES resides

3. Proposal

It is proposed to agree the following changes to 3GPP TS 23.558 v1.0.0.

* * * First Change * * * *

### 8.2.4	Edge Application Server Profile

Table 8.2.4-1: Edge Application Server Profile

| Information element | Status | Description |
| --- | --- | --- |
| EAS ID | M | The identifier of the EAS |
| EAS Endpoint | M | Endpoint information (e.g. URI, FQDN, IP address) used to communicate with the EAS. This information maybe discovered by EEC and exposed to Application Clients so that application clients can establish contact with the EAS. |
| Application Client ID(s) | O | Identifies the Application Client(s) that can be served by the EAS |
| EAS Provider Identifier | O | The identifier of the EAS Provider |
| EAS Type | O | The category or type of EAS (e.g. V2X) |
| EAS description | O | Human-readable description of the EAS |
| EAS Schedule | O | The availability schedule of the EAS (e.g. time windows) |
| EAS Service Area | O | The geographical service area that the EAS serves |
| EAS Service KPIs | O | Service characteristics provided by EAS, detailed in Table 8.2.5-1 |
| EAS service permission level | O | Level of service permissions e.g. trial, gold-class supported by the EAS |
| EAS Feature(s) | O | Service features e.g. single vs. multi-player gaming service supported by the EAS |
| Service continuity support | O | Indicates if the EAS supports service continuity or not. This IE may also indicate whether the EAS supports Application Context Transfer. |
| List of EAS DNAI(s) | O | DNAI(s) associated with the EAS. This IE is used as Potential Locations of Applications in clause 5.6.7 of 3GPP TS 23.501 [2]. It is a subset of the DNAI(s) associated with the EDN where the EAS resides. |
| EAS Availability Reporting Period | O | The availability reporting period (i.e. heart beat period) that indicates to the EES how often it needs to check the EAS's availability after a successful registration. |
| EAS Required Service APIs | O | A list of the Service APIs that are required by the EAS |
| EAS Status | O | The status of the EAS (e.g. enabled, disabled, etc.) |

Editor's Note: Should the EAS DNAIs be limited to a subset of DNAIs of the EES it is registered at is FFS.

### 8.2.6	Edge Enabler Server Profile

The Edge Enabler Server profile includes information about the EES and the services it provides.

Table 8.2.6-1: Edge Enabler Server Profile

| Information element | Status | Description |
| --- | --- | --- |
| EES ID | M | The identifier of the EES |
| EES Endpoint | M | Endpoint information (e.g. URI, FQDN, IP address) used to communicate with the EES. This information is provided to the EEC to connect to the EES. |
| Edge Application Server IDs | M | List of Edge Application Server IDs registered with the EES. |
| EES Provider Identifier | O | The identifier of the EES Provider (such as ECSP) |
| List of EES DNAI(s) | O | DNAI(s) associated with the EES. This IE is used as Potential Locations of Applications in clause 5.6.7 of 3GPP TS 23.501 [2]. It is a subset of the DNAI(s) associated with the EDN where the EES resides. |

Editor's Note: Whether there is a need to specify a Service Area for the EES is FFS.

* * * Next Change * * * *

#### 8.8.3.3	Retrieve Target Edge Enabler Server procedure

Figure 8.8.3.3-1 illustrates the procedure for the source Edge Enabler Server to retrieve the target Edge Enabler Server information from the Edge Configuration Server.

Pre-condition:

1.	The source Edge Enabler Server has been pre-configured with the address of the Edge Configuration Server; and

2.	The Application Client at the UE already has on-going application traffic with the source Edge Application Server.

Figure 8.8.3.3-1: Retrieve target Edge Enabler Server procedure

1.	The source Edge Enabler Server sends the Retrieve Edge Enabler Server request (UE location information or UE identity, EAS ID of the source Edge Application Server, target DNAI) to the Edge Configuration Server in order to identify the target Edge Enabler Server which has an Edge Application Server available to serve the given Application Client in the UE.

2.	If the request contains the UE identity (e.g. GPSI) but the UE location is not known to the Edge Configuration Server, then the Edge Configuration Server interacts with 3GPP core network to retrieve the UE location. The Edge Configuration Server determines target Edge Enabler Server(s) as per the parameters (e.g. EAS ID, target DNAI) in the request and the UE location information.

3.	The Edge Configuration Server sends the Retrieve Edge Enabler Server response (EAS ID of the source Edge Application Server, list of target Edge Enabler Server(s) information) to the source Edge Enabler Server. The list of target Edge Enabler Server(s) information includes the endpoint for each of the target Edge Enabler Server(s), e.g. IP address determined in step 2.

Editor's note:	It is FFS whether and what additional info is included in the Retrieve EES Request.

Editor's note:	How to handle the case of multiple ECS(s) configured at the UE is FFS.

#### 8.8.4.1	Edge Application Server discovery request

Table 8.8.4.1-1 describes information elements for the Edge Application Server Discovery Request from the EAS to the Edge Enabler Server and from the source Edge Enabler Server to the target Edge Enabler Server. Table 8.8.4.1-2 provides further detail about the EAS Discovery Filter information element.

Table 8.8.4.1-1: Edge Application Server discovery request

| Information element | Status | Description |
| --- | --- | --- |
| Requestor identifier | M | The ID of the requestor (e.g. EAS ID or EES ID) |
| UE identifier | O | The identifier of the UE (i.e. GPSI or identity token). |
| Security credentials | M | Security credentials resulting from a successful authorization for the edge computing service. |
| EAS Discovery Filter Set of characteristics to determine required Edge Application Servers, as detailed in Table 8.5.2.3.1-2. | M | Set of characteristics to determine required Edge Application Servers, as detailed in Table 8.8.4.1-2. |
| UE location | O | Location of the UE (e.g. geographical area, civic address). |
| Target DNAI | O | Target DNAI information which can be associated with potential target EAS(s) |

Editor's Note:	Detailed description of Target DNAI information is FFS.

Editor's Note: With regards to UE location & Target DNAI - it is for FFS if we need two different UE Location definitions as per Editor’s Note in clause 7.3.2,

Editor's Note: Whether and how security credentials corresponding to different Requestors considering different deployments are handled is FFS and in scope of SA3.

Table 8.8.4.1-2: EAS Discovery Filter

| Information element | Status | Description |
| --- | --- | --- |
| List of Edge Application Server characteristics | M | Describes the characteristics of required Edge Application Servers as per table 8.5.3.1-2 |