3GPP TSG-SA WG6 Meeting #40-e	S6-202210

e-meeting, 16th – 24th November 2020	(revision of S6-20xxxx)

Source:	Huawei, Hisilicon, Qualcomm

Title:	New KI on UAS enabler layer and Edge Enabler Layer alignment

Spec:	3GPP TR 23.755 v0.b.0

Agenda item:	8.4

Document for:	Approval

Contact:	Niranth (namogh@huawei.com)

1. Introduction

This contribution provides a proposal for a new KI on UAS enabler layer and Edge Enabler Layer alignment alignment.

2. Reason for Change

SA2 has specified local DN and mechanisms to route data traffic of the UE to the local DN in 3GPP TS 23.501.

SA6 has specified edge enabler layer to optimize the access to applications deployed on the edge data network in 3GPP TS 23.558..

It can be studied further from the perspectives of Edge deployments whether and how alignment can be achieved between UAE layer and Edge Enabler Layer.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.755v0.b.0.

* * * First Change * * * *

## 5.z	Key issue #z: UAE and EEL alignment

Edge deployments are vitally important for applications that require performance levels that cannot be met by existing cloud deployments. Applications executing on a UAV or UAV-C may require performance levels that can only be met when using edge deployed application servers.

It should be studied how application servers deployed in an edge data network can be utilized by the corresponding application clients in the UAV or UAV-C by aligning the UAE architecture with the EEL architecture (as specified in 3GPP TS 23.558 [x]).