3GPP TSG-SA WG6 Meeting #40-e	S6-202060_rev1

e-meeting, 16th – 24th November 2020	(revision of S6-20xxxx)

Source:	Huawei, Hisilicon

Title:	Corrections about MSGin5G gateway

Spec:	3GPP TR 23.700-24 v1.1.0

Agenda item:	8.5

Document for:	Approval

Contact:	Hongxia Hao, haohongxia@huawei.com

1. Introduction

Just for changing MSGin5G Gateway to Non-3GPP Message Gateway.

2. Reason for Change

Align with the architure.

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.1.0.

* * * First Change * * * *

## 3.1	Definitions

For the purposes of the present document, the terms and definitions given in 3GPP TR 21.905 [1] and the following apply. A term defined in the present document takes precedence over the definition of the same term, if any, in 3GPP TR 21.905 [1].

Controller UE: usually a smart device or an application in the terminal that can send control message instructions to machine equipment. A controller terminal can control multiple controlled terminals.

Controlled UE: an IoT equipment which can access the network through a variety of technologies and network slicing. A controlled terminal can be controlled by a number of controller terminals.

Non-3GPP Message: the message supported in a message service which is not defined by 3GPP (e.g. RCS message as specified in GSMA PRD RCC.07 [4], OMA LWM2M message as specified in OMA OMA-ERELD-LightweightM2M [5]).

MSGin5G service capabilities: the subset of MSGin5G service available to access and/or communicate with other UEs or application servers. The whole set of MSGin5G service includes point-to-point messaging, application-to-point messaging, group messaging and broadcast messaging.

For the purpose of the present document, the following terms given in 3GPP TS 22.262 [2] apply:

MSGin5G Server

MSGin5G Gateway

* * * Next Change * * * *

### 4.2.2	Scenario 1.2: Message between non-3GPP Controller UE and MSGin5G Controlled UE

This scenario describes the case where Controller UE1 (e.g. a mobile handset Terminal 1, or an application client APP 1 in a mobile handset Terminal 1) communicates with Controlled UE2 (e.g. wearable device Terminal 2 like a smart watch) by using non-3GPP message service (e.g. RCS message service specified in GSMA PRD RCC.07 [4]), and UE2 uses MSGin5G service and is 5GMSG transport capable.

UE1 is connected to a non-3GPP message server and then connected to MSGin5G application layer via Non-3GPP Message Gateway. UE2 connected the 5G system directly and served by MSGin5G application layer. The scenario is illustrated in figure 4.2.2-1.

NOTE:	The Non-3GPP Message Gateway facilitates the translation between the MSGin5G Service and non-3GPP message service. The application functional aspect and procedure in Non-3GPP Message Gateway will be studied.

# Figure 4.2.2-1: Message between non-3GPP Controller UE and MSGin5G Controlled UE

The scenario consists of the following aspects:

-	UE 1 is authorized by the MSGin5G service via Non-3GPP Message Gateway.

-	The Non-3GPP Message Gateway records the mapping between the identity in MSGin5G service and the identity in non-3GPP message service for both UE1 and UE2.

-	If message is originated by authorized UE1, non-3GPP message server forwards the message to Non-3GPP Message Gateway. MSGin5G server identifies the UE2 and forward the MSGin5G message to UE2. UE2 or MSGin5G server may send the delivery status to UE 1.

For the case where Controlled UE2 (e.g. wearable device Terminal 2 like smart watch) communicates with Controller UE1 (e.g. a mobile handset Terminal 1, or an application client APP 1 in a mobile handset Terminal 1) that uses non-3GPP message (e.g. RCS message service specified in GSMA PRD RCC.07 [4]) .

-	If message is originated by authorized UE2, the MSGin5G service forwards the message to UE1 (mobile handset terminal 1 or a specific application in terminal 1) in the MSGin5G service, and the Non-3GPP Message Gateway forward the message to UE1. UE1 or MSGin5G server may send the delivery status to UE 2.

* * * Next Change * * * *

### 4.2.3	Scenario 1.3: Message between MSGin5G Controller UE and non-3GPP Controlled UE

This scenario describes the case where Controller UE1 (e.g. a mobile handset Terminal 1, or an application client APP 1 in a mobile handset Terminal 1) communicates with Controlled UE B  (e.g. wearable devices Terminal 2 like smart watch) by using MSGin5G service, and UE2 uses non-3GPP message service (e.g. OMA LWM2M specified in OMA OMA-ERELD-LightweightM2M [5]).

UE1 connected to 5G system and served by MSGin5G application layer. UE2 served by non-3GPP message server. The MSGin5G message and non-3GPP message will be transferred to each other by the Non-3GPP Message Gateway. The scenario is illustrated in figure 4.2.3-1.

# Figure 4.2.3-1: Message between MSGin5G Controller UE and non-3GPP Controlled UE

The scenario consists of the following aspects:

-	UE2 is authorized by the MSGin5G service via Non-3GPP Message Gateway.

-	The Non-3GPP Message Gateway records the mapping between the identity in MSGin5G service and the identity in non-3GPP message service for both UE1 and UE2.

-	If message is originated by authorized UE1, the MSGin5G server forwards the message to UE2 in the MSGin5G service, and the Non-3GPP Message Gateway forwards the message to UE2. UE2 or MSGin5G server may send the delivery status to UE1.

For the case where Controlled UE2 (e.g. wearable device Terminal 2 like smart watch) that uses non-3GPP message communicates with Controller UE1 (e.g. a mobile handset Terminal 1, or an application client APP 1 in a mobile handset Terminal 1).

-	If message is originated by authorized UE2, the MSGin5G server forwards the MSGin5G message to the Non-3GPP Message Gateway. MSGin5G server identifies the identity of UE1and forward the non-3GPP message to UE1. UE1 or MSGin5G server may send the delivery status to UE2.

NOTE:	The scenario is out of scope if both UE1 and UE2 use non-3GPP message.

* * * Next Change * * * *

### 4.4.1	Scenario 3.1: Group message between MSGin5G UEs

This scenario describes the case where MSGin5G UE1 (e.g. a mobile handset terminal 1 or an application client APP 1 in a mobile handset Terminal 1) communicates with a group of UEs (MSGin5G UEs or legacy 3GPP UEs or non-3GPP UE). All UEs may be in different geographical area.

NOTE:	MSGin5G server may consist of numerous functions, e.g. MSGin5G Server group function. The application architecture to support the scenarios will be studied.

The message will be first routed to the MSGin5G server and then forwarded to all other parties. The scenario is illustrated in figure 4.4.1-1.

# Figure 4.4.1-1: Group message between MSGin5G UEs

The scenario consists of the following aspects:

-	all  in group can communicate with each other, which means the message sent by a MSGin5G UE will be received by all the other UEs in the group, either directly from MSGin5G server (if MSGin5G UEs) or via Message Gateway (if Non-3GPP UEs or Legacy 3GPP UE).

NOTE:	Group message between UE C and UE D is also supported when the group is hosted on 5G MSG Server.

### 4.4.2	Scenario 3.2: Group message between non-3GPP UEs and MSGin5G UEs

This scenario describes the case where non-3GPP UE1 (e.g. a mobile handset Terminal, or an application client APP 1 in a mobile handset Terminal 1) communicates with a group of UEs by using non-3GPP message (e.g. RCS message service specified in GSMA PRD RCC.07 [4]), and some of UEs in this group use MSGin5G service. All UEs in the group may be in different geographical area.

UE1 connect to a non-3GPP message server and then connected to MSGin5G server via Non-3GPP Message Gateway. All MSGin5G UEs connected the 5G system directly and served by MSGin5G server. The scenario is illustrated in figure 4.4.2-1.

NOTE:	The Non-3GPP Message Gateway facilitates the translation between the MSGin5G Service and non-3GPP message service. The application functional aspect and procedure in Non-3GPP Message Gateway will be studied.

# Figure 4.4.2-1: Message from non-3GPP Message Service to MSGin5G group

The scenario consists of the following aspects:

-	all UEs in group can communicate with each other, which means the message sent by a non-3GPP UE will be received by all the other 5 MSGin5G UEs in the group, and all the other MSGin5G UEs can send the message to a non-3GPP UE.

* * * Next Change * * * *

### 4.5.3	Scenario 4.3: Message broadcast from non-3GPP Message Service to MSGin5G UEs

This scenario describes the scenario where Non-3GPP UE1  (e.g. OMA LWM2M specified in OMA OMA-ERELD-LightweightM2M [5]) delivers a broadcast message by using non-3GPP Message service to MSGin5G UEs2 (e.g. a mobile handset terminal 1 or an application client APP 1 in a mobile handset Terminal 1)  to MSGin5G UEs2which is configured according to application policy.

MSGin5G UEs2 connected to 5G system and served by MSGin5G server. The MSGin5G message and non-3GPP message will be translated by the Non-3GPP Message Gateway. The scenario is illustrated in figure 4.5.3-1.

# Figure 4.5.3-1: Message broadcast from non-3GPP message service to MSGin5G UEs 2

The scenario consists of the following aspects:

-	If broadcast message is originated by authorized Non-3GPP UE1, the MSGin5G Server broadcasts the message to all the UEs. MSGin5G UEs may send the delivery status back to Non-3GPP UE1 or APP Server.

* * * Next Change * * * *

### 5.1.2	Identified Gaps

The following gaps have been identified to fulfill the delivery status acknowledgement:

-	The protocol requirements for delivery status acknowledgement and sending a delivery status acknowledgement shall be studied.

-	If delivery status acknowledgement is supported by the non-3GPP message service, the procedure of delivery status acknowledgement interworking in the Non-3GPP Message Gateway will be defined.

-	If delivery status acknowledgement is not supported by the non-3GPP message service, then if the Non-3GPP Message Gateway or MSGin5G server will send the delivery status acknowledgement on behalf of the non-3GPP UE needs to be defined.

* * * Next Change * * * *

### 5.3.2	Identified Gaps

The following gaps have been identified to fulfil the identifier requirements:

-	The IMSI/MSISDN or IMEI may not suitable to identify all kind of UEs, e.g. the applications in a mobile handset. The following studies are needed:

-	Whether the existing identifier(s) can fulfil the requirements.

-	Whether new identifier(s) is needed to be specified.

-	If the identifier(s) of UE is assigned by MSGin5G services, the procedure of generating, assigning and managing the identifier(s) are needed to be defined.

-	The procedure of managing both the MSGin5G identifiers(s) and identifier(s) of non-3GPP message services in Non-3GPP Message Gateway is needed to be defined.

* * * Next Change * * * *

### 5.5.1	Description

MSGin5G UE is a Controller UE that sends messages in MSGin5G message format to the MSGin5G Server.

Non-3GPP UE is a Controller UE that sends messages in a non-3GPP message format via the Non-3GPP Message Gateway to the MSGin5G Server.

The 5G Network provides data delivery methods over the control plane (i.e. via N1) and over the user plane (i.e. via N3). Application Servers access control plane and user plane data delivery features via N6 or via exposed APIs (e.g. T8 and Nnef).

* * * Next Change * * * *

### 5.6.1	Description

The MSGin5G Server supports messages in the MSGin5G message format and needs to be able to deliver messages to Non-3GPP UE type devices that do not support the MSGin5G message format, but support a non-3GPP message format.

The Non-3GPP Message Gateway acts as a gateway as shown in figure 5.6.1-1 and takes care of message delivery via the 5G System.

Figure 5.6.1-1 also shows message delivery (and reception) to Device E. Device E is a device that does not support the MSGin5G Service and is not connected to the 5G System but is connected to the MSGin5G Server, via the MSGin5G Inter-Working Function (IWF), but has otherwise similar capabilities and functionality as Non-3GPP UE has.

# Figure 5.6.1-1: Non-3GPP Message Gateway as gateway

The Non-3GPP Message Gateway needs to support the capability of message delivery to Non-3GPP UE in point-to-point, point-to-group and broadcast scenarios. The MSGin5G Server supports this same capability for delivery of messages to MSGin5G UE in the same scenarios.

### 5.6.2	Identified gaps

-	The interface between the MSGin5G Server and the Non-3GPP Message Gateway needs to be specified.

-	The interface between the MSGin5G Server and the MSGin5G IWF needs to be specified and it needs to be studied if the interface towards the Non-3GPP Message Gateway can be the same as the interface towards the MSGin5G IWF.

NOTE: Functionality of the Non-3GPP Message Gateway and MSGin5G IWF beyond the interface to the MSGin5G Server are out of scope of the study.

* * * Next Change * * * *

### 5.7.1	Description

The requirement of group message is specified in requirement [R-5.4.2-001] of 3GPP TS 22.262 [2]:

-	[R-5.4.2-001] The MSGin5G Service shall support group message communication, i.e. a UE sends a message to a group of UEs. All the members in a group can send messages. The UEs in a group can be located in different geographical areas.

The requirements of roaming and interconnection specified in 3GPP TS 22.262 [2] are also applied:

-	[R-8.2-001] The MSGin5G Service shall support a roaming UE sending and receiving messages.

-	[R-9.2-001] The MSGin5G Service shall support an UE within an operator sending a message to another UE within another operator.

The following conclusion can be made based on the requirements above:

-	The UEs in a group may locate in different PLMNs or roam to VPLMN.

According to requirement [R-5.1.2-007] of 3GPP TS 22.262 [2], non-3GPP message UE may also send and receive group message via MSGin5G Gateway (i.e. Non-3GPP Message Gateway in this TR).

Issues include:

-	How to support different UEs sending and receiving group message in an MGSin5G group. The UE may include MSGin5G UE located in HPLMN, MSGin5G UE located in VPLMN, MSGin5G UE interconnected from other PLMN and non-3GPP UE,

* * * Next Change * * * *

### 5.8.2	Identified Gaps

The following gaps have been identified to fulfil the identifier requirements:

-	Whether the existing mechanism, e.g. SEAL specified in 3GPP TS 23.434 [9] can fulfil the group management requirements specified in 3GPP TS 22.262 [2]. If gaps are identified, the following studies are needed:

-	The group information used for MSGin5G group management.

-	The procedures of MSGin5G group management.

-	The group management interworking in the Non-3GPP Message Gateway are needed to be defined.

-	Technical requirements caused by the characters of UEs are needed to be fulfilled.

-	UE may have the limitation of resource, some specified mechanism of managing the group data in the UE are needed.

-	Long latency may exist between UE and MSGin5G server due to the UE may be offline or in Power Saving Mode specified in 3GPP TS 23.682 [3]. The group data in the UE and the MSGin5G server may not be synchronized on time, so some abnormal scenarios are needed to be specified.

* * * Next Change * * * *

### 5.10.2	Identified Gaps

The following gaps have been identified to fulfil the identifier requirements:

-	What is broadcast area configuration information used for MSGin5G broadcast message.

-	How broadcast areas configuration related information can be used in the application layer.

-	The broadcast area configuration interworking in the Non-3GPP Message Gateway are needed to be defined.

* * * Next Change * * * *

### 5.15.1	Description

The key issue addresses message delivery from the MSGin5G Server to an end-point or to multiple end-points.

It is assumed that the MSGin5G Server is the only entity in the MSGin5G Service that is aware how messages need to be forwarded towards the various UEs that participate in the service and that only the MSGin5G Server has access to a broadcast function, an SMS delivery function in the 5GC, and to a Non-3GPP Message Gateway.

### 5.15.2	Identified Gaps

The following gaps are identified:

-	The MSGin5G Server needs to be able to forward messages to the requested end-point, based on UE types (determined by the Service ID).

-	The MSGin5G Server needs to be able to forward messages to a Group of UEs. The MSGin5G Server needs to forward the message to each of the Group members. Further details on the group message are described in Key Issue 7.

-	The MSGin5G Server needs to be able to forward messages to the broadcast function in the 5GC, so the message will be broadcast in a service area.

-	The MSGin5G Server needs to be able to forward messages to the Application Server. The Application Server may reside outside the 3GPP domain and may be connected through the NEF to 5GC.

-	The MSGin5G Server needs to be able to forward messages to the Non-3GPP Message Gateway for UEs that support a non-3GPP transport mechanism. Further details on message transfer to a Non-3GPP Message Gateway are described in Key Issue 6.

* * * Next Change * * * *

#### 6.5.1.6	Non-3GPP message client receives message from group

Figure 6.5.1.6-1 shows the procedure for Non-3GPP message client to receive message from group.

Pre-conditions:

1)	The MSGin5G server is aware of the UE type (determined by service ID) which is Non-3GPP message client.

2)	The MSGin5G server has received the message to send to target UE.

# Figure 6.5.1.6-1: Non-3GPP message client receives a message from the group

1)	The MSGin5G server sends the Group Message Request to the Non-3GPP Message Gateway. The information elements defined in Table 6.5.1.4-1 are included in the request.

2)	The Non-3GPP Message Gateway translates the MSGin5G message to Non-3GPP message.

3)	The Non-3GPP Message Gateway sends message to Non-3GPP Message Client.

NOTE:	The procedure to translate MSGin5G message to Non-3GPP message and to send Non-3GPP message from Non-3GPP Message Gateway to Non-3GPP Message Client are out of scope of 3GPP.

* * * Next Change * * * *

### 6.5.3	Solution evaluation

This procedure can be used by MSGin5G Client, Legacy-3GPP Client, Non-3GPP Message Gateway Function and MSGin5G Server to send and receive group message. This procedure can simplify the functional requirements for the MSGin5G Client and MSGin5G Server.

* * * Next Change * * * *

# Comments

To be modified