3GPP TSG-SA WG6 Meeting #40-e	S6-20xxxx

e-meeting, 16th – 24th November 2020	(revision of S6-202059)

Source:	Huawei, Hisilicon

Title:	Conclusion

Spec:	3GPP TR 23.700-24 v1.1.0

Agenda item:	8.5

Document for:	Approval

Contact:	Hongxia Hao, haohongxia@huawei.com

1. Introduction

This pCR is for adding some conclusions.

2. Reason for Change

3. Conclusions

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.1.0.

* * * First Change * * * *

## 10.1	Conclusions

The results from the study will be considered for follow-up normative work in Release 17 as follows:

Editor's Note: The conclusions listed below are used for early consideration. When more solutions are provided and analyses of these solutions are finished, the following conclusions are needed to be updated accordingly.

- The architecture requirements and UE definitions (in clause 8) will be considered as the basis for technical specification with necessary enhancements and additions;

- The solution (in Solution 8) for UE identifier will be used as the baseline solution for technical specification with necessary enhancements;

- The message reply from a Legacy 3GPP UE or Non-3GPP UE to a 5GMSGS UE in Solution 15 will be used as the baseline solution for technical specification with necessary enhancements.

- The solution (in Solution 18) for interconnection will be used as the baseline solution for technical specification with necessary enhancements;

- The solution 19 and solution 23 for MSGin5G Server to interact with Application Server will be used as the baseline solution for technical specification with necessary enhancements.

- As solution 13, if MSGin5G Server/Client receives a message payload from Application Server/Client and the message payload size exceeds the maximum allowed packet size (e.g. due to limitation by the UE's access network transport), the MSGin5G Server/Client should perform the message segmentation and re-assembly.

* * * Next Change * * * *

<Proposed change in revision marks>

* * * Next Change * * * *

<Proposed change in revision marks>