3GPP TSG-SA WG6 Meeting #40-e	S6-20xxxx

# e-meeting, 16th – 24th November 2020									            (revision of S6-202280)

| CR-Form-v12.0 |
| --- |
| CHANGE REQUEST |
|  | 23.286 | CR | 0027 | rev | 2 | Current version: | 16.4.0 |  |
| For HELP on using this form: comprehensive instructions can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: | UICC apps |  | ME |  | Radio Access Network |  | Core Network | X |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: | Support local MBMS |
| --- | --- |
| Source to WG: | Ericsson |
| Source to TSG: | S6 |
| Work item code: | eV2XAPP |  | Date: | 2020-10-30 |
| Category: | B |  | Release: | Rel-17 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) Rel-13 (Release 13) Rel-14 (Release 14) Rel-15 (Release 15) Rel-16 (Release 16) Rel-17 (Release 17) |
| Reason for change: | TR 23.764 sol#17 describes the local MBMS support in the V2X enabling layer. Such solution should be considered in the normative work. |
| Summary of change: | Add local MBMS support for V2X file distribution. |
| Consequences if not approved: | The V2X file distribution cannot utilize local MBMS delivery. |
| Clauses affected: | 2, 9.5.2 |
|  | Y | N |  |  |
| Other specs |  | N | Other core specifications | TS/TR ... CR ... |
| affected: |  | N | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | N | O&M Specifications | TS/TR ... CR ... |
| Other comments: |  |
| This CR's revision history: |  |

* * * First Change * * * *

# 2	References

The following documents contain provisions which, through reference in this text, constitute provisions of the present document.

-	References are either specific (identified by date of publication, edition number, version number, etc.) or non-specific.

-	For a specific reference, subsequent revisions do not apply.

-	For a non-specific reference, the latest version applies. In the case of a reference to a 3GPP document (including a GSM document), a non-specific reference implicitly refers to the latest version of that document in the same Release as the present document.

[1]	3GPP TR 21.905: "Vocabulary for 3GPP Specifications".

[2]	3GPP TS 22.185: "Service requirements for V2X services; Stage 1".

[3]	3GPP TS 22.186: "Enhancement of 3GPP support for V2X scenarios; Stage 1".

[4]	3GPP TS 23.280: "Common functional architecture to support mission critical services".

[5]	3GPP TS 23.285: "Architecture enhancements for V2X services".

[6]	3GPP TS 23.434: "Service enabler architecture layer for verticals; Functional architecture and information flows".

[7]	3GPP TS 23.468: "Group Communication System Enablers for LTE (GCSE_LTE); Stage 2".

[8]	3GPP TS 23.682: "Architecture enhancements to facilitate communications with packet data networks and applications".

[9]	3GPP TR 23.795: "Study on application layer support for V2X services".

[10]	3GPP TS 26.346: "Multimedia Broadcast/Multicast Service (MBMS); Protocols and codecs".

[11]	3GPP TS 26.348: "Northbound Application Programming Interface (API) for Multimedia Broadcast/Multicast Service (MBMS) at the xMB reference point".

[12]	3GPP TS 29.214: "Policy and Charging Control over Rx reference point".

[13]	3GPP TS 29.468: "Group Communication System Enablers for LTE (GCSE_LTE); MB2 Reference Point; Stage 3".

[14]	3GPP TS 36.300: " Evolved Universal Terrestrial Radio Access (E-UTRA) and Evolved Universal Terrestrial Radio Access Network (E-UTRAN); Overall description; Stage 2".

[15]	ETSI EN 302 637-3 (V1.3.1): "Intelligent Transport Systems (ITS); Vehicular Communications; Basic Set of Applications; Part 3: Specifications of Decentralized Environmental Notification Basic Service".

[16]	ETSI TS 102 894-2 (V1.2.1): "Intelligent Transport Systems (ITS); Users and applications requirements; Part 2: Applications and facilities layer common data dictionaryMultimedia Broadcast/Multicast Service (MBMS); Protocols and codecs".

[17]	ETSI TS 102 965 (V1.4.1): "Intelligent Transport Systems (ITS); Application Object Identifier (ITS-AID); Registration".

[18]	ISO TS 17419: "Intelligent Transport Systems - Cooperative systems - Classification and management of ITS applications in a global context".

[TS29116]	3GPP TS 29.116, "Representational state transfer over xMB reference point between Content Provider and BM-SC".

* * * Next Change * * * *

### 9.5.2	Use of MBMS "files" session type

The VAE server acts as a content provider and the VAE client acts as an MBMS client in the xMB reference model (subclause 4.1 in 3GPP TS 26.348 [11]).

The VAE server makes use of the xMB procedures from 3GPP TS 26.348 [11] to create MBMS sessions whose type is set to "files" and to request the delivery of files over these sessions. Before provisioning files to the BM-SC, the VAE server prepares the file for distribution, which may include partition of large files into smaller files or encryption.

The VAE server is responsible for translating the parameters related to the V2X application triggering the file delivery into corresponding xMB parameters. Table 9.5.2-1 describes the mapping between the V2X parameters and the xMB API properties specified in 3GPP TS 26.348 [11].

Table 9.5.2-1: Mapping between V2X parameters and xMB APIs

| V2X parameter | Corresponding xMB API property |
| --- | --- |
| File transfer session indicator | Session Type: Files |
| List of files to be sent by the VAE server and their locations | File List |
| Target geographical area for the V2X Ues | Geographical Area |
| Information about the V2X application (e.g., software update, HD map download) | Service Class |
| Maximum bitrate for the V2X application | Max Bitrate |
| Maximum delay for the V2X application | Max Delay |
| QoE metrics the VAE server is interested in receiving about the V2X application | QoE Reporting |
| Local MBMS information or local MBMS activation indication | Local MBMS information (NOTE) |
| NOTE: The local MBMS information as the xMB API property is defined in 3GPP TS 29.116 [TS29116]. |

NOTE:	The list of V2X parameters needed for file delivery is not exhaustive and can be updated based on the specific V2X application requirements.

* * * End of Change * * * *