3GPP TSG-SA WG6 Meeting #40-e	S6-20xxxx

e-meeting, 16th – 24th November 2020	(revision of S6-202249_was_202084)

Source:	Samsung

Title:	pCR on EEC executed ACR via T-EES

Spec:	3GPP TS 23.558

Agenda item:	7.6

Document for:	Approval

Contact:	Hyesung Kim <hs1207.kim@samsung.com>

1. Introduction

This pCR clarifies detail operations and information flows for application context relocation procedure executed by EEC via T-EES

2. Reason for Change

In the last meeting, it was agreed that target EES executed ACR relocation is revised to EEC-executed one via T-EES. According to this change, detailed operations and information flows for the EEC-executed ACR via T-EES needs to be aligned with the existing procedure of EEC executed application context relocation. To this end, the existing ACR request/response procedure between EEC and EES in clause 8.8.3.4 can be applied to the EEC-executed ACR via T-EES with minor modifications. Also, this pCR proposes information flows for ACR notification and complete message between T-EAS and T-EES.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TS 23.558 v1.1.0.

* * * First Change * * * *

#### 8.8.2.6	EEC executed application context relocation via T-EES

Figure 8.8.2.6-1 illustrates the procedure for the Edge Enabler Client to execute the application context relocation via target Edge Enabler Server.

Pre-condition:

1.	The PDU session to the target EDN where the target EES is located is available at the EEC.

2.	The EEC has the source EAS information that serves the AC.

Figure 8.8.2.6-1: EEC executed application context relocation via T-EES

1.	The EEC detects that application context relocation may be required as described in clause 8.8.1 and decides to proceed required procedures for application context relocation.

NOTE:	If supported, the AC can be involved in the decision. It is out of scope of the present document how the AC is involved.

2.	The EEC determines the T-EES by using the provisioned information or performing service provisioning procedure per clause 8.3. Upon selecting T-EES the UE may need to establish a new PDU connection to the target EDN. The EEC performs EAS Discovery with the T-EES per clause 8.5.2.

3.	The EEC sends the Application Context Relocation Request message with including source Edge Application Server information to indicate that the Application Context Relocation may be required.

4.	The T-EES may apply the AF traffic influence with the N6 routing information of the T-EAS in the 3GPP Core Network (if applicable), then sends the Application Context Relocation Notify message to the T-EAS.

5.	The T-EAS initiates application context transfer between the S-EAS and the T-EAS. This process is out of scope of the present specification.

6.	The T-EAS sends the Application Context Relocation Complete message to the T-EES to confirm that the application context relocation has completed.

7.	The T-EES sends the Application Context Relocation Response message to the EEC.

* * * Next Change * * * *

#### 8.8.4.2	Application Context Relocation request

Table 8.8.4.2-1 describes information elements for the Application Context Relocation request sent from the EEC either to the S-EES or T-EES.

Table 8.8.4.2-1: Application Context Relocation request

| Information element | Status | Description |
| --- | --- | --- |
| EEC ID | M | Unique identifier of the EEC. |
| Security credentials | M | Security credentials resulting from a successful authorization for the edge computing service. |
| UE identifier | M | The identifier of the UE (i.e. GPSI). |
| Target EAS Endpoint | M | Endpoint information (e.g. URI, FQDN, IP 3-tuple) of the target EAS. |
| DNAI of the target EAS | O | DNAI information associated with the target EAS. |
| EAS notification indication | M | Indicates whether to notify the EAS about the need of application context relocation. |
| Source EAS endpoint | O (NOTE) | Endpoint information of the source EAS |
| NOTE: This IE shall be present if the Application Context Relocation request message is sent form EEC to T-EES. |

Editor's note:	It is FFS whether additional N6 routing info (e.g. routing profile ID) is needed.

* * * Next Change * * * *