3GPP TSG-SA WG6 Meeting #40-e	S6-20xxxx

e-meeting, 16th – 24th November 2020	(revision of S6-202180, 2311, merge of 2099)

Source:	Huawei, Hisilicon, InterDigital, Vivo

Title:	Update to relationship between ETSI MEC and 3GPP EDGEAPP

Spec:	3GPP TS 23.558 v1.1.0

Agenda item:	7.6

Document for:	Approval

Contact:	Niranth (namogh@huawei.com)

1. Introduction

This contribution provides a proposal for update to relationship between ETSI MEC and 3GPP EDGEAPP.

2. Reason for Change

The relationship diagram in figure C.2-1 is causing confusion to the readers as there is no associated description.

There are ENs in Annex C also needs to be resolved.

3. Proposal

It is proposed to agree the following changes to 3GPP TS 23.558v1.1.0.

* * * First Change * * * *

Annex C (Informative):
Relationship with ETSI MEC architecture

## C.1	General

This clause shows an example for how the EDGEAPP architecture and ETSI ISG MEC architecture as specified in ETSI MEC 003 [15] can complement each other.

ETSI ISG MEC addresses aspects pertaining to MEC Application enablement through the MEC platform. Additionally, ETSI ISG MEC supports management and orchestration aspects for MEC components.

## C.2	Relationship between EDGEAPP and ETSI MEC architectures

Figure C.2-1 provides the relationship of ETSI ISG MEC architecture with EDGEAPP architecture.

Figure C.2-1: Relationship between EDGEAPP and ETSI MEC architectures

Details about MEC entities (MEC Platform, MEC Application, MEC Platform Manager, MEC Orchestrator, OSS and CFS) can be found in ETSI MEC 003 [15].

In ETSI MEC, MEC Applications and MEC Platform can expose services which can include network services, subject to their availability at the core or access network level.

Both EAS and MEC application are application servers and can provide the same application specific functionalities. Also the EAS and MEC application can be collocated in an implementation. Hence, they are grouped together as shown in the figure C.2-1

NOTE:	The details of the functionalities of application servers and alignment are implementation specific.

Both EES and MEC platform are edge platforms and provide application support capabilities towards the application servers. Also, the EES and MEC platform can be collocated in an implementation. Hence, they are grouped together as shown in the figure C.2-1. How EES and MEC platform are implemented or aligned is implementation specific. Likewise, alignment of the EDGE-3 and Mp1 reference points and EDGE-9 and Mp3 reference points is implementation specific.

The orchestration and management aspects of architecture for enabling edge applications are specified by 3GPP SA5 specification.