3GPP TSG-SA WG6 Meeting #40-e	S6-20xxxx

e-meeting, 16th – 24th November 2020	(revision of S6-202262)

Source:	Samsung, InterDigital

Title:	Pseudo-CR on Key issue on track UAV location deviation

Spec:	3GPP TR 23.755 0.11.0

Agenda item:	8.4

Document for:	Approval

Contact:	Basavaraj (Basu) Pattan, basavarajjp@samsung.com

1. Introduction

According to the requirements [R-5.1-012] and [R-5.1-013] of TS 22.125, one of the key functionality of the UTM is to track the UAV/UAV-C location. This contribution proposes new key issue to track the location deviation of the UAV.

Further analysis presented on SA6 conference call:

- Current Monitoring capabilities for detection abnormal UE

  - NEF exposes services for UTM to fetch UAV location information.

  - Support UTM in UAV tracking as per SA2 conclusion (TR 23.754, , KI#4, Solution #25).

  - SEAL offers location management service for UTM.

- Missing capabilities:

  - Support additional positioning methods by the enabler layer, as per UAS industry needs.

  - Leverage the enabler layer location information, in addition to the ones provided by the core network.

2. Reason for Change

New key issue proposed on flight path tracking

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.755 v0.11.0.

* * * NEW Proposal * * * *

## 5.Z	Key issue#Z: Track UAV location deviation

According to the requirements [R-5.1-012] and [R-5.1-013] of 3GPP TS 22.125 [3], one of the key functionalities of the UTM is to track the UAV/UAV-C location. Also, for “Automatic flight by UTM” control mode as mentioned in 3GPP TS 22.125 [3], it is required for UTM to track the UAV’s location. In order to achieve this, the USS/UTM needs to obtain UAV’s current location information periodically and process it to confirm the UAV’s location deviation.

NOTE: This key issue can be seen as an add-on to Key issue#3.

Hence, it is required to the study the following:

- Whether the existing location reporting capabilities in the UAE/SEAL are sufficient to enable the USS/UTM to monitor the UAV’s location deviation.

Editor’s note: The validity (i.e. potential deletion) and alignment of the gap related to location deviation due to the clarification of the source requirement from SA1 is FFS.

* * * End of Change * * * *