## Slide 1: Discussion on SA6 Service Layer and the Core Network Exposure APIs
Catalina Mladin, Convida Wireless

## Slide 2: Summary
CN service exposure functionality was designed to provide a standardized exposure of network services/capabilities and reduce the complexity of a variety of 3rd parties accessing different 3GPP CN functionality.
SA6 specifies common capabilities for a service enabler architecture in SEAL, in order to be utilized by multiple verticals and applications.

## Slide 3: What
A set of APIs for accessing CN services has been defined since Rel-15
What can the Service Layer and Applications do with the APIs?
Access internal capabilities of the core network
  Location
  Reachability ….
Assist services that are already in the core network
  Sleep
  Communication Patterns ….
Coordinate its activity with the core network
  Network Congestion Reports
  Schedule Background Data Transfer …
Exchange Small Data Packets
  SMS
  Non-IP
The Cellular Core Network already knows a lot about the device. Network Applications should leverage network services whenever possible (thus asking the device to do less).
Application Servers, together with the Service Layer, provide underlying network abstraction along with the services to the customer facing Application and Devices, e.g. data storage, device management, location services, data analytics, charging, discovery, etc.
.. so that Application Servers are enabled to provide Value–add functionality, e.g.:
Deal with long sleep times or long transmission delays.
pre-plan UE activity whenever possible (e.g. background data transfers).
etc.
Why

## Slide 4: How
By getting information from CN
The core network generally knows:
  where devices are located
  when they are in deep sleep
  when they are available
  when they lose connectivity
  when they are roaming
  when the SIM card is moved to another device
This is all information that Network Applications can get from the device.
However, we want to minimize signaling/messaging from the device.
It is more efficient to have Network Applications use Exposed Network Services to obtain this information.
By giving information to CN
The core network does not generally know:
  How often a device needs to be available
  how long it can buffer downlink data for sleeping device
  how much downlink data it should buffer for sleeping devices
This is all information that the Network can get from the device.
However, we want to minimize signaling/messaging from the device.
The Server can provide this information to the network

## Slide 5: Proposal +
Proposal: Ensure that the use of the 5GS northbound exposure interfaces is included in SEAL to prevent fragmented or inconsistent deployments or inconsistent use of 5GS capabilities.
The following slides provide:
  Technical background and usecases on the capabilities supported by 5GS northbound exposure

## Slide 6: Exposed Network Services (Location Queries)
Location Queries from Network Applications can be sent to the network instead of the devices.
The Server can get a list devices in a given area, without ever communicating with a device.
3GPP Network
NFs
API
Customer Facing Applications
(e.g. Fleet Management)
Service Layer
Server
SCEF/NEF
How many trucks are in the northeast section of the city?
Here is a list of discovered devices.

## Slide 7: Exposed Network Services (Change of SIM)
The network can notify Server when a SIM card is moved to another device.
The Server can react by requiring that that the device re-authenticate, by sending a technician to investigate, invalidating the device’s security credentials, etc.
3GPP Network
NFs
API
Customer Facing Applications
(e.g. Fleet Management)
Service Layer
Server
SCEF/NEF
Notification: SIM Card Moved

## Slide 8: Exposed Network Services (Long Sleep Cycles)
The Device and Network can negotiate a sleep schedule, but …
What happens if the Server is not involved in this negotiation?
Devices might not sleep enough
Devices might not stay awake long enough
Data from the device might not be available when the Server needs it
The SCEF/NEF exposes APIs that allow the Server to configure a device’s sleep parameters.
How long between wake-up events
How long to stay awake
Server
Device Available (Minutes)
Data Packet 1
Ack 1
Packets 2 and 3 are dropped
Packets 2 and 3 are retransmitted and dropped again
Device Available (Minutes)
Device Sleeping (Hours)
Data Packet 2
Data Packet 3
Data Packet 2
Data Packet 3
IoT Device (CAT-M, NB-IoT)

## Slide 9: Exposed Network Services (Long Sleep Cycles)
Once the length of the sleep time has been agreed, how does the Server know when the device is awake?
A conventional way of dealing with this is for the Device to send a “I am Awake” message to the Server every time it wakes up.
In many cases, it is very inefficient to do this.
  The Server may have nothing to say.
Server
Device Available (Minutes)
IoT Device (CAT-M, NB-IoT)
Data Packet 1
Ack 1
Device sends notification, the Server sends commands
I am Awake
I am Awake
Device sends notification, the Server has no pending commands
Device Available (Minutes)
Device Sleeping (Hours)

## Slide 10: Exposed Network Services (Reachability Notifications)
Instead of requiring the Device to indicate to the Server that it is awake, the core network can send a wake-up indication to the Server.
In many cases, there will be no need for the device to communicate with the Server after a wake-up event.
Mobile Core Network (SCEF/NEF)
Server
Device Available (Minutes)
Device Available (Minutes)
Device Sleeping (Hours)
IoT Device (CAT-M, NB-IoT)
Data Packet 1
Ack 1
Device is Awake
Device is Awake
Notifications come from the core network instead of the device

## Slide 11: Exposed Network Services (Buffering)
The core network offers a buffering service for downlink data. The Server configures:
How many packets to buffer
How long to buffer
If not properly configured….
Retransmissions may be buffered and delivered (duplicate packets) or
Packets may be dropped (lost packets).
Transport and Application Layer Retransmission Timers need to be tuned.
Mobile Core Network (SCEF/NEF)
IoT Network Application/Server
Device Available (Minutes)
Device Available (Minutes)
Device Sleeping (Hours)
In Network Buffering
Device
Buffer Config
Data Packet 1
Ack 1
Data Packet 2
Data Packet 2 (Retransmit)
Ack 2

## Slide 12: Exposed Network Services (NIDD)
Coordination between the Core Network and Server
The core network knows when it is experiencing congestion in particular geographical areas.
The Server knows when it wants to communicate with devices that are in a particular geographical area.
The Server can coordinate its activity with a Network Service and avoid times of congestion.
Background Data Transfer and Network Status Reports
3GPP Network
NFs
API
Customer Facing Applications
(e.g. Fleet Management)
Service Layer
Server
SCEF/NEF