3GPP TSG-SA WG6 Meeting #42-e	S6-210485

e-meeting, 1st – 9th March 2021	(revision of S6-21xxxx)

Source:	China Mobile

Title:	Pesudo-CR on non-MSGin5G UE Configuration

Spec:	3GPP TR 23.700-24 v1.3.0

Agenda item:	8.4

Document for:	Approval

Contact:	liuyueyjy@chinamobile.com

# 1. Introduction

A new solution addressing non-MGSin5G UE configuration.

# 2. Reason for Change

Contribute a new solution addressing non-MGSin5G UE configuration.

# 3. Conclusions

<Conclusion part (optional)>

# 4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.3.0.

* * * First Change * * * *

### 6.8.5b	non-MSGin5G UE identity (non-MSGin5G UE ID)

The non-MSGin5G UE ID is a unique identifier that represents the non-MSGin5G UE. A non-MSGin5G UE ID is associated with a specific non-MSGin5G UE. The format of non-MSGin5G UE ID may differ among different VALs. The non-MSGin5G ID may be pre-configured to the non-MSGin5G UE by its vendor.

* * * Next Change * * * *

## 6.X	Solution X: non-MSGin5G UE Configuration

### 6.X.1	Description

#### 6.X.1.1	General

When a non-MSGin5G UE (such as a legacy 3GPP UE or a non-3GPP UE) connects to the Message Gateway (such as a Legacy-3GPP Message Gateway or a non-3GPP Message Gateway) first time (e.g. a non-MSGin5G UE sends a message to a MSGin5G UE or a Application Server which uses MSGin5G Service), the non-MSGin5G Message Gateway records the non-MSGin5G UE ID and performs the configuration procedure on behalf of the non-MSGin5G UE to get the MSGin5G Service configuration information (e.g. MSGin5G Service ID).  the MSGin5G Service configuration information is needed to be used in the future messaging communication.

#### 6.X.1.2	non-MSGin5G UE configuration

The configuration procedures may re-use VAL UE configuration data specified in TS 23.434 [9] as described in this solution. After the configuration procedure, the non-MSGin5G Gateway can register to MSGin5G Server on behalf of the Non-MSGIn5G UE with the MSGin5G Service ID got from the configuration procedure.

In the non-MSGin5G UE configuration procedure, the non-MSGin5G Message Gateway acts as Configuration management client specified in 3GPP TS 23.434 [9] on behalf of each non- MSGin5G UE.

The following steps of configuration management service may apply for the non-MSGin5G Message Gateway:

-	Get VAL UE configuration request specified in subclause 11.3.2.1 of 3GPP TS 23.434 [9];

-	Get VAL UE configuration response specified in subclause 11.3.2.2 of 3GPP TS 23.434 [9];

The usage of the above information flows are clarified as below:

-	The VAL UE ID is the non-MSGin5G UE ID plus GW service ID;

-	The VAL user ID is the MSGin5G service identifier assigned to the non-MSGin5G UE specified in clause 6.8;

-	The VAL service ID is the service identifier of MSGin5G Service;

Besides the IEs specified in subclause 11.3.2.1 of 3GPP TS 23.434 [9], the information in table 6.X.1.2-1 is also included in the Get VAL UE configuration request.

# Table 6.X.1.2-1: Additional Information in the  Get VAL UE configuration request

| Information element | Status | Description |
| --- | --- | --- |
| Non-MSGin5G UE information | O | Other information needed by the configuration procedure.(NOTE) |
| NOTE1: The information can be the device type, device Vendor, etc. It is specified by application provider or MSGin5G service provider and is out of scope of this document. The MSGin5G service provider can configure the non-MSGin5G UE with different configuration data based on this IE. E.g. all sensors can be configured to a same MSGin5G Server. |

-	Besides the IEs specified in subclause 11.3.2.2 of 3GPP TS 23.434 [9]. The information in table 6.X.1.2-2 is also included in the Get VAL UE configuration response as a part of VAL UE configuration data.

# Table 6.X.1.2-2: Additional information in the Get VAL UE configuration response

| Information element | Status | Description |
| --- | --- | --- |
| MSGin5G service ID | M | MSGin5G service ID assigned to the requesting non-MSGin5G UE. |
| MSGin5G Server | M | The MSGin5G Server which serves this MSGin5G UE. |
| MSGin5G service specified information | O | The specific information of the MSGin5G Service specified by the MSGin5G Service Provider. (NOTE) |
| NOTE1: e.g. the segment size of MSGin5G Message in this Service Provider, The detailed definition is out of scope of this document. |

The following additional functional requirement is needed to be added to the Configuration Management Server:

-	The MSGin5G Configuration Function checks whether the non-MSGin5G UE ID (i.e. VAL UE ID) is included in a former Get VAL UE configuration request. If so, the MSGin5G Configuration Function included the MSGin5G Service ID assigned to the non-MSGin5G UE in the former configuration procedure as a part of VAL UE configuration data, otherwise a new MSGin5G Service ID is assigned to the non-MSGin5G UE, and included in the  VAL UE configuration data. Then the MSGin5G Configuration Function processes the configuration request according to the service policy.

### 6.X.2	Solution Evaluation

This solution provides a non-MSGin5G UE configuration procedures. The non-MSGIn5G UE may use this solution to obtain MSGin5G Service ID which is mandatory for the future messaging communication.

* * * Next Change * * * *

<Proposed change in revision marks>