3GPP TSG-SA WG6 Meeting #42-e	S6-210456

e-meeting, 1st – 9th March 2021

# Source:	China Mobile

# Title:	New SID for Network Slice Capability Exposure for Application Layer Enablement

# Document for:	Approval

Agenda Item:	9

3GPP™ Work Item Description

Information on Work Items can be found at http://www.3gpp.org/Work-Items 
See also the 3GPP Working Procedures, article 39 and the TSG Working Methods in 3GPP TR 21.900

# Title: 	Study on Network Slice Capability Exposure for Application Layer Enablement

## Acronym: FS_NSCALE

## Unique identifier: 	{A number to be provided by MCC at the plenary}

Potential target Release: Rel-18.

## 1	Impacts

| Affects: | UICC apps | ME | AN | CN | Others (specify) |
| --- | --- | --- | --- | --- | --- |
| Yes |  | X |  | X |  |
| No |  |  | X |  |  |
| Don't know | X |  |  |  | X |

## 2	Classification of the Work Item and linked work items

### 2.1	Primary classification

|  | Feature |
| --- | --- |
|  | Building Block |
|  | Work Task |
| X | Study Item |

### 2.2	Parent Work Item

| Parent Work / Study Items |
| --- |
| Acronym | Working Group | Unique ID | Title (as in 3GPP Work Plan) |

### 2.3	Other related Work Items and dependencies

| Other related Work Items (if any) |
| --- |
| Unique ID | Title | Nature of relationship |
| 850010 | Study on enhancement of network slicing; Phase 2 | SA2’s works about key issues and solutions on enhancement of network slicing |
| 860022 | Study on network slice management enhancement | SA5’s works about network slice management enhancement |
| 760065 | Provisioning of network slicing for 5G networks and services | SA5’s works about management services, and procedures for provisioning of 5GS including network slice |
| 900024 | Enhanced Service Enabler Architecture Layer for Verticals | SA6’s work about service enabler architecture layer which contains Network Slice Enablement. |

## 3	Justification

Network slicing is the key technology for differentiated network requirements of vertical industries. SA1 defines the relevant requirements of the open network slicing capability API for trusted third parties in TS 22.261 section 6.10, including the need to support the creation, modification, and deletion of slices, support the definition and update of slice capabilities, and support slice-related UE and service information configuration

Based on these requirements, for network slice capability exposure, both SA2 and SA5 have related directions. SA5 has already defined support of the exposure capability of MnS related to slices. For example, TS 28.531 specifies use cases, requirements, management services, and procedures for provisioning of network slice, including Provisioning exposure for NSI, Provisioning data report exposure. TS 28.532 specifies the stage 2 and stage 3 of generic management services for network slice. SA5 has not yet decided which APIs and if APIs could be exposed to third party applications. SA6 is supposed to output the requirements from verticals and coordinate with SA5.

SA2 has defined some slice related abilities at UE/session level in TS23.501.

- In clause 5.15, it describes the features and high level function of network slice, including slice configuration, mapping;

The solutions and procedures of slice related capabilities exposure in SA2 is under study in TR 23.700-40, for example,

- Key issue #4 "Support for network slice quota event notification in a network slice", studies on the mechanism of network slice exposure, which is NEF enhancement in the view of SA2.

- In clause 6.23, it studies the question “whether and how an AF can request event notifications from 5GS and be notified by 5GS on quotas on network slice related attributes”,

- In section6.19.3.4, it studies the procedure about AF requirement on “analytics information exposure of network slice quota via NEF by invoking the Nnef_AnalyticsExposure_Subscribe service”,

- Quoting from section6.9.1, ”A network slice customer (e.g. vertical) can determine an "action" (e.g. limitation) to be applied in the 5GS upon exceeding a particular quota",

In short, after receiving those “analytics information”, “provisioning data report” and “event notification”, which “action” should verticals take is in SA6’s scope.

Besides these existing initiatives, there exists gaps between management of network slices and their utilization by the vertical applications. Specifically to support end-to-end network services, application layer and network layer need to coordinate (e.g. related modification of resource or policies).

Therefore, there’s a clear gap in supporting network slice capability for vertical applications. Possible functional entities, procedures, and APIs involved in the opening of network slicing capabilities need to be clearly defined, and how to combine the vertical application enabling architecture already defined by SA6 with network capabilities exposure requires further study.

Further, in the study of eSEAL, “The support of SEAL services based and complementing on existing Core Network capabilities, e.g. Network Exposure Function (NEF);” has been concluded in the WID objective, but for the full supporting of network slice capability exposing, services for management aspects have not been concluded in any existing studies in SA6.

## 4	Objective

The SA6 objectives include the following:

- To study how SA6 enablement layer can invoke network slicing API offered by SA2 and SA5. Based on use cases and requirements of network slice capability exposure, analyze and investigate the services and functions of current SA6 enablement layer that require access to control and management plane aspects from SA2 and SA5 pertaining to network slicing (e.g. SEAL and vertical application enablers).

- Identify possible gaps in APIs exposed by the control and management planes and liaise with SA2 and SA5 as appropriate.

- Identify potential enhancements to SEAL, as an entity invoking control and management APIs pertaining to network slicing.

NOTE: The study will not study topics addressed in SA2 and SA5, and needs to closely coordinate with SA5 for the management aspects exposure and SA2 for NEF exposure capability utilization.

## 5	Expected Output and Time scale

| New specifications {One line per specification. Create/delete lines as needed} |
| --- |
| Type | TS/TR number | Title | For info at TSG# | For approval at TSG# | Rapporteur |
| TR | xx | Study on Enabler Layer Support Network Slice Capability Exposure for Vertical Application Layer Enablement | SA#94(Dec 2021) | SA#95(Mar 2022) | zheng, Shaowen, CMCC, zhengshaowen@chinamobile.com |

| Impacted existing TS/TR {One line per specification. Create/delete lines as needed} |
| --- |
| TS/TR No. | Description of change | Target completion plenary# | Remarks |

## 6	Work item Rapporteur(s)

Zheng, Shaowen, CMCC, zhengshaowen@chinamobile.com

## 7	Work item leadership

SA6

## 8	Aspects that involve other WGs

SA2 for core network architecture aspects, SA3 for security aspects, SA5 for slicing management aspects.

## 9	Supporting Individual Members

Supporting IM name

CMCC

Huawei

Caltta

China Unicom

Lenovo

Motorola Mobility

CATT

CAICT

Tencent

InterDigital

Convida Wireless

ZTE