3GPP TSG-SA WG6 Meeting #42-e	S6-210381

e-meeting, 1st – 9th March 2021	(revision of S6-21xxxx)

Source:	InterDigital, Samsung

Title:	Pseudo-CR on removal of Editor’s note for KI#12

Spec:	3GPP TR 23.755 v1.1.0

Agenda item:	8.3

Document for:	Approval

Contact:	Atle Monrad, <atle dot monrad at interdigital dot com>

1. Introduction

The KI#12 in 3GPP TR 23.755 has an Editor’s Note on validity and alignment of the gap related to location deviation due to the clarification of the source requirement from SA1.

2. Conclusions

It is proposed that this Editor’s note is removed, as the topic is valid for SA6 to study.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.755 v 1.1.0.

* * * First Change * * * *

## 5.12	Key issue#12: Track UAV location deviation

According to the requirements [R-5.1-012] and [R-5.1-013] of 3GPP TS 22.125 [3], one of the key functionalities of the UTM is to track the UAV/UAV-C location. Also, for "Automatic flight by UTM" control mode as mentioned in 3GPP TS 22.125 [3], it is required for UTM to track the UAV's location. In order to achieve this, the USS/UTM needs to obtain UAV's current location information periodically and process it to confirm the UAV's location deviation.

NOTE:	This key issue can be seen as an add-on to Key issue#3.

Hence, it is required to the study the following:

-	Whether the existing location reporting capabilities in the UAE/SEAL are sufficient to enable the USS/UTM to monitor the UAV's location deviation.

* * * End-of-Changes * * * *