## Slide 1: Discussion on SA6 Service Layer and the Core Network Exposure APIs
Catalina Mladin, Convida Wireless

## Slide 2: Summary
CN service exposure functionality was designed to provide a standardized exposure of network services/capabilities and reduce the complexity of a variety of 3rd parties accessing different 3GPP CN functionality.
SA6 specifies common capabilities for a service enabler architecture in SEAL, in order to be utilized by multiple verticals and applications.
R1 provides:
  Discussion on:
    What exposure functions need SEAL services
    Is this re-exposing via SEAL?
    What about cases when application data influences CN
  Slides with references for existing CN Exposure work (at the end)
  Proposal update

## Slide 3: What
A set of APIs for accessing CN services has been defined since Rel-15
What can the Service Layer and Applications do with the APIs?
Access internal capabilities of the core network
  Location
  Reachability ….
Assist services that are already in the core network
  Sleep
  Communication Patterns ….
Coordinate its activity with the core network
  Network Congestion Reports
  Schedule Background Data Transfer …
Exchange Small Data Packets
  SMS
  Non-IP
The Cellular Core Network already knows a lot about the device. Network Applications should leverage network services whenever possible (thus asking the device to do less).
Application Servers, together with the Service Layer, provide underlying network abstraction along with the services to the customer facing Application and Devices, e.g. data storage, device management, location services, data analytics, charging, discovery, etc.
.. so that Application Servers are enabled to provide Value–add functionality, e.g.:
Deal with long sleep times or long transmission delays.
pre-plan UE activity whenever possible (e.g. background data transfers).
etc.
Why

## Slide 4: How
By getting information from CN
The core network generally knows:
  where devices are located
  when they are in deep sleep
  when they are available
  when they lose connectivity
  when they are roaming
  when the SIM card is moved to another device
This is all information that Network Applications can get from the device.
However, we want to minimize signaling/messaging from the device.
It is more efficient to have Network Applications use Exposed Network Services to obtain this information.
By giving information to CN
The core network does not generally know:
  How often a device needs to be available
  how long it can buffer downlink data for sleeping device
  how much downlink data it should buffer for sleeping devices
This is all information that the Network can get from the device.
However, we want to minimize signaling/messaging from the device.
The Server can provide this information to the network

## Slide 5: SEAL & exposure functions
Assumption: There is no need to justify usecases that the functionality provided by the exposure functions (e.g.in 23.682) is required at SCS/AS/AFs.
All SCEF/NEF APIs are currently exposed to AS. Therefore, exposure functionality in SEAL is useful when:
    When AS implementation simplification and to abstraction are needed - more than one vertical or “general purpose” AS
    When optimizations/services to the CN needed or when AS influence CN functionality
    When PLMN operator service agreement is preferred at SEAL provider level
    For all cases, the choice of using the SCEF/NEF APIs directly by VAL Servers is always open!

## Slide 6: a. Exposure services across verticals
Example: Smart City platform which may include:
  V2X, FFApp, but also..
  IoT, Media, etc. … and may include
  Edge deployments
If several VAL servers in this deployment use location, group functionality from SEAL server, why should they implement those that require more CN knowledge?
Currently, if an AS needs no SA6 SL services, it can use capability exposure directly. Why would it use CAPIF exposure?
    Assumption: other SL services are being used, which justifies the use of CAPIF.
    By exposing via SEAL, we have the option of providing some value-add services. At a minimum, these services are optimizations for multiple verticals.

## Slide 7: b. CN resource optimizations or CN functional influence
Network Configuration Parameters Provisioning, some monitoring, change of chargeable party, CP provisioning, etc. influence CN functionality or require CN resources.
Being able to rely upon SEAL implementation of functionality not only simplifies VAL server, but ensures that CN influence is optimized.

## Slide 8: c. Service agreement is preferred at SEAL provider level
Example: background data transfer
  Usecase is in SEES WID
  pre-provisioned info about BDT policy is required (i.e. reference to a charging rate)
  We don’t want that pre-provisioning to be needed for each AS, if they belong to a common SEAL platform
  We want the SEAL to be able to perform BDT management as “group management” – UE groups, BDT window grouping, etc.

## Slide 9: Proposal
Proposal: Enable SEAL services based on 5GS northbound exposure interfaces.
  To narrow scope:
    Start with features introduced by SEES and AESE, e.g. enabling IoT platforms
    Use criteria such as
      When AS implementation simplification and to abstraction are needed - more than one vertical or “general purpose” AS
      When optimizations/services to the CN needed or when AS influence CN functionality
      When PLMN operator service agreement is preferred at SEAL provider level
  Requirements: 22.101 clause 29. Additional/specific requirements can be captured as part of TR work, to be merged into the eSEAL TS, similarly to location or group management sections
NOTE: The following slides provide technical background and usecases on the SOME capabilities supported by 5GS northbound exposure

## Slide 10: Exposed Network Services (Location Queries)
Location Queries from Network Applications can be sent to the network instead of the devices.
The Server can get a list devices in a given area, without ever communicating with a device.
3GPP Network
NFs
API
Customer Facing Applications
(e.g. Fleet Management)
Service Layer
Server
SCEF/NEF
How many trucks are in the northeast section of the city?
Here is a list of discovered devices.

## Slide 11: Exposed Network Services (Change of SIM)
The network can notify Server when a SIM card is moved to another device.
The Server can react by requiring that that the device re-authenticate, by sending a technician to investigate, invalidating the device’s security credentials, etc.
3GPP Network
NFs
API
Customer Facing Applications
(e.g. Fleet Management)
Service Layer
Server
SCEF/NEF
Notification: SIM Card Moved

## Slide 12: Exposed Network Services (Long Sleep Cycles)
The Device and Network can negotiate a sleep schedule, but …
What happens if the Server is not involved in this negotiation?
Devices might not sleep enough
Devices might not stay awake long enough
Data from the device might not be available when the Server needs it
The SCEF/NEF exposes APIs that allow the Server to configure a device’s sleep parameters.
How long between wake-up events
How long to stay awake
Server
Device Available (Minutes)
Data Packet 1
Ack 1
Packets 2 and 3 are dropped
Packets 2 and 3 are retransmitted and dropped again
Device Available (Minutes)
Device Sleeping (Hours)
Data Packet 2
Data Packet 3
Data Packet 2
Data Packet 3
IoT Device (CAT-M, NB-IoT)

## Slide 13: Exposed Network Services (Long Sleep Cycles)
Once the length of the sleep time has been agreed, how does the Server know when the device is awake?
A conventional way of dealing with this is for the Device to send a “I am Awake” message to the Server every time it wakes up.
In many cases, it is very inefficient to do this.
  The Server may have nothing to say.
Server
Device Available (Minutes)
IoT Device (CAT-M, NB-IoT)
Data Packet 1
Ack 1
Device sends notification, the Server sends commands
I am Awake
I am Awake
Device sends notification, the Server has no pending commands
Device Available (Minutes)
Device Sleeping (Hours)

## Slide 14: Exposed Network Services (Reachability Notifications)
Instead of requiring the Device to indicate to the Server that it is awake, the core network can send a wake-up indication to the Server.
In many cases, there will be no need for the device to communicate with the Server after a wake-up event.
Mobile Core Network (SCEF/NEF)
Server
Device Available (Minutes)
Device Available (Minutes)
Device Sleeping (Hours)
IoT Device (CAT-M, NB-IoT)
Data Packet 1
Ack 1
Device is Awake
Device is Awake
Notifications come from the core network instead of the device

## Slide 15: Exposed Network Services (Buffering)
The core network offers a buffering service for downlink data. The Server configures:
How many packets to buffer
How long to buffer
If not properly configured….
Retransmissions may be buffered and delivered (duplicate packets) or
Packets may be dropped (lost packets).
Transport and Application Layer Retransmission Timers need to be tuned.
Mobile Core Network (SCEF/NEF)
IoT Network Application/Server
Device Available (Minutes)
Device Available (Minutes)
Device Sleeping (Hours)
In Network Buffering
Device
Buffer Config
Data Packet 1
Ack 1
Data Packet 2
Data Packet 2 (Retransmit)
Ack 2

## Slide 16: Exposed Network Services (NIDD)
Coordination between the Core Network and Server
The core network knows when it is experiencing congestion in particular geographical areas.
The Server knows when it wants to communicate with devices that are in a particular geographical area.
The Server can coordinate its activity with a Network Service and avoid times of congestion.
Background Data Transfer and Network Status Reports
3GPP Network
NFs
API
Customer Facing Applications
(e.g. Fleet Management)
Service Layer
Server
SCEF/NEF

## Slide 17: CN exposure- existing 3GPP work
WIDs:
SEES (Service Exposure and Enablement Support) (rel-13) SP-130505
AESE (rel-13) SP-140704
  Under Release 13 Features on Internet of Things (IoT)
  Features implemented using SCEF
  Related specs:
    Stage1: 22.853
    Stage 2: TR 23.708, TS 23.621
    Stage 3: TS 29.122 (T8; SCEF-AS)

## Slide 18: CN exposure- existing 3GPP work
In 5G:
  Features implemented using NEF
  Related specs:
    Stage 2: TS 23.502
    Stage 3: TS 29.522 (Nnef)
  “NEF is integrated with SCEF as a combined SCEF+NEF” (23.502, clause 5.2.6.12)
  “Procedure {xyz} as described in 29.122 shall be applicable in 5GS with […] description of SCEF applies to NEF” (29.522 clause 4.4)
    {xyz} applies to: Monitoring, Device triggering, Background Data Transfer, CP Parameter Provisioning, PFD Management, changing the chargeable party, AF session with required QoS, MSISDN-less Mobile Originated SMS, Network Configuration Parameters Provisioning, NIDD, RACS Parameter Provisioning, Enhanced Coverage Restriction Control