3GPP TSG-SA WG6 Meeting #42-e	S6-210462

e-meeting, 1st – 9th March 2021	(revision of S6-21xxxx)

Title:	Reply LS on clarification regarding EEC ID

Response to:	LS (S3-203339 / S6-210376) on clarification regarding EEC ID

Release:	Release 17

Work Item:	EDGEAPP

Source:	SA6

To:	SA3

Cc:	CT1, CT3

Contact Person:

Name:	Wenliang Xu

Tel. Number:

E-mail Address:	wenliang.xu@ericsson.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

SA6 would like to thank SA3 for their LS in S3-203339 / S6-210376.

Q1: Is the EEC ID globally unique across different UEs? Or can several UEs have the same EEC ID?

A1: EEC ID is globally unique across different UEs.

Q2: Who is responsible for generating the EEC ID? How is the EEC ID configured into the EEC?

A2: The EEC ID may be generated by a function module in the UE (e.g. application installer). The method is outside the scope of TS 23.558.

Q3: What is the format of the EEC ID?

A3: The detailed format of the EEC ID will be decided by CT group(s).

In addition, SA6 would like to express the following view for EEC ID:

The EEC ID is introduced to identify the EEC software in the UE and it is an application level identifier, TS 23.558 has specified procedures in Edge-1 & 4 requiring EEC ID to be included as part of the EEC request. It is expected that the ECS/EES should be able to authorize EEC before service invocation.

2. Actions:

To SA3:

ACTION: 	SA6 kindly requests SA3 to take the above information into account.

3. Date of Next TSG-SA6 Meetings:

SA6#42-bis-e   12th – 20th April 2021 	e-meeting

SA6#43-e          24th May – 2nd June 2021 	e-meeting