3GPP TSG-SA WG6 Meeting #42-e	S6-210568

e-meeting, 1st – 9th March 2021	(revision of S6-21xxxx)

Source:	CATT

Title:	Pseudo-CR on solutions for 5GS resource control

Spec:	3GPP TR 23.783 v1.1.0

Agenda item:	8.1

Document for:	Approval

Contact:	Ling Zhang, zhangling@catt.cn

1. Introduction

Tihs contribution provides additional solutions for 5GS resource control.

2. Reason for Change

The solutions address how the 5G QoS new functionalities are supported for MC service sessions, which includes:

- AF session with required QoS;

- QoS Monitoring to assist URLLC Service;

- QoS capability exposure by NEF.

3. Proposal

It is proposed to agree the following changes to 3GPP TR 23.783 v1.1.0.

* * * First Change * * * *

#### 6.3.1.x	Request for unicast resources at session establishment using AF session with required QoS

The procedure is applied to SIP based MC service sessions (e.g. MCPTT, MCVideo). In the procedure the SIP core interacts with 5GC for setting up QoS control and resource allocation.

The procedure in figure 6.3.1.x illustrates the originating side of the request for unicast resource at session establishment using AF session with required QoS procedure (as defined in 3GPP TS 23.502 [11] and 3GPP TS 23.503 [12]). For the terminating side the MC service server, SIP core and 5GS use similar approaches (step 3 to step 8) for resource reservation for downlink resources.

Figure 6.3.1.x-1: Request for unicast resources at session establishment using AF session with required QoS (originating side)

1.	MC service client sends a call/session establishment request. The request carries the QoS requirements (e.g. one or more QoS reference parameters) and necessary information (e.g. UE’s IP address) that can be further used for setting up an AF session for the MC service with 5GS.

2.	MC service server evaluates the QoS requirements for the MC service call/session. The MC service server may decide on a different QoS than requested for the call/session.

3.	MC service server send a session progress request to the SIP core containing the QoS requirements in SDP offer.

4.	The SIP core reserves resources for the call/session by setting up an AF session with required QoS procedure as defined in 3GPP TS 23.502 [11] subclause 4.15.6.6 and 3GPP TS 23.503 [12] subclause 6.1.3.22.

NOTE:	If the SIP core is not trusted by 5GC/PCF (e.g. it belongs to a third party ASP), it only interacts with NEF (performs Nnef_AFsessionWithQoS services) to request resource with a specific QoS. If the SIP core is trusted to 5GC/PCF, it may interact directly with PCF (performs Npcf_PolicyAuthorization services) for the policy control.

5.	The SIP core forwards session progress request to the MC service client.

6.	The MC service client acknowledges the session progress request with an OK message.

7.	The SIP core forwards the OK message to the MC service server.

8.	The MC service call/session is established and resources have been allocated.

* * * Next Change * * * *

#### 6.3.1.y	Request for unicast resource update in ongoing session using AF session with required QoS update

The procedure is applied to SIP based MC service sessions (e.g. MCPTT, MCVideo). In the procedure the SIP core interacts with 5GC for QoS update and resource modification.

The procedure in figure 6.3.1.y illustrates the request for unicast resource update using AF session with required QoS update procedure (as defined in 3GPP TS 23.502 [11] and 3GPP TS 23.503 [12]) for ongoing sessions.

Figure 6.3.1.y-1: Request for unicast resource update in ongoing session using AF session with required QoS update

0.	The MC service call/session using unicast is ongoing.

1.	MC service server decides to update the QoS parameters of the session (e.g. upon a request to upgrade the existing MC service call to an MC service emergency or imminent threat call, receiving the QoS notification indicating the QoS target can be no longer fulfilled, etc.).

2.	MC service server sends a session update to the SIP core which contains the alternative service requirements or QoS information that can be further derived to alternative QoS parameters at 5GS.

3.	The SIP core initiates AF session with QoS update procedure with 5GS as defined in 3GPP TS 23.502 [11] subclause 4.15.6.6a and 3GPP TS 23.503 [12] subclause 6.1.3.22.

NOTE:	If the SIP core is not trusted by 5GC/PCF (e.g. it belongs to a third party ASP), it only interacts with NEF (performs Nnef_AFsessionWithQoS Update services) to request QoS update. If the SIP core is trusted to 5GC/PCF, it may interact directly with PCF (performs Npcf_PolicyAuthorization Update services) for the policy update.

4.	The SIP core forwards the session update request to the MC service client.

5.	The MC service client acknowledges the request with an OK message.

6.	The SIP core forwards the OK message to the MC service server.

7.	The MC service call/session continues with the udated unicast resources.