3GPP TSG-SA WG6 Meeting #42-e	S6-210xxx

e-meeting, 1st – 9th March 2021	(revision of S6-210589)

Source:	Huawei, Hisilicon

Title:	FS_5GMARCH Conclusions on UE registration

Spec:	3GPP TR 23.700-24

Agenda item:	8.4

Document for:	Approval

Contact:	Hongxia Hao, haohongxia@huawei.com

1. Introduction

This pCR is a suggestion on conclusions about UE registration.

2. Reason for Change

To add some conclusions about UE registration.

About MSGin5G UE, solution 27 can make sure the provisioned service ID is permanent, but solution 2 cannot make sure the generated service ID is permanent, it’s lack of the procedures on how to ensure the generated service ID permernant/static.

3. Conclusions

<Conclusion part (optional)>

4. Proposal

It is proposed to agree the following changes to 3GPP TR 23.700-24 v1.3.0.

* * * First Change * * * *

## 10.1	Conclusions

The results from the study will be considered for follow-up normative work in Release 17 as follows:

Editor's Note: The conclusions listed below are used for early consideration. When more solutions are provided and analyses of these solutions are finished, the following conclusions are needed to be updated accordingly.

1)	The architecture requirements and UE definitions (in clause 8) will be considered as the basis for technical specification with necessary enhancements and additions;

2)	For key issue 3, the solution8 for UE identification will be used as the baseline solution for technical specification with necessary enhancements (e.g. if enabling multiple Application Clients on a UE to communicate with the same Application Server, an identifier for Application Clients is necessary for routing).

3)	The message reply from a Legacy 3GPP UE or Non-3GPP UE to a MSGin5G UE in Solution 15 will be used as the baseline solution for technical specification with necessary enhancements.

4)	The solution (in Solution 18) for interconnection will be used as the baseline solution for technical specification with necessary enhancements;

5)	The solution 19 and solution 23 for MSGin5G Server to interact with Application Server will be used as the baseline solution for technical specification with necessary enhancements.

6)	As solution 13, if MSGin5G Server/Client receives a message payload from Application Server/Client and the message payload size exceeds the maximum allowed packet size (e.g. due to limitation by the UE's access network transport), the MSGin5G Server/Client will need to perform the message segmentation and re-assembly.

7)	The solution of message reply from a Legacy 3GPP UE or Non-3GPP UE to Application Server in Solution 22 will be used as the baseline solution for technical specification with necessary enhancements.

8)	As shown in solution 9, 10, 15, 20 and 22, the Legacy 3GPP Message Gateway will be used for interworking with legacy 3GPP messaging services, the Non-3GPP Message Gateway will be used for interworking with non-3GPP message services.

9)  The solution 24 is needed to be used as a messaging mechanism especially for the scenarios which the MSGin5G Service ID of the receiver is difficult to be got by the sender.

10)	The solution 4 addressing the Group Management aspects will be used as the baseline solution for technical specification with necessary enhancements. Group management function based on SEAL Group Management Server specified in 3GPP TS 23.434 [9] can be implemented in the MSGin5G Server or outside of MSGin5G Server as a SEAL server.

11)	The solution 5 addressing the Group Messaging aspects will be used as the baseline solution for technical specification with necessary enhancements.

12)	The solution 17 addressing the Aggregated messaging for small data messages will be used as the baseline solution for technical specification with necessary enhancements.

13)	The solution 26 addressing the sending delivery report from message receiver UE back to message sender UE with store and forward with aggregation of delivery report, will be used as the baseline solution for technical specification with necessary enhancements.

14)  For key issue 1, solution 14 for Acknowledgement of Delivery Status, implemented to complement the message delivery solutions 9, 10, 15, 20 and 22, will be used as the baseline solution for the technical specification with necessary enhancements.

15) For key issue 4, solution 3 for MSGin5G Triggering will be used as the baseline solution for technical specification with necessary enhancements.

X)	Solution 27 is proposed as the baseline for registration with pre-provisioned ID with necessary enhancements;

Y)	Solution 2 proposes a registration procedure for MSGin5G UEs that don’t have pre-provisioned MSGin5G service ID; Support for this use case will be be further developed in normative phase based on this solution, with necessary enhancements.

* * * Next Change * * * *

<Proposed change in revision marks>

* * * Next Change * * * *

<Proposed change in revision marks>